## Slide 1: Modular Cavity Status
168 k$ of the 229 k$ estimated cost has been spent
Only major parts still in fab are the waveguide channels and main body
Expect to be on budget and meet the Sept 30 completion date.
Daniel Bowring coordinating FNAL/SLAC interface
Chris Adolphsen, SLAC, 7/12/13

## Slide 6: All Angle Cavity
Chris Adolphsen, Chris Nantista and Faya Wang
SLAC
Build an 805 MHz coaxial cavity such that E_rf is at all angles relative to the applied external magnetic field, H_ext
Map azimuthal breakdown dependence to assess E_rf x H_ext effects

## Slide 7
Inspired by Our X-band (11.4 GHz) Dual Mode Cavity
Designed to study effect of pulse heating on breakdown rate – excite two modes, TE011 (H only) and TEM3 (E and H) through two ports to vary the pulse surface heating for a fixed surface electric field (~ 200 MV/m)
TEM3 Electric Field

## Slide 10
Q0
(theor. 17,585)
In this case, choose inner radius, r1 = 2.34 in and outer radius, r2 =5.6 in so have same stored energy as Modular Cavity and same 805 MHz frequency
QL
All Angle Cavity Design Example
Chris Nantista

## Slide 11
Matched at ~-18.3 dB level
Match to Existing Waveguide (Beta ~ 1)

## Slide 12
r1 | U/Upillbox | Pd/Pd, pillbox | Q0 | E(r2)/E(r1)
1.000” | 0.360 | 0.527 | 17,735 | 0.179
1.674” | 0.708 | 1 | 18,355 | 0.299
2.342” | 1 | 1.475 | 17,585 | 0.418
r2 = 5.600” (fixed for size constraints)
l = 7.331” (½-wavelength)
Coaxial Cavity Design Options
@ common |Es|m
initial choice:
fix dissipated power:
fix stored energy:

## Slide 13: Use Acoustic Sensors to Map Azimuthal Breakdown Distribution

## Slide 14
Raw signals triggered by RE protection circuit
(35 Mev/m; 300 ms)
shows estimate of start time
Volts
msec
TTF RF Gun Breakdown Localization
M Ross et al

## Slide 15: RF Breakdown in Gas Filled Cavities
Chris Adolphsen and Faya Wang
SLAC

## Slide 16
E/p ~ 20 V/cmTorr, E = Ep/sqrt(2)
Ionization rate
At pulsed breakdown threshold, diffusion loss rate << ionization rate
Muon HPRF Cavity N2 Breakdown Threshold
[1] A. D. MacDonald, “Microwave Breakdown in Gases”, John Wiley & Sons, Inc., 1966.
Faya Wang

## Slide 17
E/p ~ 20 V/cmTorr, E = Ep/sqrt(2)
At pulsed breakdown threshold, diffusion loss rate << ionization rate
Muon HPRF Cavity H2 Breakdown Threshold
[1] A. D. MacDonald, “Microwave Breakdown in Gases”, John Wiley & Sons, Inc., 1966.
Faya Wang

## Slide 18: Forty Meter ‘Big Pipe’ Test Setup
CTO coupling RF power from P1 Marx-driven Toshiba MBK into TE01 mode in resonant line using KEK circulator.
40 m of pressurized (30 psig) , 0.48m diameter circular waveguide.
Shorted bend with input
mode converter at end of run.
Operated 100+ hours breakdown free at field levels that would be seen in the ILC KCS with the beam current upgrade
Recording run data.

## Slide 19: Surface Electric Field in 90 Degree Bend
|Es|pk = 3.34 MV/m for 37.5 MW input
(= 75 MW full geometry  300 MW TW equiv. at SW anti-nodes)
Equivalent to 72 MW TW in WR650 !

## Slide 20: Breakdown Rate at Various N2 Pressures
18 psig
22 psig
26 psig
30 psig
Dotted lines: Predicted electron growth rate in the gas normalized to the 18 psig data
Faya Wang