## Slide 1: Interferometric Residual Phase Noise Measurement System
Pakpoom Buabthong
Lee Teng Internship Program
Advanced Photon Source
Accelerator System Division, RF Group
Tim Berenc
Argonne National Laboratory

## Slide 2: Noise Characterization of Radio Frequency (RF) Devices Phase & Amplitude noise of a RF Carrier
When
amplitude noise
phase noise
in-phase noise
quadrature noise
Signal Level
Frequency
Carrier
Residual or noise added to carrier by a device
- Useful for characterizing noise added by a device or differential noise between devices (i.e. Short Pulse X-ray RF Cavities)
Device Under Test
ϕ
Frequency Spectrum
Polar
Cartesian

## Slide 3: Noise Measurement Using Saturated Mixer
90⁰ Phase Shift
( 0.3 V/rad)
Source phase noise ideally cancels
Usually limited by LNA-mixer noise floor and cable vibration
Source
V1
V2
Low Noise Amplifier (LNA)
Low Pass Filter (LPF)
Fast Fourier Transform
R(t)
femto-sec rms
Frequency (Hz)
dBrad2/Hz
Frequency (Hz)
Cumulative Integral
Phase Noise Power Spectral Density

## Slide 4: Interferometric Noise Measurement
Signal Level
Frequency
Carrier
DUT Noise
Increased sensitivity 18 V/rad , Source noise cancels
Usually limited by noise of RF Amp and cable vibration
90⁰ Phase Shift
180⁰ Combiner
RF Amp
Suppress Carrier
and Amplify Residual Noise
Signal Level
Frequency
Source
LO
femto-sec rms
Frequency (Hz)
dBrad2/Hz
Frequency (Hz)
Cumulative Integral
Phase Noise Power Spectral Density