## Slide 1
ELECTRO-MECHANICAL SIMULATIONS of β=0.92 Dressed Cavity
(UPDATE)
I. GONIN
July 23, 2013

## Slide 2
50mm
59mm
β=0.9&0.92 5 CELLS STRUCTURES AND HV’S MODIFIED MODEL
1030mm
1045mm
59mm
FIXED
SPRING CONSTANT
1042.9/1043.8
Li-i
Rreg
Rend

## Slide 3
df/dP vs. Tuner Stiffnes
Chart: df/dP, Hz/mbar vs. Tuner Stiffness
| 0 | 5 | 10 | 20 | 40 | 60 | 80 | 100
0.9 Rend=Rreg=110 | -13.7642 | 0.214 | 4.553 | 8.115 | 10.535 | 11.476 | 11.976 | 12.307
0.92 Rend=Rreg=110 | -8.7 | 3.1 | 6.9 | 9.9 | 11.9 | 12.6 | 13 | 13.3
0.92 Rend=110 Rreg=120 | -12.9 | -4.9 | -0.8 | 3.3 | 6.7 | 8.1 | 8.9 | 9.4
Chart: Rreg, mm
| 110 | 115 | 120
 | 5.4 | 6.3 | 8
Stiffness of β=0.92 caviy kN/mmvs. Radius of the Regular stiffening ring
- Stiffness of β=0.9 cavity

## Slide 4
dF/dP vs. Bellows Radius, Rend=110mm, Rreg=110mm
Chart: df/dP, Hz/mbar vs. Tuner Stiffness
| 0 | 10 | 50 | 100
Bellow 115mm | -9 | 6.9 | 12.2 | 13.3
Bellow 135mm | 41 | 22.9 | 16.8 | 15.7
Bellow 165mm | 180 | 50.9 | 24.5 | 22
R=115mm
R=135mm
R=165mm

## Slide 5
Rend=110mm
Rbellow =115mm
df/dP vs. Tuner Stiffnes, new HV design
Rend=110mm
Rbellow =120mm
Modern cryogenic systems achieve rms pressure stability
~0.2 mbar
Chart: df/dP, Hz/mbar vs. Tuner Stiffness
| 0 | 5 | 10 | 20 | 40 | 60 | 80 | 100
0.9 As design | -13.7642 | 0.214 | 4.553 | 8.115 | 10.535 | 11.476 | 11.976 | 12.307
0.92 Current | -12.5 | -1 | 3.4 | 7.2 | 9.8 | 11 | 11.5 | 11.9
Rreg=110mm
Rreg=115mm
CAVITY STIFFNESS
~ 7.8kN/mm

## Slide 6
The Scope of EM-Mechanical Design Issues
Minimize a sensitivity to microphonics due to He pressure fluctuations (df/dP) and mechanical vibrations
Minimize a Lorentz Force Detuning (LFD) coefficient
Tunability: tuning for correct frequency & for field flatness
Compromise between microphonics detuning (df/dP, LFD, microphonic noise) and cavity tunability (stiffness)
Enough strength to withstand atmospheric pressure
Stress analysis of cool-down from RT to cryogenic temperature
ES&H manual requires that the cavity is rated at MAWP of 4 bars at 2 K and 2 bars in RT
Incorporate the slow and fast tuners design.