## Slide 1: FNAL Site Report
Phil DeMar
Winter 2014 ESCC meeting
SLAC
February 25, 2014

## Slide 2: Perimeter Upgrades in Progress
Current implementation:
  Primary & backup border routers for general IP traffic
  Separate router for high impact science data traffic
    Isolated via policy-based routing
    100GE WAN link here…
Limitations & Issues:
  Primary & backup routers nearing end-of-life
  100GE-capable platforms are “expensive”
  Inefficient use of 100GE WAN link(s)
6509s
CRS
(loan)
100GE

## Slide 3: Migrating to New Perimeter Architecture
Will consolidate into two 100GE-capable border routers:
  Anticipating 2x100GE WAN config.
Science data traffic will still be separated:
  Expect to deploy VRF technologies
  Initially continuing with PBR
    But possibly OpenFlow in the future?
Router procurement under way:
  Expect to have new routers in place this summer
  100GE interface(s) may have to wait until next year

## Slide 4: FNAL WLAN Upgrades (I)
Our long term WLAN strategy = eliminate copper in offices
Current WLAN deployment:
  450 APs supporting ~2200 users (peak…)
  (Virtually…) All user/office areas have WLAN coverage
  Last year, completed higher-density pilot to upgrade central computing bldg
Expanding last year’s WLAN pilot to cover rest of site
  802.11n-based, but with 802.11ac (v1) modules
  Expect to have 500 new APs deployed by end-of-year
  Legacy 802.11g-only APs (Cisco 1231s) excessed
  Older 802.11n APs (Cisco 1142s) recycled out to peripheral areas

## Slide 5: FNAL WLAN Upgrades (II)
WLAN controllers:
  Three main controllers distributed in two data centers
  Each controller capable of supporting 500APs
  Migration to new APs means using demo controller for legacy APs
    Controller software doesn’t support 3602i’s & 1231s concurrently
Some coverage issues encountered in migration
  One-to-one replacement of older units causing some coverage loss
  3602i’s apparently need higher density configuration

## Slide 6: FNAL Internal (Client) IPv6 Support
General approach:
  Computing Div. (staff) LAN as eat-your-own-dog-food environment:
    Working on hardening IPv6 there to production quality
    Stateful autoconfig (A/M/O flags = 0/1/1)
  Volunteer WLAN for general users (& their devices):
    “Stateless” autoconfig (A/M/O flags = 1/0/1)
    Not in service yet (2-3 months off…)
DHCPv6 service working on InfoBlox appliance:
  Test InfoBlox right now; need to migrate to production servers
Issues we’re grapping with right now:
  Confusing scenarios with SLAAC:
    Captive DNS-based registration process
    Working with network blocking security tools
  Lack of clarity on device client DHCPv6 support

## Slide 7: Science Applications IPv6 Testing/Evaluation
Participating in IPv6 HEPiX working group effort:
  Under direction of Worldwide LHC Computing Grid (WLCG)
  Driven by CERN data center address
  needs due to virtualization
    ~250k public addresses
    by 2015
HEPiX IPv6 test bed:
  Currently 12 sites, distributed
  globally
Testing methodology:
  Persistent thruput testing
  Dual stack configurations
  LHC applications
    GridFTP; <others>

## Slide 8: GPON Evaluations
GPON = Gigabit-capable Passive Optical Network
Target space = “Village” residences
  Currently supported via Cisco LRE:
    Uses 40 yr old phone lines
    Max b/w = 5Mb/s
Deployment goal:
  GPON service into each residence unit
  GPON ports provide shared ~2Gb/s downstream & 1Gb/s upstream
  Between 8 & 16 units per port
    Worst case = ~150Mb/s upstream & 75Mb/s downstream per unit
Fermilab Village
~64 residence units
Internet via phone lines

## Slide 9: GPON Evaluations (cont)
Selected vendor - Zhone
  Base unit (MXK198) costs $8-10k
    Provides 16 GPON ports
  Premise units cost ~$250/each
GPON requires single mode fiber
  Investigating micro-trenching (~1ft deep) to get fiber into units
  Costliest part of the project – estimating $2-3/ft
Current status – Lab test bed
Next steps – limited user trial with existing fiber
Other potential users:
  Sensors
  Environmental monitoring
  Security guard shacks