## Slide 1
Fermilab Limited Scope Accelerator Readiness Review (ARR)
October 1 -3, 2013
Technical Breakout Session 2A
Radiological Safety for 700 kW Operations

## Slide 2: Increased Beam Power
Change in operating parameters (per approved shielding assessments):
Recycler Ring:
Operating Intensity: 1.5x1013 p/pulse  8.33x1013 p/pulse @ 8 GeV
Cycle Time: 1.33 seconds/pulse
2.25x1017 p/hr (80 kW)
Main Injector:
Operating Intensity: 5.00x1013 p/pulse  5.16x1013 p/pulse @ 120 GeV
Cycle Time: 1.87 seconds/pulse  1.33 seconds/pulse
9.63x1016 protons/hr  1.39x1017 protons/hr
513 kW  743 kW
NuMI: 513 kW  778 kW

## Slide 3: Shielding Evaluation
Shielding thickness determined:
via Monte Carlo modeling (e.g., MARS15)
Derived from Generic Shielding Criteria via known scaling laws:
Dt = -(TVL)log[(E’/E)0.8 (I’/I) (T/T’)]
Note: labyrinths and penetrations are scaled slightly differently since dose rates are dominated by changes in geometry, rather than passive shielding
“Incremental Shielding Assessment”

## Slide 4: Scaling sheet for MI

## Slide 5: Longitudinal Summary for MI

## Slide 6: Labyrinth/Penetration Summary for MI

## Slide 7: Example of Additional Shielding Needed for 700 kW Operations
20 RF bus penetrations at MI-60 gallery

## Slide 8: Operational/Environmental Impacts
Residual activity
  Scaled from previous measurements/surveys
Releases to air and water
  air release estimates based on annual proton beam loss rates since direct measurement below detection threshhold
  surface/ground water estimates assume losses at discrete (e.g., extraction, injection, and abort) locations
Prompt air-scattered radiation (‘skyshine’)
Not relevant at NuMI or RR/MI tunnels due to thick shielding

## Slide 9: Verification Studies
Shielding effectiveness studies will soon be performed
Plan currently being developed