## Slide 1: Comparison of Radionuclide Activity in the NuMI Decay Pipe to Results from the MARS Monte Carlo
S. Diane Reitzner
Satif-12
28-04-2014

## Slide 2: Outline
Introduction
NuMI beamline
Core sample results
MARS simulation
Nuclide distribution results
Activity results
Conclusions

## Slide 3: Introduction
Tritium is highly mobile.
  Transfers from one medium to another
Important to understand tritium production in beamline shielding.
  Develop method of tritium inventory
Difficult to assess tritium activity in solid samples
  Need to extract the tritium first before measuring its activity.
    Not guaranteed to extract the tritium.
  Tritium is difficult to contain.
Try MC methods to predict tritium production in shielding
  Compare MARS output to activity from other radionuclides in core samples taken from the NuMI decay pipe shield at Fermilab.

## Slide 4: NuMI Target Hall
120 GeV
proton beam
Decay
Pipe
Horn 2
Horn 1
Target/Baffle Carriage
Steel Shielding
Flowable Fill
ρ= 2.2 g/cm3
Graphite Target
Focus resultant
pions and kaons

## Slide 5
93 m
98 m
249 m
683 m
2 m diameter pipe
2.9 m outer
radius of shield
3.7 m outer
radius of shield
Dolomite
Decay Pipe Walkway
To Target
Hall
To Absorber Hall
Neutrinos to MINOS in Soudan MN
2.1 m outer
radius
NuMI Decay Pipe
675 m long
Pions and kaons
decay to neutrinos and muons

## Slide 6
Face of the NuMI decay pipe shield where the core samples were extracted.

## Slide 7: Activity in Decay Pipe Shield
Tritium Activity
Dehumidifiers installed in target hall between 2006 and 2010
Fixed Radionuclide Activity
Maximum depth from surface: 30”
2010

## Slide 8: Activity in Leachate
Comparison of 22Na Activity in solid sample to leachate
Leaching fraction for 22Na as a function of depth
2010
2010
ST9.99

## Slide 9: MC Analysis of Nuclide Production
Use MARS to predict nuclide distribution in the NuMI decay pipe shield.
  Compare to fixed nuclide distributions such as 7Be and 54Mn
Simple model of NuMI target hall and decay pipe in MARS
Detailed horns and target
Idealised horn magnetic field
Horn1
Horn2
Target

## Slide 10
NuMI Target
Hall in MARS
Horn 1
Horn 2
Baffle
Target
Decay Pipe
Entrance

## Slide 11: MC Analysis
Core samples extracted at large radius.
  1.5 m < R < 3.7 m
  Inner radius of decay pipe shield: 1.0 m
  Thick shielding problem.
  Decay pipe shield has large volume.
Use star densities with fine bins to extract spatial distributions.
Use coarse radial bins for nuclide production.
  Run MARS in MCNP mode
    En,th = 1 meV

## Slide 12: Star Density per Proton in the Decay Pipe Shield
Radius (m)
stars/cm3/s per proton

## Slide 13: Longitudinal Distribution Comparison
R = 2.1m

## Slide 14: Radial Distribution Comparison
Z=93 m

## Slide 15: Radial Distribution Fits
MARS Fit:
  Identify first term with rapid drop-off at small radius
  Identify second term with attenuation at large radius
  b1 = 0.077±0.002, b2 = 0.024±0.001
Data Fit:
  Core samples not deep enough to fit the first term
  b2 = 0.0229±0.0011

## Slide 16: Nuclide Production Calculation
Extract nuclide production per proton for R>1.7m
Use DETRA to calculate activity Atot.
  Intensity based on NuMI POT data
  Integrate over 375 days (300 day beam on, 75 day s beam off) to compare to 2006 results
Intensity profile input to DETRA

## Slide 17: Nuclide Activity Comparison
Nuclide | MARS Activity (pCi/g) | DATA Activity (pCi/g) | MARS Ratio 7Be/X | Data Ratio 7Be/X
7Be | 454±91 | 346±52 | 1 | 1
22Na | 111±22 | 78.7±11.9 | 4.1±0.7 | 4.4±0.9
54Mn | 25.1±5.0 | 19.7±3.0 | 18.1±3.4 | 17.6±3.7
3H | 229±46 | 57.9±0.9 | 2.0±0.4 | 6.0±0.9
The activity at R=2.1 m and Z=93m (from Horn 1) in the NuMI decay pipe for 300 days of beam on followed by 75 days beam off.
Activities for 7Be, 22Na, and 54Mn agree with the activity seen in the core samples.
Ratio of 7Be/22Na, 7Be/54Mn agree very well with data.
MARS reports greater activity for tritium
  Tritium underreported in data as a single leach cycle does not collect all of the tritium

## Slide 18: Tritium Leaching Predictions from MARS
Unknown value for leaching fraction L3H
  Lower bound of 0.10 from 22Na data.
  Upper bound of 0.88 from the assumption that all of the tritium is collected in two leachings.
Use ratio of 7Be/3H in MARS to predict L3H

## Slide 19: Predicted Leaching Fraction
Location from Horn 1 | Year | Radius | 7Be/3H from Data | Estimate L3H
93 m | 2006 | 2.1 m | 6.0 | 0.33±0.09
683 m | 2006 | 1.5 m | 8.0 | 0.25±0.07
93 m | 2010 | 2.1 m | 2.9 | 0.41±0.11
98 m | 2010 | 3.0 m | 1.8 | 0.66±0.17
249 m | 2010 | 3.0 m | 2.9 | 0.41±0.11
693 m | 2010 | 1.5 m | 3.0 | 0.40±0.10
Ratio of 7Be/3H from MARS:
2006: 2.0
2010: 1.2

## Slide 20: Conclusions
Activity in samples taken from the NuMI decay pipe shielding in 2006 and 2010 demonstrate the mobility of 3H.
Fixed nuclides like 7Be and 22Na can be used to benchmark Monte Carlo codes used for radionuclide production in shielding.
  MARS prediction of nuclide distributions match data.
  Predicted activity of fixed nuclides agree with data.
Comparison of tritium activity predicted by MARS to the activity seen in the samples implies that only 41% of the tritium collected in the deep samples.