## Slide 1
The Normal Conducting RF Program
Derun Li
Center for Beam Physics
Accelerator and Fusion Research Division
Lawrence Berkeley National Laboratory
MAP Collaboration Meeting
Fermilab, June 19-22, 2013

## Slide 2: Outline
Introduction and Goals
  Brief review of NCRF program
RF R&D Plan
  Experimental Studies at 805-MHz
    RF gradients (pillbox cavity with and without RF buttons) in multi-Tesla magnetic fields
    Modular cavity (Drs. D. Bowring and Z. Li)
    All season cavity
    High pressure RF cavity + Beam test at the MTA
    Dielectric loaded HP cavity
    RF breakdown studies (Prof. Y. Torun)
  MuCool 201-MHz cavity tests
    MuCool prototype cavity: baseline design for MICE
    Prototype for MICE
    MP studies (Drs. T. Luo and Z. Li)
  RF cavities for MICE
Summary
Dr. Y. Yonehara

## Slide 3: Introduction I: NCRF Requirements
Muon capture, bunching, phase rotation, ionization cooling require
  Low frequency normal conducting RF cavities
  High RF gradient operation in a few-T to 10 T magnetic fields
* RF gradients for Guggenheim cooling channels: ~ 25 MV/m at 3-T initially & tapering to ~ 10 MV/m at 18-T

## Slide 4: Introduction II: NCRF Cavity Programs
We have learned a great deal about the NCRF for muon acceleration: design/construction/experiments
  Cavity design, engineering and construction, and experimental programs at the MTA (Prof. Y. Torun’s talk)
    805-MHz open-cell cavity
    805-MHz pillbox cavity
    Be windows for 805-MHz and 201-MHz cavities
    Pillbox cavity with RF buttons
    805-MHz HP RF cavity (Muons Inc.)
    Two 805-MHz box cavities (ExB studies)
    All season cavity
    Dielectric loaded cavity (low power prototype)
    201-MHz cavity with Be windows for MuCool (baseline for MICE)
    201-MHz prototype cavity for MICE using the single cavity vessel

## Slide 5
Review: NCRF Vacuum Cavity for Muon Beams
RF cavity options, why and how we got here:
  Muon beams are born with large emittance and decay and must be confined by strong magnetic field
  Must use NCRF
    Pillbox-like cavity with beam irises terminated by thin Be windows (muons can penetrate)
      High RF electric field between two “parallel” planes
      TiN coating at high electric field region
      A factor of 2 higher cavity shunt impedance
      Less RF power for a given gradient
      Independent cavity phase control
    RF heating on thin Be windows could detune the cavity
      Two double-curvature windows pointing in the same direction

## Slide 6
805 MHz Cavities

## Slide 7: Overview: Pillbox Results - High Gradient in Strong B Field
What we have learned from the high power tests so far
  Achievable accelerating gradients degrade due to external magnetic fields (by approximately a factor of 2 at 3-Tesla magnetic field)
  Combination of strong magnetic field + RF fields cause damage on cavity surface
Coupling iris
805 MHz Cavity
Be window
Single button test results
Scatter in data is due to surface damage on
the iris and the coupling slot

## Slide 8: Overview: HPRF Cavity
Maximum electric field gradient in HPRF test cell
Schematic view of HPRF test cell
High Pressure RF (HPRF) cavity has been successfully operated in strong magnetic fields
Use Hydrogen gas as ionization cooling material
Metallic breakdown
Gas breakdown
Operation range for muon cooling
Gas breakdown:
Linear dependence
Governed by electron mean free path
Metallic breakdown:
Plateau
Depend on electrode material
No detail study have been made yet

## Slide 9: Overview: Beam Test of HPRF Cavity
Beam-induced plasma
Muon beam
Beam-induced plasma
formed in GH2
Plasma is drifted by
RF E field
Absorb RF power
Beam on
Observed beam-induced plasma loading effect
with 400 MeV proton beam
RF envelope w/o beam
RF envelope w beam
Add small amount of
electronegative gas
(SF6, O2, etc)
Ionized electrons
disappear
Still positive ions (mainly
ionized hydrogen)
consume RF power
Pure GH2
1% Dry Air (0.2 % O2) in GH2
1% Dry Air
(0.2 % O2)
in GH2
at B = 3 T
Inject either proton
or muon
electron
Positive ion
E0 = 25 MV/m
E0 = 25 MV/m
~ 50X reduction in
RF power dissipation

## Slide 10: Summary of HPRF Cavity
What we learned from the HPRF Test Cavity Experiment:
No gradient (50 MV/m) dependent on B field for HPRF for H2 gas pressure above 400 psi
Beam tests showed: introduction of less than 1 % air (negative gas absorbs electron) reduces the HPRF cavity loading greatly
Demonstrate that HPRF cavities can be used in the HCC
Design and build a practical HPRF test cavity (not buttons) with improved diagnostics
  Muon beam dynamics associated with plasma, collective and space charge effects

## Slide 11: Dielectric Loaded Gas-Filled RF Cavity
Helical Cooling Channel requires small size (radius) RF cavities
A compact RF system loaded by a dielectric material
Design, construction and measurements:
Measured frequency = 814.544 MHz @ 1 atm, QL = 4,250
• N2 gas pressure = 1,000 psi; observed unusual BD event at Esurface < 10 MV/m
• Observed usual BD event at Esurface > 10 MV/m; Long run at Esurface = 12 MV/m,
No more BD during 2 hrs long run; but multiple BD at 14.5 MV/m
Dielectric materials:
Determine breakdown limit, strength, and loss tangent that are suitable for cooling channels.
Design and build a full scale practical dielectric loaded cavity

## Slide 12: Overview: All Season Cavity
The All-Season Cavity (Muons Inc + Fermilab):
  Modular pillbox with replaceable end walls
  Designed for both vacuum and high-pressure
  Made of 316 SS with 25m Cu-plating
  3.9cm-thick center ring, 6.6cm-thick outer
  End-plates; 2.7mm-thick inner plates
  RF volume 29.1cm x 12.9 cm (Long)
  1-5/8" Cu coax coupler
  f0 = 810.375 MHz with vacuum (at upper edge
  of RF source power band); Q0  2.8x 104
Successful operation of the All-Seasons Cavity in 3 T magnetic field under vacuum
  Reached  20 MV/m
Detailed data analysis in progress
Operation of RF cavity in strong B field is a challenge
Goal: Find a workable solution through targeted R&D

## Slide 13: Modular RF Cavity
Modular cavity design and fabrication (Dr. D. Bowring’s Talk)
  Require a new RF cavity to replace the damaged 805-MHz LBNL pillbox cavity for normal conducting RF experimental programs at MTA
  Complete new cavity complex with waveguide coupler that fits inside the Lab-G magnet at MTA, Fermilab
    Cavity fabrication using the state-of-art of normal conducting techniques developed at SLAC
    Systematical RF breakdown studies in an external magnetic field
    The cavity design allows for testing of different materials (beryllium, copper), surface finish and processing (EP, brite-dip, etc..) end-plates
    Different cavity lengths (testing effects from time transit factor)
Lab-G magnet
Cavity support rail
Modular cavity complex

## Slide 14: The Modular Cavity Design
  Cavity design optimization
    Minimize peak surface field at the RF power coupling region
    Minimize multipacting at B=0 and B=3 Tesla
  Current status
    Fabrication in progress
    Many parts made
  Schedule
    A complete modular cavity assembly will be delivered to Fermilab by FY13.
  RF experimental programs developed
MP with & without external B field

## Slide 15: Cavity Fabrication Progress
Photos of parts being fabricated;
Cavity braze at SLAC;
Assembly and low power measurement at SLAC;
To be delivered to the MTA, Fermilab for high power test by end of FY2013

## Slide 16
201 MHz Cavities

## Slide 17
Cavity has been tested successfully without magnetic fields
Be windows can withstand high RF power in strong magnetic field without damage
201 MHz Cavity for Muons
Stiffener ring
Low peak surface
E-field at iris
121.7-cm
42-cm

## Slide 18
Cavity Design Parameters
The cavity design parameters
  Frequency: 201.25 MHz
  β = 0.87
  Shunt impedance (VT2/P):  22 MΩ/m
  Quality factor (Q0):  53,500
  Be window diameter and thickness: 42-cm and 0.38-mm
Nominal parameters for MICE and (cooling channels) in a neutrino factory or muon collider
  8 MV/m ( 16 MV/m) peak accelerating field
  Peak input RF power: 1 MW ( 4.6 MW) per cavity
  Average power dissipation per cavity: 1 kW ( 8.4 kW)
  Average power dissipation per Be window: 12 watts ( 100 watts)

## Slide 19: Development of 201 MHz Cavity
42-cm
Cavity fabrication technique development, in collaboration with JLab; The cavity has been high power tested at MTA, Fermilab

## Slide 20: Tests of 201-MHz RF Cavity I
SRF cavity post-processing techniques help NCRF
Fast conditioning, 21 MV/m with no B field, no surface damage found
Tests with fringe fields of Lab G magnet, 12 MV/m
  Damage in coupler and coaxial transmission line, Cu sputtering in ceramic windows, more realistic and systematic studies require Coupling Coil magnet

## Slide 21: 201 MHz MICE Prototype Cavity Test at MTA
Preparation for testing of the first MICE 201 MHz cavity using the single cavity vacuum vessel at the MTA, Fermilab
  The cavity
    Electro-polishing of the first cavity completed at LBNL (May 2012)
    Cavity is at Fermilab now & being prepared for installation at MTA
    An RF Workshop held May 28-29, 2013
  Status of other accessory components
      Beryllium windows received
      Tuners: fabrication of tuner arms (FNAL) and actuators (LBNL) complete
      Couplers: fabrication started at Fermilab
      RF windows (received)
1st 201 MHz MICE Cavity
Curved Be window

## Slide 22: 201 MHz MICE Prototype Cavity Test at MTA
  Using the single cavity vacuum vessel at Fermilab
    Same dimensions and features that a MICE RFCC vacuum vessel would have
    Installation fixtures and cavity handling experience
    RF commissioning and testing with external magnetic field
      Require a coupling coil magnet for testing at MTA
Single cavity vessel
Configuration of cavity and the vessel
Loop coupler
Loop coupler
Vacuum pump
Tuner actuator
Tuner arms
6 Tuners

## Slide 23: 201 MHz MICE Prototype Cavity Test at MTA
23
Close collaboration between Fermilab and LBNL
  Hardware design and fabrication (cavity, vessel, accessory components and etc. ) complete, and most parts are at Fermilab
  Development of installation concept
  Fixture fabrication
  Experimental testing program at MTA, Fermilab
  Development of test plan

## Slide 24: Tuner Test
Tuner assembly has been tested (in air) at Fermilab
Consistent performance of each tuner arm
Measurement agree well with FEA simulations
Push and pull have slight slope difference for pressure versus deflection
Measurements of pressure versus cavity frequency shift will be conducted this summer
Lucas Somaschini

## Slide 25: MICE RF Coupler
Updated coupler design
Fabrication drawings complete
Quotes from vendors reviewed
Fabrication start soon at LBNL
  Materials ordered
  Ti-N coating of the loop region and outer tube of the coaxial transmission line
  Need to modify existing vacuum chamber at LBNL
Schedule
  Estimated to be  12 weeks at LBNL machine shop

## Slide 26: MP Simulation Studies
High power RF tests of MuCool prototype cavity at MTA showed damage in RF couplers and sputtering of Cu on ceramic RF windows
  Suggest MP may have happened in the couplers
MP simulation studies (Dr. T. Luo’s talk)
  Collaboration with SLAC using ACE3P, including some code development
  Simulation studies using MICE B-field map & cavity and coupler geometry

## Slide 27: US MICE Responsibility
Hardware responsibility in MICE cooling channel
  Two RFCC modules: eight RF cavities
  Two spectrometer solenoid magnets
Demonstration of muon ionization cooling
International MICE experiment at RAL

## Slide 28: MICE Cavity Status
  All ten cavities with brazed water cooling pipes (two spares), nine cavities at LBNL to be EPed and 1st EPed cavity at FNAL
  Five cavities measured (low power measurements)
  Received 11 beryllium windows
  Received 10 ceramic RF windows
  Tuner design complete, one set of tuner assembly fabricated and tested offline
  PO of 24 tuner arms placed
  Updated design of RF power coupler complete, fabrication of two coupler started
  Assembly and installation of the 1st EPed MICE prototype cavity in progress at FNAL (Prof. Y. Torun’s presentation)
Sectional view of RFCC module

## Slide 29: NCRF R&D Goals
  Trying to understand the RF breakdown problems in magnetic fields
  Develop a workable solution for high gradient NCRF operating in B fields approximately 3 Tesla (initially) and higher (future).
  Support sub-assembly prototyping for the 6D cooling bench test.
    Guggenheim
    FOFO Snake
    HCC

## Slide 30: Multi-Institute Collaboration
RF R&D program has been operating successfully in a collaborative effort:
    Fermi National Accelerator Laboratory
    Lawrence Berkeley National Laboratory
    Brookhaven National Laboratory
    Jefferson Laboratory
    Illinois Institute of Technology
    Argonne National Laboratory
    University of Mississippi
    SLAC National Accelerator Laboratory
    Muons Inc.
    Tech-X Corp.
RF test facility, MTA at Fermilab

## Slide 31
Summary
Muon front-end system requires normal conducting RF cavity operating at high gradient in a few Tesla magnetic field
  Remains a challenge
  R&D plans developed to find a workable solution
Plans for RF breakdown studies
  Vacuum cavities
  High pressure RF cavity tests + beam at the MTA
  Dielectric loaded cavity
First MICE 201-MHz prototype cavity using the single cavity vessel this fall
  We believe our targeted R&D programs will help understand the RF BD and lead to a workable RF cavity solution in a strong magnetic field!