## Slide 1: Muon Campus Installation Travelers Cons Gattuso 8/28/13

## Slide 2: Why do we need such thing???
RR LAM 232
What went wrong?
Water connection did not
made hidden behind magnet
Klixons cables were connected and tested
  Cable damage and replaced but never retested
    Connected to wrong power supply
Several walk through missed it
  Configuration Change RR never had power Lambertson, thus no need for H2O

## Slide 3: Installation Travelers
What is an Installation Traveler ?
Where will these Travelers be kept ?
Who is responsible for filling out Installation Travelers ?
What will these Installation Travelers look like?
Road map for the installation for that location
A the tunnel location where the work is located.
Gives the Techs and inspectors a road map as to what needs to be done at this location.
Paper copies will be collected and stored, Electronic copies will just exist on line
Keep it simple, concise and to the point
Not looking for formal procedures
Techs doing the work

## Slide 4: 1st Traveler used on the RR LAM 232

## Slide 5: The process
Machine/Enclosure
Beam line/Quad location/Period
Generate the Traveler
Fine Tune add-remove items if needed

## Slide 6: Creating a Data Base and Algorithm to Generate Traveler
Data Base (Needs to be cross checked by Machines)
  Magnet
  Instrumentation
  Vacuum
  *Alignment
Algorithm
  Set by the support Dept (ownership, responsibility)
    Risks based driven
      Flag
        Water/power/interlocks/ceramics/ect
Use after installation usage
  Magnet replacement