## Slide 1: Summary of HPRF cooling channel workshop
K. Yonehara
APC, Fermilab

## Slide 2: Goal of workshop
  Make a list of criteria for baseline selection
  Identify “strong points” and “challenges” in HCC
  Distribute challenge issues in the group
Organize group
Schedule

## Slide 3: Our “Strong points”
HCC theory is very robust and accurate
  Possible to estimate cooling performance from a lattice
  Guide for optimization
    Improved matching at RF frequency transition
    Designed bunch merging by using features of helical magnet
High Pressurized Hydrogen gas filled RF cavity
  Feasible for a muon cooling channel
  Gas-plasma dynamics is a key to have better cooling performance, i.e. a lower emittance than possible in a vacuum channel
Developed a helical solenoid magnet technology
  NbTi, YBCO
  Consider BiSCCO in future

## Slide 4: What is present “challenges”?
Moving conceptual design to engineering design
  How to incorporate an RF system into an HCC magnet?
    A practical HCC design for λ ≥ 0.5 m looks available
    Find coil geometry, current (margin), and tolerance particularly for a final cooling section (λ < 0.5 m)
    Find RF geometry, power, operating temperature (room vs. LN2 temp), thermal isolation, and tolerance
    Additional space (> 15 %) for maintenance, plumbing, instrumentation, infrastructure
Challenge of extrapolating to final system
  What happens in the channel with a muon collider beam?
    Beam loading, Plasma loading, Plasma interacting with beam
    But, gas plasma could have a positive effect

## Slide 5: Additional challenges
Matching
  Phase slip should shift from negative to positive
  Consider pre-cooler
    Snake FOFO and COBRA
Safety aspect
  What is a safety requirement for usage of pressurized hydrogen?
  Engineering drawing is required for the safety committee
Beam instrumentation
  How to measure muon beam profile?
Consider cold RF operation
  A commercial LN2 chiller has enough cooling power to cool the present DL RF cavity

## Slide 6: Charge in the rest of time
Accomplish end-to-end cooling simulation
  Fix matching section
  Compute emittance evolution and transmission efficiency in analytical/practical EM fields
  Test field tolerance
  Finalize bunch merging
Design HCC magnet
  Nb3Sn vs. HTS for λ < 0.5 m
Design HCC RF system
  Investigate gas-plasma dynamics
  Design cold RF system

## Slide 7: Additional criteria for baseline selection
RF must work in a multi-Tesla field
RF must accept a muon collider beam
What is the limit of cooling?
  Space charge?
  Beam loading?
  Magnetic field?
  RF gradient?
  Non-linear dynamics?