## Slide 1: The Radiochemical Detector Robert Zwaska Fermilab May 22, 2014 High Power Targetry Workshop

## Slide 2: Thanks for Discussion and Input
Moses Chung
Nathan Eddy
Ben Freemire
Nikolai Mokhov
Igor Rakhno
Gianni Tassotto
Randy Thurman-Keup
Alvin Tollestrup
Katsuya Yonehara
Jim Zagel

## Slide 3: Introduction
Instrumentation for the beam resulting from the target
  Secondary Beam Instrumentation
  Target Hall Instrumentation
  Target & Horns Instrumentation
  Beam Monitoring
Neutrino beams, particularly, need a beam of consistent composition
  Within a few % over the exposure period
Challenges for the instrumentation:
  Measurement quality (precision, stability, etc.)
  Survivability

## Slide 4: Example: NuMI Target Alignment
Proton beam scanned horizontally across target and protection baffle
Hadron Monitor used to find the edges
Measured a small (~1.2 mm) offset of target relative to primary beam instrumentation.
Systematic effect of this misalignment would exceed statistical uncertainties
Pulse Height in Chamber (arb.)
target
baffle
baffle
target
baffle
baffle
Graphite protection baffle
Graphite target
Water cooling line
21.4 mm
15.0 mm
11.0 mm
6.4 mm
Horizontal Fin
Target
Horn
Baffle
p
p
Notes: Harp on implementation

## Slide 5: Why was the Target Misaligned?
Aimed at the target by using correctors and 2 BPMs, 10 & 20 m upstream
  BPM precision better than 0.1 mm
  Everything aligned optically to few tenths of a mm
Loading of the target hall
  Shielding piled on top after the optical survey – this can be corrected
Thermal deviation
  Stations are fixed at different locations, move relative to eachother as temperatures change
Can we design these out? Were we just unlucky?

## Slide 6: These Issues are Everywhere
Gate at the top of my stairs, installed in summer

## Slide 7: Tight Closure

## Slide 8: Misaligned by ~ 2 mm
Change of seasons in a temperature-controlled building caused a misalignment of 2 mm
This difference accumulated over only 1 m of span
  Here, it is a safety issue!
We are fortunate we only had ~ 1 mm to deal with in NuMI

## Slide 9: Approach to Tolerances
Minimize
Model
Measure

## Slide 10: Measure: NuMI Hadron Monitor
This is what we want to replace:
Array of helium ionization chambers
  Sits in the beam at the end of the decay pipe
  Measures remaining proton beam and larger secondary beam
Needed for operation and alignment
Degrades with exposure
  Radiation damage of components or cables
Sensitive to gas composition
Lid
Ceramic
Plates
PEEK
Cap
Stainless
Nut
Aluminum
Gasket
Stainless
Bulkhead
Ceramic
Feedthrough
Ceramic
Washer

## Slide 11: LBNE Hadron Monitor Placement
Air
He
HM
N. Mokhov

## Slide 12: Hadron Monitor Model in MARS
N. Mokhov

## Slide 13: Absorbed Dose
N. Mokhov

## Slide 14: Residual Dose on Contact
N. Mokhov

## Slide 15: Summary of Environmental Issues
Dose to components: 500 MGray / yr.
  0.02 DPA/yr
Residual activation after a few days:
  0.5 Sv/hr for steel
  10-100x less for Al and Ceramic (advantage grows with time)
Particle Flux:
  1012 charged particles / cm2 in center of monitor
    Drops off fast
  1011 neutron / cm2 background
Heating
  Max density: 0.2 W / cm3 in steel

## Slide 16: Detector Options
LBNE detector will be subject to ~ 20x greater flux than NuMI
  Shorter decay pipe
  Higher beam power
Extension of the ionization chamber technology is difficult and risky
  Chambers themselves, but also electrical cables and feedthroughs
Some conventional options:
  SEMs
  OTR
  …

## Slide 17: New Concept: Flowing Gas Detector
Actively flow reactants through the region.
  Beam ionizes the gas and produces reaction products
  Products are measured outside of the radiation field
  Time series measurement can give spatial information

## Slide 18: Choice of Reactants
E.g. aN2 + bO2 -> NOX
  Ionize few parts in 105 each spill
Commercial, flowing detectors available
  1 ppb NO sensitivity
  Up to 10 Hz rate
  “Cavity-Enhanced Laser Absorption Spectrometry”
Numerous other options (chemistry)
  Electrical conductivity of water is a great proxy, but water is not so desirable
  Would need to calibrate the approach and understand linearity
Seriously considering a prototype of this for LBNE

## Slide 19: Bonus Concept: Microwaves
Passage of microwaves through a plasma induces a phase shift proportional to plasma density:
Fusion community uses laser interferometry to interrogate plasmas
  Optical paths into the shielding not so desirable
Microwaves can be transported with waveguides

## Slide 20: Existing Experiment: ECloud Measurement with Microwaves
ECloud induced phase shift
  Carrier is injected with BPMs at just above the cutoff for the elliptical beam pipe
  Beam modulates the ECloud
  ECloud cause PM of carrier
  PM accumulates over the distance
Sideband, zero-span, and direct phase measurements
  Sidebands come from modulation, give intensity (convolved with harmonic information)
  Zero-span gives a cycle-wide measurement of intensity
  Direct phase gives excellent time resolution
    Issue is getting enough transmission
FERMILAB-CONF-09-168-AD
inspirehep.net/record/820122

## Slide 21: Microwave Detector
Effect would integrate along path length
Time resolution would be very good
Requires tricky/expensive electronics
Need to understand normalization of the plasma to ionization and linearity

## Slide 22: Conclusion
Need for secondary instrumentation in neutrino beams
  Needed for operation and alignment
  Subject to enormous particle fluxes and radiation damage
Existing technology from NuMI is questionable for LBNE
  Gaseous ionization chambers
    Uncertain gas linearity issues
    Problem of electrical connections and cables
Considering novel approaches that do not involve wires or electrodes
  Radiochemical detector uses the beam to react gasses, the products are detected outside
    Time-series can give spatial information
  Microwave detector uses the plasma from ionization to induce a phase shift in a passing microwave
    Proven concept, enormous signal
    An affordable, stable system may be out of reach

## Slide 23: The Radiochemical Detector Robert Zwaska Fermilab May 22, 2014 High Power Targetry Workshop