## Slide 1
Target System Concept for a Muon Collider/Neutrino Factory
(5th High Power Target Workshop, Fermilab, May 20, 2014)
K.T. McDonald,5 X. Ding2, V.B. Graves,3 H.G Kirk,1 H. K. Sayed,1 N. Souchlas,4 D. Stratakis,1 R.J. Weggel4
1Brookhaven National Laboratory, Upton, NY 11953, 2UCLA, Los Angeles, CA 90095
3ORNL, Oak Ridge, TN 38731, 4Particle Beam Lasers, Inc., Northridge, CA 91324
5Princeton University, Princeton, NJ 08544
Specifications from the Muon Accelerator Staging Scenario
6.75 GeV (kinetic energy) proton beam with 3 ns (rms) pulse.
1 MW initial beam power, upgradable to 2 MW (perhaps even to 4 MW).
60 Hz initial rep rate for Neutrino Factory;
15 Hz rep rate for later Muon Collider.
The goal is to deliver a maximum number of soft muons,
~40 < KE < ~ 180 MeV.
Target System Concept
Graphite target (ρ ~ 1.8 g/cm3), radiation cooled (with option for convection cooling); liquid metal jet as option for 2-4 MW beam power.
Target inside high-field solenoid magnet (20 T) that collects both µ±.
Target and proton beam tilted with respect to magnetic axis.
Superconducting magnet coils shielded by He-gas-cooled W beads.
Proton beam dump via a graphite rod just downstream of the target.
Some of the proton and /µ transport near the target is in air.
Stainless-steel target vessel (double-walled with intramural He-gas flow for cooling) with graphite target and beam dump, and downstream Be window.
This vessel would be replaced every few weeks at 1 MW beam power.
15 T superconducting coil outsert,
Stored energy ~ 3 GJ, ~ 100 tons
5 T copper-coil insert. Water-cooled, MgO insulated
He-gas cooled W-bead shielding (~ 100 tons)
Last Final-Focus quad
Upstream proton beam window
Target System Optimizations
High-Z favored.
Optima for graphite target: length = 80 cm (for ρ = 1.8 g/cm3),
radius ~ 8 mm (with 2mm (rms) beam radius),
tilt angle = 65 mrad.
nominal geometric rms emittance ε = 5 µm.
β* = σr2 /ε = 0.8 m.
Graphite proton beam dump, 120 cm long, 24 mm radius to intercept most of the (diverging) unscattered proton beam.
The 20 T field on target should drop to the ~ 2 T field in the rest of the Front End over ~ 5 m.
Issues for Further Study
Thermal “shock” of the short proton pulse on the graphite target.
Probably OK for 2 MW and 60 Hz operation; 15-Hz option needs study.
Cooling of target, and the W beads.
Lifetime of target against radiation damage.
Beam windows.
* and beam emittance at the target.
To preserve liquid-metal-jet upgrade option, need related infrastructure installed at t = 0.
Proton beam tube