## Slide 1: Overview of HOM-based Diagnostics at FLASH and the European XFEL
N. Baboi, DESY
HOMSC 14, WG 2 HOM-based Diagnostics Fermilab, 14 July 2014

## Slide 2: Contents
Principle, benefits
HOMBPMs for 1.3 GHz cavities
  FLASH
  E-XFEL
HOMBPMs for 3.9 GHz cavities
  FLASH
  E-XFEL
HOM-based beam phase
Measurement of cavity alignment at FLASH
Summary

## Slide 3: Principle
Phase difference
Filter higher dipole mode for beam position
Filter higher monopole mode for beam phase
×
Beam offset [mm]
e-

## Slide 4: Benefits
Additional beam diagnostics without additional vacuum component
  Beam alignment
  Additional information on cavity alignment
Reduction in emittance dilution from transverse wakefields by centering beam in accelerating cavities
Direct, on-line measurement of beam phase wrt RF phase

## Slide 5: Accelerating Cavities in the E-XFEL and FLASH
The 1st dipole band
The 1st dipole band
The 2nd dipole band
Coupled cavities

## Slide 6: FLASH
 | European XFEL | FLASH
1.3 GHz cavities | 100 x 8 cavities | 7 x 8 cavities
3.9 GHz cavities | 1 x 8 cavities | 1 x 4 cavities
Charge | 0.02-1 nC | 0.2 – 1 nC
Energy | Up to 17.5 GeV | Up to ~1.2 GeV
Bunch frequency | Up to 4.5 GHz | Up to 1 MHz
Macro-pulse frequency | 10 Hz | 10 Hz
Macro-pulse length | ≤ 650 ms | ≤ 800 ms
Tests for E-XFEL made at FLASH

## Slide 7: HOMBPMs at FLASH: 1.3 GHz Cavities
Electronics built by SLAC
HOMBPM-electronics installed in 40 cavities in FLASH
  Use 1 dipole mode at 1.7 GHz
  Used as operator tool for beam alignment
  Used for measurement of cavity alignment
  Demonstrated use as BPM 10 mm rms resolution
Presently
  Study stability of calibration into BPM-signals
The 1st dipole band
Bandpass Filter 1.7 GHz 20 MHz BW
Mixer
Digitizer
LO 1.68 GHz
Clock 108 MHz
Joe Frisch et al., SLAC

## Slide 8: HOMBPMs at FLASH: 1.3 GHz Cavities (cont. 1)
Preliminary stability study
  Mostly parasitical measurements
  It seems that there is a strong correlation between calibration stability and the data position
Relevant for the E-XFEL as well
Liangliang Shi, DESY, UNIMAN

## Slide 9: HOMBPMs at the E-XFEL: 1.3 GHz Cavities
Electronics Design
  Direct sampling of all three frequencies without any DCW
  MTCA standard
  Multiple filtering
Samer Bou-Habib, WUT, DESY

## Slide 10: HOMBPMs at FLASH: 3.9 GHz Cavities
Theoretical studies made within EuCARD
  4 coupled cavities
frequency / Hz
Simulation
T. Flisgen et al., Phys. Rev. ST Accel. Beams, 17:022003, February 2014
Measurement
Thomas Flisgen, UROS

## Slide 11: HOMBPMs at FLASH: 3.9 GHz Cavities (cont. 1)
Experimental studies made within EuCARD
  Specs for FLASH and E-XFEL
Presently: stability study (Liangliang Shi)
Integrated power
Coupled modes 5.437 MHz RMS Error at Module Center
Pei Zhang, ex-DESY (now CERN)

## Slide 12: HOMBPMs at FLASH: 3.9 GHz Cavities (cont. 2)
Electronics built at FNAL
  Now under commissioning
  Will serve as prototype for the E-XFEL
Bandpass Filter ~5.43 GHz or 9.06 GHz 100 MHz BW
Mixer
uTCA Digitizer
SIS8300
(108MS/sec)
LO
30 MHz IF
Nathan Eddy, FNAL

## Slide 13: HOMBPMs at the E-XFEL: 3.9 GHz Cavities
Electronics under design, based on same specifications as for FLASH
  Designed at DESY
  Design of 5GHz DCW and PLL ready
Bandpass Filter ~5.43 GHz or 9.06 GHz 100 MHz BW
Mixer
uTCA Digitizer
SIS8300
(108MS/sec)
LO
30 MHz IF
Thomas Wamsat, DESY

## Slide 14: HOMBPMs at the E-XFEL: 3.9 GHz Cavities (cont. 1)
But much more challenging:
  8 coupled cavities cf. 4
  4.5 cf 1 MHz bunch frequency
  Different orientation of cavities
Presently: Need significant theoretical and experimental studies
  Prototype cavity arrived at DESY
  SSC (State Space Concatenations) approach developed at Uni Rostock and ready for simulation of 8-cavity simulations
  Direct simulations of full module started at Uni Manchester

## Slide 15: HOMBPMs at the E-XFEL: 3.9 GHz Cavities (cont. 2)
Impedance Parameter Comparison with SSC
Thomas Flisgen, UROS

## Slide 16: HOM-based Beam Phase Measurement wrt RF
Proof-of-principle made at FLASH
Presently:
  Phase monitors for 1.3 GHz cavities
  No nice monopole mode found for 3.9 GHz cavities
Phase difference
~2.4 GHz
1.3 GHz
(leaking through HOM-coupler)
~0.1 deg noise (at 1.3 GHz)
Joe Frisch, SLAC

## Slide 17: HOM-based Beam Phase Measurement wrt RF (cont)
Same electronics as for HOMBPMs / 1.3GHz / E-XFEL
  Prototype under construction
  First beam tests expected in the next few months
Samer Bou-Habib, WUT, DESY

## Slide 18: Measurement of Cavity Alignment at FLASH
Ayaka Kuramoto, KEK

## Slide 19: Summary
Aim: HOM-based beam diagnostics for the E-XFEL
Based on large previous experience at FLASH
  1.3 GHz cavities: same specs as FLASH New concept for electronics, no DCW, multiple filter New: beam phase
  3.9 GHz cavities: same specs as in FLASH, but much more challenging:
    8 coupling cavities instead of 4
    different orientation of cavities
    4.5 MHz beam instead of 1 MHz
    Simulations being made
Tests on cavity alignments at FLASH
    Ayaka Kuramoto’s talk