## Slide 1: VISTA near IR survey data and DES
Richard McMahon,
Manda Banerj (UCL), Mike Irwin
Eduardo Gonzalez, Jim Lewis

## Slide 2: VISTA Summary
Location: ESO, Paranal, Chile
Aperture: 4.1 m diameter f/1 primary
Field of view: 1.65 degree diameter
Instrumentation: VIRCAM ― 8k x 8k sparse filled mosaic near-infrared camera
Detectors: 16 x 2k x 2k pixel (Raytheon VIRGO HgCdTe); 67 megapixels
Wavelength range: 0.84–2.5 microns
Pixel scale: 0.34 arcseconds/pixel
Filled field of view: 0.60 deg2
Surveys started: April 2010
Visible and Infrared Survey Telescope for Astronomy (VISTA)

## Slide 3
4.1 m diameter f/1 primary

## Slide 4: VISTA site choice: Cerro Paranal (ESO) or Cerro Pachon (Gemini)

## Slide 5
http://casu.ast.cam.ac.uk/
VLT Survey Telescope
UKIRT
Gaia/Euclid
Group is led by Mike Irwin
http://casu.ast.cam.ac.uk/surveys-projects/software-release

## Slide 6: VISTA Surveys Processing Status

## Slide 7: VHS and other DES-centric VISTA Surveys
Survey | Area (deg2) | Depths | Nominal Depth (mag)
VHS (PI: Richard McMahon) | 18, 000 | 5σ, AB | J=21.2 Ks=20.0
1. VHS-DES | 4500 | 5σ, AB | J=21.6 (H=21.0)* Ks=20.4
2. VHS ATLAS | 5000 | 5σ, AB | Y=21.2 J=21.2 (H=20.6) Ks=20.0
3. VHS-GPS | 8000 | 5σ, AB | J=21.2 Ks=20.0
VIKING (PI: Alistair Edge | 1,500 (450 250 deg2 in DES) | 5α, AB | Z=23.1 Y=22.3 J=22.1 H=21.5 Ks=21.2
VIDEO (PI: Matt Jarvis) | 15 (DES SN fields) | 5σ, AB | Z=25.7 Y=24.6 J=24.5 H=24.0 Ks=23.5
Note: since April 2012, VHS H-band has been dropped to increase J-band exposure time and meet nominal J-band depth requirement.

## Slide 8
around 10,000 deg2 observed

## Slide 9: VHS Components
VHS-Dark Energy Survey (VHS-DES)
  4500deg2 ( excludes 500deg2 from VIKING footprint)
  J (120sec), H(120sec), K(120sec)
    Changed April 2012 to J(240sec), H(0sec), K(120sec)
VHS-ATLAS (VST-ATLAS PI: Shanks):
  Non-DES High Galactic latitude including NGP
  5000deg2
  Y(60sec), J(60sec), H(60sec), K(60sec)
    Changed April 2012 to Y(120sec), J(60sec), H(0sec), K(60sec)
VHS Galactic Plane (VHS-GP)
  5< |b| <30
  8200deg2
  J(60sec); K(60sec)

## Slide 10: VHS observations status on 2013, Sep 1st
Observing Block(OB);
Tile = 1.5deg2
VIKING
VHS-DES currently completed ~2900 sq deg: ~250 sq deg overlapping DES SVA1
VIKING
VIKING

## Slide 12: CASU processing for VISTA
CASU responsible for all NIR processing for VISTA and WFCAM as part of the VISTA Data Flow System(VDFS)
VISTA pipelines run: Paranal; Garching; Cambridge
Mike Irwin
Jim Lewis
Eduardo Gonzalez-Solares
Simon Hodgkin
Aybuke Kupcu Yoldas
Eduardo Gonzalez-Solares

## Slide 13: CASU mantra
MEFs as container -> simplifies bookkeeping
use lossless Rice-compression -> (x 2-4 less space)
FITS images and catalogue binary tables (CFITSIO)
FITS headers record processing details
  derived data quality control (QC) parameters
  WCS astrometric calibration
  photometric calibration
  versioning and software details
modular software -> C & perl/python scripts
minimise external software dependencies

## Slide 14: IR Data Reduction Issues
IR detectors are inherently more unstable than optical CCDS
  some odd electronic effects
  not as good cosmetically as CCDs
Sky background >100x brighter than most objects of interest
Sky background is variable temporally and spatially
Exposure times are short, so nightly data rates for VISTA are (~250-500GB)

## Slide 15: Time Variable Sky

## Slide 16: Image processing Steps
Raw data transfer, ingest and organisation
Monthly calibration updates (flats, linearity, masks)
Nightly processing:
  reset correction (debias)
  dark correction
  linearity correction
  flat field correction
  sky background correction *****
  destripe - controller level pickup
Crosstalk, persistence, no fringing corrections needed for VISTA

## Slide 17: Software Solutions
nebuliser
  removes complex background variations
  enhanced object detection & parameterisation
despiker
  removes diffaction spikes, charge bleeding artefacts, and satuarated stellar cores
mosaicer
  CASU tiling software developed for VISTA
psf’ers
  automatically generates detector-level PSFs
  and performs PSF photometry

## Slide 18: VISTA IR focal plane
16 arrays, 64 Mpix = 0.60 deg2 on-pixels , 0.34 arcsec/pix.
  - 6 offset pawprints gives 1.5 x 1.0 deg2 “tile”, every pixel covered by at least 2 pawprints.
Completed Tile
Relative Exposure Time
dark green = 1, light green = 2, magenta = 3
red = 4, yellow = 6

## Slide 19
x6
......
+ confidence map
+ catalogue
+ confidence map
+ catalogue
96 chips
VISTA
pawprints
dither
stacked
mosaic
tile

## Slide 20: Challenges when dealing with tiles
imperfect sky subtraction pawprint matching + artefacts
variable PSF across pawprint detectors
variable seeing conditions for entire pawprint
variable saturation levels of each detector
variable extinction (ZP) during tile observations
astrometric distortion = photometric distortion
interpolation = varying correlated noise patterns

## Slide 21
Tile photometric distortion
Tile exposure map
Inherent illumination correction

## Slide 22
Detector PSF variations

## Slide 23: MJD variation across tiles

## Slide 24: Tile vs Stack photometry (before grouting)
∆j = 0.05

## Slide 25: Tile vs Stack Photometry (after grouting)
∆j = 0.015

## Slide 26: Tile grouting
Before
After

## Slide 27: Nebulised pawprints and tiles
Nebulosity filter applied to stacks before mosaicing

## Slide 28
Nebuliser -> M17 K-band

## Slide 30
Nebuliser -> M31 field 23 MegaCam

## Slide 31: Post-Processing Steps
monthly zeropoint updates
  stack 2MASS photometric residuals
  compute detector-level ZP offsets
  and residual spatial illumination correction
tile grouting
  fix catalogues for variable PSFs
  and for varying pawprint-level ZPs
  and for individual detector-level ZPs
reclassify and update tile catalogue calibration

## Slide 32: Data Products - recap
products consist of:
  calibrated single exposure images
  shifted ”average” stack frames (pawprints) + conf maps
  calibrated stacked pawprint catalogues
  filled area tile images + confidence maps
  calibrated tile object catalogues
  sky background images, flats, darks, bad pixel mask
science products are MEF files (images Rice-compressed)
all QC parameters are stored in MEF headers
headers contain provenance information
processing web page updates
  http://casu.ast.cam.ac.uk/surveys-projects/vista

## Slide 33
Preview of images, QC information, catalogue detections and calibration images.

## Slide 34: An example of long QC trend analysis
Variable zero-point (and hence survey depth) with time
  silvered mirror degradation
  aluminised mirror
  a bit of window cleaning

## Slide 35
Astrometric Calibration from 2MASS/UCAC3
Linear solution
per detector
Tabulated
systematics
from stacked
residuals
WCS - ZPN projection
rms < 100 mas
sys < 25 mas

## Slide 37: DECam@CASU PI data on Carina dwarf
From Mike Irwin this morning: “You might be interested in this. I only had 5 fields in and around the Carina dwarf to derive the ZPN coeffs but here's Decam’s radial residuals from 2MASS stars
distortion leftovers after our usual processing.

## Slide 39: List driven photometry using DES as master image
DES r
VHS K
Uncircled objects are sources with K band detections < 1.5sigma

## Slide 42: END

## Slide 43: CASU mantra
MEFs as container -> simplifies bookkeeping
use lossless Rice-compression -> (x 2-4 less space)
FITS images and catalogue binary tables (CFITSIO)
FITS headers record processing provenance details
  derived data quality control (QC) parameters
  WCS astrometric calibration
  photometric calibration
  images used at image processing step
  versioning and software details
modular software -> C & perl/python scripts
minimise external software dependencies