## Slide 1: Double Quarter Wave Crab Cavity Design and Plans
Qiong Wu
2/17/2014

## Slide 2: Outline
Proof of Principle (PoP) Double Quarter Wave Crab Cavity (DQWCC)
  Cavity Design
  Cold Tests
SPS DQWCC
  Cavity Design
  Couplers
  Helium Vessel, Tuner, Cryostat Design
Future Plans
Summary

## Slide 3: The Proof of Principle
 | Crabbing (fundamental) mode freq. | 1st HOM | Cavity length | Cavity width | Beam pipe diameter | Deflecting voltage
Unit | MHz | MHz | cm | cm | cm | MV
DQW crab cavity | 400 | 579 | 38.4 | 14.2 | 8.4 | 3.3

## Slide 4
Cavity Parameters
Electric field (top) and magnetic field (bottom) of the fundamental mode.
 | Unit | DQWCC
Fundamental Mode Frequency | MHz | 400
Nearest Mode Frequency | MHz | 579
Vertical Deflection Voltage | MV | 3.3
Rt/Q (Fund. Mode) | Ohm | 400
Epeak | MV/m | 44
Bpeak | mT | 60 on cavity 79 on port blending
Energy Content | J | 12
Peak field on port blending region. Improved in SPS prototype cavity design, see later slides.

## Slide 5: Cavity Stress Analysis
Pressure: 2e5 Pa (2 bar) outside, vacuum inside. Requirement for PoP Cavity.
Fixed Support: One side of beam port.
Stiffening plates and frames are added to the cavity for vertical cold tests.
The material for stiffening components can be either Nb or Ti.
Bare cavity without stiffening frame
Cavity stress with stiffening frame

## Slide 6: Multipacting study
© Z. Li @ CM20
Small multipacting (MP) region was found around the waist of the cavity at ~0.1 MV of deflection voltage. Verified and processed during vertical tests.

## Slide 7
PoP Cavity Fabrication & Preparation
Test II
Test I

## Slide 8
PoP cavity test results (1st)
1st cooled down test done in June 2013.
Multipacting (MP) was found for the region of 0.07-0.16 MV and was easily conditioned through. The MP did not come back after the conditioning.
Q0 measured at 3×108
Q0 did not improve by cooling down from 4.2 to 2 K.
Vt reached 1.34 MV, limited by the RF power amplifier.
Further chemistry cleaning and niobium plated flanges helped decrease the heating issue in the cavity.

## Slide 9
PoP cavity test results (2nd)
© B. Xiao@ CC13
Q0 reached 3e9 at low field. The requirement is above 1e10.
Q0 decreases starting from 2MV, associating with high radiation.
Q0 got recovered after ~30 minutes conditioning.
Radiation is lower than 15mR/h after the conditioning.
Reached 4.6MV kick in CW with Q0 above 2e9, limited by quench.
Temperature increase on both beam pipe flanges and pickup port blending area.
Rs at 4.3K: 57nΩ
1.9K: 18.6nΩ
Rres is 18.5nΩ
Chart: T [K]
| 4.3 | 4.14 | 4.1 | 4.07 | 4.01 | 3.94 | 3.9 | 3.85 | 3.75 | 3.66 | 3.6 | 3.51 | 3.44 | 3.38 | 3.29 | 3.2 | 3.14 | 3.08 | 3.01 | 2.93 | 2.85 | 2.78 | 2.7 | 2.64 | 2.59 | 2.53 | 2.45 | 2.38 | 2.319999999999998 | 2.27 | 2.22 | 2.17 | 2.11 | 2.05 | 1.99 | 1.93 | 1.86 | 1.84
Rs (T) | 56.9548 | 52.4625 | 51.3427 | 50.3602 | 48.9057 | 46.7577 | 45.7378 | 44.4315 | 41.8113 | 39.552 | 37.5727 | 36.159 | 34.3606 | 33.5941 | 31.9088 | 30.3144 | 29.3079 | 28.4066 | 27.2908 | 26.2857 | 25.3097 | 24.4482 | 23.5438 | 22.9212 | 22.4261 | 21.9948 | 21.4042 | 20.9141 | 20.4464 | 20.1333 | 19.8744 | 19.938 | 19.7792 | 19.6241 | 19.4183 | 19.2129 | 19.11 | 18.6005
Fitting | 57.4465 | 52.4139 | 51.2148 | 50.3311 | 48.6026 | 46.6517 | 45.5682 | 44.2462 | 41.7086 | 39.5459 | 38.1677 | 36.1954 | 34.7402 | 33.5479 | 31.8542 | 30.2742 | 29.284 | 28.3439 | 27.3105 | 26.2122 | 25.2015 | 24.3879 | 23.5377 | 22.9548 | 22.5041 | 22.0044 | 21.4058 | 20.9432 | 20.5901 | 20.3252 | 20.0858 | 19.8706 | 19.6428 | 19.4459 | 19.2777 | 19.1356 | 18.9997 | 18.9663

## Slide 10
PoP cavity test results (2nd)
Q0 at around 3~4.5e9.
In CW mode, temperature of beam pipe flanges increase.
Reached 4.5MV kick in pulsed mode with Q0 always above 3e9, limited by quench, consistent with conditioning test.
Temperature increase on pickup port blending area.
Quench field at ~110mT, with peak E field at 52.8MV/m

## Slide 11
Prototype For SPS
Cavity
wall
4 mm
He vessel
wall
Adjacent beam
pipe wall
3 mm
R 42mm
194 mm
140 mm
352 mm
286 mm
Wall thickness = 4mm
524 mm
684 mm
342 mm
288 mm
MODES |  |  | 
Fundamental frequency (crab mode frequency) | f0 | 400 | MHz
First HOM frequency | f1 | 580 | MHz
FIGURES OF MERIT |  |  | 
Transversal R/Q | Rt/Q | 430 | Ohm
Geometry factor | G | 89 | Ohm
FIELDS |  |  | 
Maximum peak surface electric field | Emax | 37 | MV/m
Maximum peak surface magnetic field | Hmax | 69 | mT
Accelerating voltage | Vacc | 15 | kV
OTHER |  |  | 
Field center offset | 𝒪field | 0.22 | mm
Stored energy | U | 10 | J
Electric field
Magnetic field
f(0)
© S. Verdu-Andres
@ CC13

## Slide 12: Improvement in SPS Design
Quench for SPS DQWCC extrapolated to
About 5.3 MV deflecting voltage using the measured quench voltage of the demo cavity (~ 14% higher voltage).
The FPC port diameter was determined by CERN according to the cooling needed for the coupler. Then all ports were selected to be at the same dimension to minimize the field asymmetry.

## Slide 13: Couplers
FPC hook: Qext f(0) = 6x105, 40 kW power supply is enough to feed the cavity
Pick-up antenna: Qext f(0) about 3x1010, enough to extract about 1W of fundamental mode.
HOM coupler and filter
The maximum magnetic field on the HOM coupler is 50 mT, and the coupling to the first HOM is 471.
Three (3) Higher Order Mode (HOM) couplers are proved by simulation to be sufficient for damping. The coupler hook and filter will be actively cooled by liquid helium, and the analysis is undergoing at CERN.
Fundamental mode coupler (FPC) is designed for providing coupling with Qext 1e5 to 1e6, and peak magnetic field at the same level of the cavity. The FPC waveguide, cooling, and power input will be provided by CERN.
Pick-up coupler should bring minimum disturbance to the cavity field symmetry and ~ 1 W of power for the low level control system.
FPC
HOM Coupler
HOM Coupler

## Slide 14: HOM table
The HOMs are coupled out with the design of the coupler hook shown in the.
The external Q of the first HOM is 471, which is much lower than the limit of 1000. The Qext shown here is before the filter.
The mode at 1.5 GHz with Qext above 1e5 has a very small R/Q of 6e-3 Ohm.
The impedance of each HOM is calculated accordingly. We will collaborate with beam dynamics study at CERN to validate the design.

## Slide 15: Dressed Cavity
Tuner + reinforcement
beam
Space for
adjacent beam pipe
HOM
FPC
HOM
Cryo jumper
Piezo + reinforcement
362.4 mm
400 mm
565 mm

## Slide 16: Cryostat (SPS)
Helium vessel
Cavity
FPC
Input power waveguides
Tuning system
Cryo jumper
Thermal shielding
(80K – nitrogen)
Magnetic
shielding
The cryomodule design concept was first initiated at STFC Daresbury Laboratory (UK), then adopted and substantiated by CERN engineers.

## Slide 17: Plans (2014)
PoP Cavity
  Profile measurement of PoP DQWCC (Done)
  Static magnetic field measurement of the test dewar (Done)
  Beadpull measurement for HOMs and off-center field
  Cold test again at CERN
  Test tuning system for SPS prototype cavity
SPS Prototype Cavity
  Rf/thermal/mechanical studies of cavity-vessel system
    Multipacting studies and verification of fields
    Table of frequency shifts
  Finalize thermal-mechanical design of helium vessel and tuning
  Send final version of design with helium vessel to Niowave in April for fabrication
  Multipole studies
HOM filter
  RF design completion of HOM filter (near complete)
  Make a 3D printing of the RF design and copper plate the surface (Done) for RF measurements
  Thermo-mechanical design of HOM filter

## Slide 18: Plans (2015-2017)
HOM coupler and filter
  Finalize thermal and mechanical design.
  Prototyping HOM coupler and filter for RF measurements at liquid He temperature.
  Fabricate six assemblies for SPS cavities.
SPS prototype cavity
  Cold test both prototype cavities
  Cold test dressed prototype cavities
  Deliver both dressed cavities to cryomodule assembly site
  Support SPS beam test
LHC cavity
  Adopt cavity for both deflection schemes (vertical & horizontal) at IP1 and IP5
  Adopt cavity ancillaries for both deflection schemes
  Collaborate with CERN to revisit both deflection cavity assembly specifications
  Collaborate with CERN on alignment and other issues for LHC installation

## Slide 19: Summary
The PoP cavity has confirmed our design concept by achieving 4.6 MV of deflecting voltage in vertical test.
The prototype cavity design for SPS test is coming to an end.
It will join the helium vessel design with CERN collaboration and delivered to Niowave for fabrication in April.
The HOM coupler and filter RF design is close to completion. Simulation will be verified with a Proof of Principle model. We will incorporate minor changes to lower surface field and suppress multipacting.
A prototype HOM filter will be made for testing.
Tuner and Cryomodule design is underway with close collaboration with CERN scientists and engineers.
We are using all the resource available to us at BNL to improve our design of the entire crab cavity assembly.

## Slide 20: Collaboration
Sergey Belomestnykh, Ilan Ben-Zvi, John Skaritka, Silvia Verdú-Andrés, Binping Xiao, Qiong Wu
Luis Alberty, Rossana Bonomi, Rama Calaga, Ofelia Capatina, Federico Carra, Giuseppe Foffano, Raphael Leuxe, Thierry Renaglia
Zenghai Li