## Slide 1: Fine-Grained Tracking Detectors for Neutrino Physics: Part I
Christopher Mauger
Los Alamos National Laboratory
24 October 2014

## Slide 2: Outline
What are we trying to measure?
  Characteristics of typical neutrino beams
  Event signatures
What are the characteristics of a fine-grained tracking detector?
  Monolithic vs. tracking detectors
  Characteristics of neutrino targets
Examples of fine-grained tracking detectors
Basic Principles of tracking elements
  Scintillator/Fiber Bars
  Straw Tubes
  Resistive Plate Chambers
Gross Design Features
  Tracking detector assembly
  Magnet Issues
  Nuclear targets
Advantages/Disadvantages
Conclusions

## Slide 3: Long-Baseline Neutrino Oscillation Experiments
The study of oscillation physics provides the opportunity to study interaction physics with the near detector

## Slide 4: The Long-Baseline Neutrino Experiment
LBNE consists of
  an intense neutrino beam at Fermilab
  near detector systems at Fermilab
  a 34 kt liquid argon time-projection chamber (TPC) at Sanford Laboratory at 4850 foot depth – 1300 km from Fermilab
When constructed, LBNE will have the longest manmade baseline of any neutrino experiment

## Slide 5: Appearance Oscillograms (Normal Hierarchy)
Left plots: Neutrino oscillations vs energy and baseline for neutrinos (top) and antineutrinos (bottom) for dCP = 0
Right: Neutrino oscillations as a function of neutrino energy for different values of dCP for neutrinos (top) and antineutrinos (bottom) – solar term shown in yellow
All plots assume Normal Hierarchy

## Slide 6: Appearance Oscillograms (Inverted Hierarchy)
Left plots: Neutrino oscillations vs energy and baseline for neutrinos (top) and antineutrinos (bottom) for dCP = 0
Right: Neutrino oscillations as a function of neutrino energy for different values of dCP for neutrinos (top) and antineutrinos (bottom) – solar term shown in yellow
All plots assume Inverted Hierarchy

## Slide 7: Long-Baseline Neutrino Oscillation Experiments
The study of oscillation physics requires the study of interaction physics with the near detector

## Slide 8: Layout on the Fermilab site
asD

## Slide 9: Cross-section of LBNE Near Site

## Slide 10: Layout of LBNE: Neutrino Beam
p+ m+ + nm
p- m- + nm

## Slide 11: Characteristics of the Neutrino Beam
Resultant Neutrino Beam (LBNE case)
Neutrinos from few hundred MeV to 10’s of GeV
Predominantly muon (anti)neutrinos, but enough electron (anti)neutrinos to carry out studies in high-flux environments – it’s a good thing, since LBL experiments are searching for electron neutrino appearance!

## Slide 12: Event signatures of these beams
Particle type: electron, gamma, muon, charged and neutral mesons, protons, neutrons (not usually done well
Particle sign
Momentum: Range of 10’s MeV/c to multi-GeV
Direction: Mostly forward-going, but some high-angle and backward-going
Signature label | Charged Current | Neutral Current
Quasi-elastic | Charged lepton + proton or neutron | Neutrino + proton or neutron
Resonance | Charged lepton + proton or neutron + a few other hadrons | Neutrino + several hadrons
DIS | Charged lepton + hadronic shower | Neutrino + hadronic shower

## Slide 13: Tracking Detectors vs Monolithic
Monolithic detectors have large uniform volume of neutrino target
Target material is active – creates light, ionization, phonons, etc.
Detectors positioned on the outer surface
Good isotropic capabilities
Super-Kamiokande: water Cherenkov
KamLAND: organic liquid scintillator

## Slide 14: Tracking Detectors vs Monolithic Detectors
Localization of particles by deploying many low-profile detector elements
Detector elements throughout the volume
Anisotropic distribution of elements
Elements can be the target or targets can be separate from the elements
3.5 m

## Slide 15: Fine-grained trackers and targets
Fine-grained trackers mean high pixelization of the detector – many detector elements
The neutrino target can be active or passive
Passive targets allow for the study of any nucleus
Active targets in principle give better signal efficiency
3.3 cm

## Slide 16: Examples of detectors - NOMAD
Drift planes
Transition radiation detectors
E&M calorimeter
Hadronic calorimeter
Muon detectors
Magnet
Magnet Return
Veto plane

## Slide 17: Examples of detectors - NOMAD

## Slide 18: Examples of detectors – T2K
See Professor Kendall Mahn’s talk for more details

## Slide 19: Examples of detectors – Minerva
120 modules for tracking and calorimetry
Magnetized MINOS near detector for downstream muon tracking/sign selection
From: Brian Tice

## Slide 20: Examples of detectors – Minerva active target modules
Inner detector: active scintillator strip tracker – triangular extrusions using charge sharing rotated by 60 degrees for stereo views
Lead pieces on outer 15cm of active target for side electromagnetic calorimeter
Outer frame provides side hadronic calorimeter/muon identifier
3.3 cm
From: Jorge Morfin

## Slide 21
Solid Nuclear Target Region
Carbon, Iron, Lead – mixed elements in layers to give similar systematics
XUXVXUXV (4 tracking points) between each layer
Main detector
Beam
From: Jorge Morfin

## Slide 22: Examples of detectors - Minerva
From Minerva website

## Slide 23: LBNE Near Neutrino Detector
3.5 m
High precision straw-tube tracker with embedded high-pressure argon gas targets
4p electromagnetic calorimeter and muon identification systems
Large-aperture dipole magnet
Philosophy
  make high-precision, high-statistics measurements of neutrino interactions with argon (far detector nucleus)
  measure inclusive and exclusive cross-sections to build and constrain models to predict the event signatures at the far site and correlate them with the true neutrino energy
  make detailed studies of electron (and muon) neutrinos and anti-neutrinos separately

## Slide 24
ECal designed to identify electrons and photons – critical for measuring neutral pion background
Sandwich of lead and plastic scintillator
Downstream ECal has 58 layers of 1.75mm lead with scintillator bars of 2.5cmx0.5cm profile (4m long)
The Barrel ECal (shown at left) and Upstream ECal have 3.5mm of lead
Total lead mass is 110 tons, scintillator mass is 35 tons
4p coverage gives
excellent neutral
pion identification
and containment
Electromagnetic Calorimeter

## Slide 25
External Muon
Identifier
Steel interleaved with Resistive Plate Chambers
Identifies muons – separates muons and charged hadron (e.g. pions)

## Slide 26: LBNE Near Neutrino Detector
Transition Radiation Detector
Radiator foils, argon gas targets, other
nuclear targets
Average density ~ 0.1 g/cm3
UA1-style dipole magnet – 0.4 T
Muon identifier – also interleaved in magnet

## Slide 27
XX YY Module
62mm thick leaving 18mm for a nuclear target module
TRD XX YY Module
76mm thick
Strawtube Tracker
Module

## Slide 28
Argon Gas Target Assembly – SS Version
216 tube assemblies welded to manifold
SS Tube Cap
Manifold
Weld
Manifold Cover
SS Tube Adapter
SS Tube .625” OD x .065” wall butt welded to adapter and cap

## Slide 29: Basic Elements – Scintillator Bars
Scintillation peaks at 420nm, cuts off at 400nm
Collect scintillation light with wavelength shifting fiber – emission peak at 476 nm (green) – total internal reflection to end of bar
Maximize collection efficiency with a reflector around the outside of the bar
TO2 reflecting material co-extruded with scintillator at FNAL
Wavelength shifter attenuation length > 3m, so long bars are possible
Versatile – used for tracking, ECal, Hcal
Useful in moderate density applications

## Slide 30: Basic Elements – Scintillator Bars
Lab 5 at FNAL, polystyrene scintillator extrusion
Co-extrusion with titanium dioxide successful, R&D on wavelength-shifting fiber co-extrusion

## Slide 31: Basic Elements – Straw Tubes
Straws fabricated with conducting material (or coated with conducting material)
Anode wire threaded through the straw (which can be a few meters in length)
High electric field – especially near the anode results in electron multiplication
Excellent response to charged particles
Excellent in low-density applications
Charged particle
Ground
HV
Gas Volume
Ionization track

## Slide 32
Straw Tube Insert
Straw Tube Pin
Wire Connections to IO Board
Anode wire: strong, good conductor, thin (gold-plated tungsten 30 microns)
Straw: kapton, coated with conducting material
Gas mixture: usually noble gas (argon) and damping gas (hydrocarbon)
Straw material can be the neutrino target
Straw Tubes

## Slide 33: Construction of RPC
33
Pickup strips
Two 2 mm thick float Glass
Separated by 2 mm spacer
2 mm thick spacer
Glass plates
Resistive coating on the outer surfaces of glass
Naba Mondal
Notes: 33

## Slide 34: Basic Elements – Resistive Plate Chambers
RPCs can be built with glass or plastic (bakelite)
Voltage drop across the plates (several kV)
Spacers used to keep the plates separated (few mm thick)
Charged particles induce a localized discharge
Good timing resolution (25 ns)
Enables inexpensive readout over a broad area

## Slide 35: Gross Design Features - Tracking
How do we fit these together?
Next slides by Jan Boissevain (LBNE engineer)

## Slide 36
Straw Locator
Place straws and fill with precision steel balls (.375”)

## Slide 37
Complete straw placement for first row, add straw locator – all straws filled with precision steel balls

## Slide 38
Apply glue between straws

## Slide 39
Apply glue in preparation for placement of 2nd row of straws

## Slide 40
Add second row of straws, fill straws with precision steel balls – the bottom row of straws remain filled with steel balls

## Slide 41
Add glue lines for top composite sheet

## Slide 42
Groove Feature for Indexing the Outer Frame during a glue operation
FGT Straw Tube Subassembly A with aluminum channels for shipping

## Slide 43
FGT Straw Tube Subassembly B
FGT Straw Tube Subassembly A
Prepare to mate the two halves

## Slide 46
Position Outer Frame

## Slide 47
Glue Outer Frame In Place

## Slide 48
Glue Outer Frame to mated subassemblies A & B
Remove shipping fixtures

## Slide 50
Turn assembly over and glue the second outer frame

## Slide 51
Remove shipping fixtures
Result: XX straw tube plane assembly with 672 straws
3500mm x 3500mm x 30mm outside dimensions

## Slide 52
Install Window Frames – window foil not shown

## Slide 53
Straw Tube Insert
Straw Tube Pin
32 Channel I/O Board
Wire Connections to IO Board
Window Frame

## Slide 54: Gross Design Features - Magnets
Magnetic field useful for charge separation and momentum measurements
Geometry of typical neutrino beams favors dipole configuration
Low-density trackers (e.g. straw tubes) can do electron-positron separation
Requires significant power – especially for cooling (few Mwatts)

## Slide 55: UA1 magnet at CERN:
2 yoke sections on carriage, the total number of yoke sections is 16
Yoke sections assembled, tested
Assembled magnet in hall
Yoke material: EN S235JRG2, a European low Carbon steel

## Slide 56: UA1 magnet at CERN:
Assembled yoke sections on carriage in UA1 experimental hall at CERN. Total magnet weight 850. tons.
Data taking started in November, 1981.
Operating properties: 10,000 amps, 576. V., resistance .0576Ω @ 40.o C. Cooling water flow 50. liters/sec.
Original yoke costs – 2,000,000.00 Euros in 1978.
Essential to have a continuous magnetic circuit in steel yoke -
Sondheim

## Slide 57: Gross Design Features – Nuclear Targets
Geometry of typical fine-grained trackers such that planes of un-instrumented nuclear targets can be interspersed with tracking material
This allows good possibilities for neutrino-nucleus interaction studies. Targets can even be swapped out.
Care must be taken due to absorbed particles and side-going particles that will be missed.
Petti

## Slide 58: Gross Design Features – Nuclear Targets
Some materials require specialized target containment – gases, liquids
In the case of liquid, liquid in, liquid out studies can be performed
In the case of gas, can vary the pressure continuously to enable efficiency studies
Manifold
Weld
Manifold Cover
SS Tube Adapter
SS Tube .625” OD x .065” wall butt welded to adapter and cap

## Slide 59: Advantages and Disadvantages to Fine-Grained Trackers
Advantages
  exquisite reconstruction possible
  similarities to collider physics detectors
    share reconstruction tools, development costs, materials and component costs
  non-uniform: design flexibility
Disadvantages
  non-uniform, need to study efficiencies carefully
  dead space
  Issues of non-uniformity/dead space different from collider detectors since vertices happen anywhere
  cost scales like volume – not a problem for current and future experiments

## Slide 60: Conclusions
Fine-grained trackers have a long history in neutrino physics.
FGTs benefit from similarities to detector systems in other communities (e.g. collider physics)
FGT designs can be tuned to the event rate, energy regime and background environment of a particular experiment
FGTs are optimal for high precision studies important for understanding neutrino interactions