## Slide 1: Neutrino Flux Simulation Methodology nuSTORM weekly meeting 03/14/14
Ao Liu*
collaborating with J.B. Lagrange, David Adey
Fermilab, Indiana University

## Slide 2
A list of the simulations

## Slide 3: Simulation list
 Neutrinos from the nominal muon beam.
 Neutrinos from another muon beam with 120% angular divergence.
 Neutrinos from the “particle zoo” , which includes π+, π-, K+, K-.
☐ Neutrinos from FFAG lattices.

## Slide 4: More details - reminder
1 and 2 have been done.
  Muons were generated from pion decay after a single pass through the “pion beamline”, and recorded at the end of the decay straight.
  These muons were tracked step-wise in one FODO cell, by 29 times. (7 m FODO cell)
  All these muon information was gathered as a muon pool.
  We take a random 1e6 muons from the pool each time and force them to decay at 130 different positions along the decay straight. Record the neutrinos at the ND.
  Multiply the angular divergence of the muons in the pool by 1.2; repeat the steps above.

## Slide 5: More details – particle zoo
The secondary particles were taken after horn designed to collect π+, including π+, π-, K+, K-.
These particles are tracked from the horn to the end of the decay straight, with only one pass. They decay naturally (not forced to decay) in the code.
All the neutrinos from the particle decays are recorded at the FD.

## Slide 6: neutrinos from FFAG lattices
Since the pion injection hasn’t been fully demonstrated for FFAG lattices, we need to estimate the muon beam from pion decay in the straight.
J.B’s code was used to track 1e5 pi+ in the 165 m long decay straight. They are recorded every 0.25 m, i.e. 660 positions.
The pi’s do not occupy the exactly same longitudinal coordinates (Z) due to the tracking code settings. So at each of the 660 positions, all pions within +- 0.05 m range will be gathered to the same Z.
The pions will be forced to decay at these positions and the resulting muons will be recorded, and tracked in J.B’s code to form a muon pool to sample from later.
After this is done, we will be able to simulate the ν flux.