## Slide 1: Status of Partial Return Yoke

## Slide 2: Overview
Introduction and Concept
Performance
Engineering
Timeline

## Slide 3: Partial Return Yoke
MICE hall: solenoids cause large stray field
Aim of PRY: Reduce stray field in hall to tolerable level
Shielding plates
  wall thickness 10 cm
  weight: 55t
Performance
  Reduces stray field outside of shield to 5-10 Gauss
(Note: not to scale)
H Witte. Step IV & VI: Local Flux Return. MICE CM 34, October 2012.

## Slide 4: Principle

## Slide 5: Partial Return Yoke
Courtesy of Jason Tarrant / Steve Plate
8m
3m
Support Structure
Shielding plates

## Slide 6
Performance

## Slide 7: 5 Gauss Surface
5 Gauss Surface
MICE Solenoids
PRY
No iron

## Slide 8: Iso-Surface 0.5 mT
Step IV
200 MeV Flip
No Shield
12 cm Shield
9 m
MICE Solenoids

## Slide 9: 240 MeV Solenoid/Flip Mode
Notes: Redo plot

## Slide 10: Field Tracker Cryostat
Tracker readout position:
  Diameter 1 m
  Just next to shield
Fields
  No iron: 36.4 mT
  Shield: 0.6 mT
  Difference: factor 60
  240 MeV Solenoid (12 cm shield)
  Falls off quickly
No Shield
Shield

## Slide 11: Effect on Beam
MAUS tracking study
  200 MeV Flip
  Error field map: all iron versus no iron at all (worst case)
    Original and current geometry
    Misalignments (1 mm + rotation)
  Discussed at MICE analysis meeting 24/1/2013
Conclusion
  …barely measurable effect on the beam travelling through MICE.
  There is no reason, from a beam dynamics perspective, not to implement a shielding wall as described herein.
C. Rogers and H. Witte. Effect Of Iron Partial Return Yoke on the MICE Beam. 23/01/2013, http://micewww.pp.rl.ac.uk/issues/1161

## Slide 12
Engineering

## Slide 13: Connections
Backing plates
Waveguide
penetration
L-Seal

## Slide 14: September 2013 Review
Space for
Virostek Disc
Support anchored in ‘trench’
No access to absorber
Courtesy of J. Tarrant / S. Plate

## Slide 15: Present Status
6 Piece Design with central access to AFC for absorber changes
Simplified end-plates
Reduced number of more compact legs now with symmetry S-N
Courtesy of J. Tarrant / S. Plate

## Slide 16: Absorber Change
Procedure in place (J. Tarrant)

## Slide 17: Forces
Floor Fixing
~25 tonnes (self weight)
Load trying to overturn PRY half
Compressive load
Tensile load
NO CAPACITY FOR SIGNIFICANT MAGNETIC LOAD IN FLOOR FIXING: Cross-bars, leg ties & link plates will take magnetic loads
30 kN

## Slide 18: Force Scenarios
Nominal cases
  200/240 MeV flip/solenoid mode
Commissioning
  Single spectrometer powered
  Both spectrometers powered
  AFC powered
Worst case analysis
  Increased forces by factor 5
  Still very safe
Monitoring: draw-wire sensor
WDS-3000-P115-CA-P

## Slide 19: Materials

## Slide 20: Material
Fiber Tracker
Readout location

## Slide 21: Timeline
Production Readiness Review (PRR) for PRY Monday 28th April
  Green light to proceed
Steel procurement: order placed May 5th
Framework and steel machining
  RFQ: online May 14th (due June 5th)
  Expect quotes from four vendors
  Targeted award date: June 9th/16th
South Wall complete October, 2014
North Wall complete December, 2014

## Slide 22: Summary
Performance
  Reduces stray field to 5—10 Gauss (No shield: 300—600 Gauss = factor 50+)
Effect on beam: no issue
Engineering
  Finished
Timeline
  Procurement ongoing

## Slide 23: Additional Slides

## Slide 24: 240 MeV Solenoid/Flip Mode