## Slide 1
Muon Collider Design
MAP 2014 Spring Meeting, Fermilab May 27-31, 2014
Y. Alexahin
(FNAL APC)

## Slide 2
Design Goals
2
Muon Collider Design – Y.Alexahin, MAP14, Fermilab 05/29/2014
 High Luminosity (Higgs Factory L ~ 1032cm-2s-1, 3TeV MC L > 41034cm-2s-1)
 round beams (to minimize beam-beam effect)
 small * (Higgs Factory * ~ 23 cm, 3TeV MC * ~ 35 mm)
 small circumference
 small bunch length s  * (high-energy MC)
 momentum compaction factor ~ 10-5
 Acceptable detector backgrounds
 tight apertures in W absorbers (resistive wall instability?)
 dipole component in FF quads
 halo extraction (bent crystals?)
 Manageable heat loads in magnets
 enough space for W absorbers, shorter distance between masks
 * variation in wide range (w/o breaking dispersion closure)
 Small collision energy spread E /E  410-5 (for Higgs Factory)
 instabilities? longitudinal beam-beam effect?
 Safe levels of -induced radiation (for E  3 TeV)
 no long straights (except for IRs)
 combined-function magnets to spread ’s

## Slide 3
Basic Concepts (from 2014 DOE review)
3
Muon Collider Design – Y.Alexahin, MAP14, Fermilab 05/29/2014
Section | Description | Report
Interaction Region (IR) | Quadruplet Final Focus (see support slide for explanation, implemented only in the Higgs Factory lattice thus far) | IPAC13 TUPFI061, NAPAC13 THPBA19
Chromatic correction | 3 sextupole scheme with 1st sextupole correcting vertical chromaticity while 2nd and 3rd sextupoles form -I separated pair for horizontal correction | PRSTAB 14, 061001 (2011)
IR-to-Arc Matching | *-tuning section with a chicane allowing for * variation in a wide range and having bending field everywhere to spread ’s | IPAC12 TUPPC041
Arc | Flexible Momentum Compaction arccell allowing for independent control of tunes, chromaticities, momentum compaction factor and its derivative with momentum | PRSTAB 14, 061001 (2011)
New concepts were developed in the course of muon collider design:
) for High-Energy MC

## Slide 4
x (inwards)
By
dipole component
x (inwards)
By
dipole component
defocusing quad + dipole
 Dipole component in a defocusing quad is more efficient for cleaning purposes – it is beneficial to have the 2nd from IP quad defocusing
 The last quad of the FF “telescope” also must be defocusing to limit the dispersion “invariant” generated by the subsequent dipole (not shown)
– both requirement are met with either doublet or quadrupole FF:
focusing quad + dipole
x
y
y
x
Why Quadruplet Final Focus?
4
Muon Collider Design – Y.Alexahin, MAP14, Fermilab 05/29/2014

## Slide 5
Higgs Factory Lattice
5
Muon Collider Design – Y.Alexahin, MAP14, Fermilab 05/29/2014
Specifics of the Higgs Factory lattice are discussed in a support slide
IR
CCS
sextupoles
The dynamic aperture at IP and projection of FF quad aperture (solid ellipse).
Higgs Factory Interaction Region (IR) and Chromaticity Correction Section (CCS), *=2.5cm
IR quad cold mass inner radii and 4 beam envelopes for *=2.5cm

## Slide 6
6
Muon Collider Design – Y.Alexahin, MAP14, Fermilab 05/29/2014
Higgs Factory Layout
Dispersion suppressor and * tuning section noticeably increase the ring circumference, but they are probably indispensable
dispersion suppressor
chromaticity correction sextupoles
* tuning section
95.5 m
Arcs are very short and do not allow for wide-range tune adjustment
Flexibility of the optics (*=1.5-10cm) allows for adjustments depending on the parameters of the muon beam

## Slide 7
7
Muon Collider Design – Y.Alexahin, MAP14, Fermilab 05/29/2014
Modified Higgs Factory Lattice
No reverse bends  circumference reduced to 283m (from 300m).
Difficulty in adjustment of the horizontal tune (now Qx=5.16, Qy=4.56).
Some unexpected problem with vertical dynamic aperture is encountered.
½ Arc
IR
CCS
Matching Section
Half ring layout
Optics functions in half ring for *=2.5cm
dispersion suppressor
* tuning section
chromaticity correction sextupoles

## Slide 8
8
Muon Collider Design – Y.Alexahin, MAP14, Fermilab 05/29/2014
Higgs Factory Parameters
Parameter | Startup | Design | Baseline
Beam energy, GeV | 63 | 63 | 63
Average luminosity, 1031/cm2/s | 1.7 | 2.5 | 8.0
Collision energy spread, MeV | 3 | 3 | 4
Circumference, m | 300 | 300 | 300
Number of IPs | 1 | 1 | 1
*, cm | 3.3 | 2.5 | 1.7
Number of muons / bunch, 1012 | 2 | 2 | 4
Number of bunches / beam | 1 | 1 | 1
Beam energy spread, % | 0.003 | 0.003 | 0.004
Normalized emittance, mmrad | 0.4 | 0.3 | 0.2
Longitudinal emittance, mm | 1.0 | 1.0 | 1.5
R.m.s. bunch length, cm | 5.6 | 5.6 | 6.3
R.m.s. beam size at IP, mm | 0.15 | 0.11 | 0.075
Beam-beam parameter | 0.005 | 0.007 | 0.02
Momentum compaction factor | 0.079 | 0.079 | 0.079
Repetition rate (Hz) | 30 | 30 | 15
Proton driver power (MW) | 4 | 4 | 4
> 13k h-bosons/year at this luminosity

## Slide 9
9
Muon Collider Design – Y.Alexahin, MAP14, Fermilab 05/29/2014
3 TeV MC Preliminary Design (Triplet FF)
Optics and chromatic functions in IR, horizontal Chromatic Correction Section (CCS), Matching Section and the first arc cell (out of 6 per arc)
Arccell
IR
CCS
Matching Section
This design was reported at MAP12 meeting at SLAC and IPAC12, but it was abandoned since the sequence of quad polarities in FF triplet is not favorable for detector protection.

## Slide 10
10
Muon Collider Design – Y.Alexahin, MAP14, Fermilab 05/29/2014
Matching Section with Chicane
 The required B-field in chicane is quite low – magnets can be shorter to free space for RF cavities or pulsed halo deflectors.
 Chicane length is 84.5m, depth at *=3cm is 19.6cm – small effect on the total circumference
This concept will be used in the new design but with combined-function magnets.

## Slide 11
11
Muon Collider Design – Y.Alexahin, MAP14, Fermilab 05/29/2014
3TeV MC Arc Cell with Combined-Function Magnets
name | L (m) | B (T) | G (T/m)
QD | 5 | 9 | -35
QF | 4 | 8 | 85
Momentum compaction factor for a stand-alone cell is p = ‑0.004,
betatron phase advance is 300 in both planes.
Each arc consists of six such cells and two dispersion suppressors

## Slide 12
12
Muon Collider Design – Y.Alexahin, MAP14, Fermilab 05/29/2014
3 TeV MC Design with Quadruplet FF
IR
CCS
-tuning section
y(max) is reduced to 80km compared to 118km in the previous design with triplet FF.
 | Q1 | Q2 | Q3 | Q4 | Q5 | Q6
aperture (mm) | 90 | 110 | 130 | 150 | 150 | 150
G (T/m) | 267 | 218 | -154 | -133 | 129 | -128
B (T) | 0 | 0 | 2 | 2 | 0 | 2
length (m) | 1.6 | 1.85 | 1.8 | 1.96 | 2.3 | 2.85
Now 12T pole tip field is assumed
Q3
Q4
Q5
Q2
Q1
s(m)
a(cm)
5x
5y
Q4
Q6
Q4
Q5
Q5

## Slide 13
13
Muon Collider Design – Y.Alexahin, MAP14, Fermilab 05/29/2014
3TeV MC Dynamic Aperture
1024 turns on-momentum dynamic aperture at * =5 mm for two versions of 3TeV MC lattice
The momentum acceptance for * = 5 mm is 0.45% and 0.4% for * = 3 mm
 Ay2(m)
5.5
 Ax2(m)
triplet FF
quadruplet FF

## Slide 14
14
Muon Collider Design – Y.Alexahin, MAP14, Fermilab 05/29/2014
High Energy MC Parameters
High Energy MC parameters |  |  | 
Collision energy, TeV | 1.5 | 3.0 | 6.0*
Repetition rate, Hz | 15 | 12 | 6
Average luminosity / IP, 1034/cm2/s | 1.25 | 4.4 | 12
Number of IPs | 2 | 2 | 2
Circumference, km | 2.5 | 4.5 | 6
*, cm | 1 | 0.5 | 0.25
Momentum compaction factor, 10-5 | -1.3 | -1 | -0.5
Normalized emittance, mmmrad | 25 | 25 | 25
Momentum spread, % | 0.1 | 0.1 | 0.1
Bunch length, cm | 1 | 0.5 | 0.25
Number of muons / bunch, 1012 | 2 | 2 | 2
Number of bunches / beam | 1 | 1 | 1
Beam-beam parameter / IP | 0.09 | 0.09 | 0.09
RF voltage at 1.3 GHz, MV | 12 | 150 | 600
Proton driver power (MW) | 4 | 4 | 2
*) based on extrapolation, not a real design yet

## Slide 15
Lattice Design Plans(from 2014 DOE review)
15
Muon Collider Design – Y.Alexahin, MAP14, Fermilab 05/29/2014
 | person-months
 3 TeV MC lattice with quadruplet FF | 6
 Halo extraction scheme for high energy MC electrostatic separator – too long (~25m for 3TeV) RF or pulsed septum ? bent crystals ? – First look quite encouraging | 3
 Tolerances on field errors and misalignments | 3
 Longitudinal dynamics in HF with wakes and beam-beam | 6
 Update of the HF lattice | 3
 6 TeV lattice design | 6
 1.5 TeV MC lattice with quadruplet FF (?) | 3
Total (rough estimate) | 30*

## Slide 16
16
Muon Collider Design – Y.Alexahin, MAP14, Fermilab 05/29/2014
Most Urgent Items
 Finish of the 3TeV MC lattice with quadruplet FF (will be done no matter what by end of July)
 Study tolerances on field errors and misalignments – very important for understanding the real constrains on beta-functions, momentum compaction factor etc. (will be done only if sanctioned)
 First look at 6TeV lattice (?)
Other items can be put on a slow burner
Collider Ring |  | Concept Specification | Lattice Files & Performace Eval | Lattice Sign-off | Interface Params | Technology Specification | Technology Sign-Off | IBS Review Ready Date | IBS Initial Review (where needed) | IBS Review | IB Specifications (Dependent on results from previous system)
 | Higgs Factory | 10/1/2013 | 3/30/2014 | 4/29/2014 | 5/29/2014 | 9/26/2014 | 10/26/2014 | 1/27/2015 | 2/26/2015 | 1/27/2016 | 8/29/2016
 | 1.5 TeV (2 & 4 MW Source) | 10/1/2013 | 3/30/2014 | 4/29/2014 | 5/29/2014 | 9/26/2014 | 10/26/2014 | 1/27/2015 |  |  | 
 | 3 TeV (2 & 4 MW Source) | 10/1/2013 | 7/28/2014 | 8/27/2014 | 9/26/2014 | 1/24/2015 | 2/23/2015 | 5/27/2015 |  |  | 
 | >5 TeV (<2 MW Source) | 10/1/2014 | 2/28/2015 | 3/30/2015 | 4/29/2015 | 8/27/2015 | 9/26/2015 | 12/28/2015 |  |  | 
 | Ring-MDI Interface Parameters | 10/1/2014 |  |  | 4/29/2015 |  |  |  |  |  | 8/29/2016

## Slide 17
17
Muon Collider Design – Y.Alexahin, MAP14, Fermilab 05/29/2014
Support Slide - Higgs Factory Specifics
 Large N  small * to achieve the required luminosity  very large IR magnet apertures (up to ID~50cm).
 Preservation of small E /E ~310-5 in the presence of strong self-fields (Ipeak ~ 1kA !)  LARGE momentum compaction c ~ 0.1
 Chromaticity correction is still necessary due to path lengthening effect and operational considerations.
Path length dependence on betatron amplitude (L. Emery, HEACC’92, Hamburg) translates into additional energy spread*:
With uncorrected Q~ -100 and c =0.05 we would have

## Slide 18
18
Muon Collider Design – Y.Alexahin, MAP14, Fermilab 05/29/2014
*(m)
Emax (MeV)
s=5.6cm
s/s
s=10cm
E (MeV)
s=5.6cm
*=2.5cm
Longitudinal Beam-Beam Effect (Derbenev & Skrinsky, 1972)
Effective gradient is ~0.7 MV/m for cited parameters, can exceed 2 MV/m for the upgrade.
Higher-frequency (500MHz) RF for compensation?
Collision with a thin slice of Ns particles leads to energy change
For c > 0 the effect is defocusing (good), but it is strongly nonlinear (not so good).
The finite bunch length reduces it somewhat: