## Slide 1
R. Garoby for
S. Atieh, I. Aviles Santillana, G. Arnau Izquierdo, R. Bonomi, O. Brunner, S. Calatroni, O. Capatina, J. Chambrillon, F. Gerigk, M. Guinchard, T. Junginger
P. Maesen, M. Malabaila, L. Marques Antunes Ferreira, A. McPherson,
S. Mikulas, E. Montesinos, V. Parma, F. Pillon, J. Plouin, T. Renaglia, K. Schirm, T. Tardy, M. Therasse, A. Vacca, N. Valverde Alonso,
A. Vande Craen, M. Vretenar etc.
SPL R&D at CERN
https://indico.fnal.gov/conferenceDisplay.py?confId=8365
Collaboration Meeting
Fermilab 3-4 June 2014

## Slide 2: CERN Motivation for the SPL R&D (1/5)
Þ Possibility of new injectors in the future (HE-LHC…)
PSB
SPS
Linac4
LP-SPL
PS
LHC
160 MeV
1.4 GeV
4 GeV
26 GeV
50 GeV
450 GeV
7 TeV
Linac2
50 MeV
Proton flux / Beam power
PS2
Present
Typical Future
1978
1975
1959
2008
LP-SPL: Low Power-Superconducting Proton Linac
PS2: High Energy PS (~ 5 to 50 GeV – 0.3 Hz)
PS2
SPL
LINAC4
SPS
PS
e.g.: Plan until 2010

## Slide 3: CERN Motivation for the SPL R & D (2/5)
Þ Options for neutrino physics (Conventional n Superbeams)
Accumulation of HP-SPL beam in a fixed energy Accumulator
(4-5 GeV, 4MW beam power)
Fast ejection onto target(s)
Low energy n beam
Medium energy n beam
Phase 1: SPS (400 GeV -700 kW)
Phase 2: HP-PS (50 GeV – 2 MW)
LP-SPL as 4 GeV injector of a High Power 50 GeV synchrotron
(50 GeV, 2 MW beam power)

## Slide 4: CERN Motivation for the SPL R & D (3/5)
Þ Options for neutrino physics (n Factory)
Accumulation of beam from the High Power SPL in a fixed energy Accumulator (4-5 GeV, 4MW)
Bunch compression («rotation») in a separate Compressor ring
Fast ejection of few (3-6) short (2 ns) bunches to target

## Slide 5: CERN Motivation for the SPL R & D (4/5)
Þ Next generation Radioactive Ion Beam Facility (~EURISOL)
TARGETS
RADIOACTIVE IONS LINAC
EURISOL EXPERIMENTAL HALLS
ISOLDE OR
EURISOL HIGH ENERGY EXPERIMENTAL HALL
TRANSFER LINES SPL to EURISOL
TRANSFER LINE SPL to ISOLDE

## Slide 6: CERN motivation for the SPL R&D (5/5)
  Þ Synergy with other applications at CERN (FCC-hh, -ee, -eh…) as well as outside of CERN (ESS, ADS…)
  ß
Need to update CERN capacity in superconducting RF:
  Update of staff competencies
  Upgrade of infrastructure (SM18 clean room, High Power RF, High Pressure Water Rinsing facility, Diagnostics for SC RF, New e-beam welding machine, Electro-polishing installation, etc.)

## Slide 7: SPL main characteristics
 | Option 1 | Option 2
Energy (GeV) | 2.5 or 5 | 2.5 and 5
Beam power (MW) | 2.25 MW (2.5 GeV) or 4.5 MW (5 GeV) | 5 MW (2.5 GeV) and 4 MW (5 GeV)
Protons/pulse (x 1014) | 1.1 | 2 (2.5 GeV) + 1 (5 GeV)
Av. Pulse current (mA) | 20 | 40
Pulse duration (ms) | 0.9 | 1 (2.5 GeV) + 0.4 (5 GeV)
2 ´ beam current Þ 2 ´ nb. of klystrons etc .
Re-use of LEP RF components in Front-end (Linac4)
Ion species H−
Output Energy 5 GeV
Bunch Frequency 352.2 MHz
Repetition Rate 50 Hz
High speed chopper < 2 ns
(rise & fall times)
Required for muon production (Neutrino Factory)
Required for flexibility and low loss in accumulator
Required for low loss in accumulator
General features
Options
n facility
RIB facility

## Slide 8: SPL potential front end: Linac4!
Doubled beam brightness for LHC luminosity: reduced space charge (factor 2 in bg2 ) with a higher PSB injection energy
Long term reliability using modern design, (concerns for Linac2 vacuum ).
Flexible operation and reduced loss with new technologies (chopping, H- injection).
Higher intensity for non-LHC users.
Prepare for a possible high-intensity upgrade (neutrino facility).
New 160 MeV H- linear accelerator, will replace Linac2 as injector to the PS Booster.
First step of the LIU upgrades.
Bunch Frequency 352.2 MHz
Max. Rep. Frequency 2 Hz
Max. Beam Pulse Length 0.4 ms
Max. Beam Duty Cycle 0.08 %
Chopper Beam-on Factor 65 %
Chopping scheme: 222 transmitted /133 empty buckets
Source current 80 mA
RFQ output current 70 mA
Linac pulse current 40 mA
Tr. emittance (source) 0.25 p mm mrad
Tr. emittance (linac exit) 0.4 p mm mrad
Max. repetition frequency for accelerating structures 50 Hz
Test stand
(Construction Project started in January 2008)
Notes: No space for energy upgrade – parallel to the present Linac2

## Slide 9: Linac4
CCDTL
PIMS
3MeV
50MeV
103MeV
160MeV
Length: 80 m
19 klystrons [13 x 1.3 MW (LEP), 6 x 2.8 MW (new)]
Normal conducting accelerating structures of 4 types: RFQ, DTL, CCDTL, PIMS
Single frequency: 352.2 MHz
Duty cycle: 0.1% phase 1 (Linac4), 3-4% phase 2 (SPL), (design: 10%)
H- ion current:
40 mA (avg.),
65 mA (peak)
CHOPPER
RFQ
H-
3MeV
45keV
DTL
Drift Tube
Linac
18.7 m
3 tanks
1+2 klystrons
4.7 MW
111 PMQs
Pi-Mode Structure
22 m
12 tanks
4+4 klystrons
~12 MW
12 EMQuads
Cell-Coupled Drift Tube
Linac
25 m
21 tanks
7 klystrons
7 MW
21 EMQuads
Chopper
& Bunchers
3.6 m
11 EMquad
3 cavities
Radio
Frequency
Quadrupole
3 m
1 Klystron
550 kW
RF volume
source
(DESY)
45 kV
Extrac.

## Slide 10: Linac4 status
Celebration of the first beam acceleration by the RFQ in the Test Stand (13.3.13)
CCDTL structures
Klystrons and modulators in the Linac4 Hall
DTL tank 1
RFQ & MEBT section in the Linac4 tunnel

## Slide 11: SPL block diagram
SC-linac [160 MeV ® 5 GeV] with ejection at intermediate energy
Medium beta cavities: b = 0.65
High beta cavities: b = 1
“Up-to-date” CDR to be published in 2014
Length: ~500 m
Medium b cryomodule
High b cryomodules
Ejection
20 x 3
b=0.65 cavities
10 x 8
b=1 cavities
13 x 8
b=1 cavities
2.5 GeV
Debunchers
5 GeV – 4 MW
High b cryomodules
From Linac4
0 m
0.16 GeV
129 m
0.73 GeV
280 m
2.5 GeV
505 m
5 GeV

## Slide 12: SPL cavities development
Medium beta cavities b = 0.65
  1 designed and ordered from industry by IPN Orsay (Guillaume Olry et al.) to be tested in 2014 at CEA Saclay in vertical cryostat and later in Cryho-lab (Horizontal test cryostat)
High beta cavities b = 1
  1 designed and ordered from industry by CEA Saclay (Guillaume Devanz et al.) to be tested in 2014 at CEA Saclay in vertical cryostat and later in Cryho-lab (Horizontal test cryostat)
  5 designed and ordered (4 from industry, 1 from CERN workshop) by CERN for tests at CERN (SM18) in Short cryo-module of 4 cavities
Collaboration with ESS (Lund) with contributions from IN2P3 and CEA and support from the E.U.

## Slide 13: SPL cavity b = 1 at CEA
Parameters | Value | Units
Frequency | 704.42 | MHz
Number of gaps (Ngaps) | 5 | -
Beta | 1 | -
Eacc | 25 | MV/m
Epeak/Eacc | 1.99 | -
Bpeak/Eacc | 4.20 | mT/(MV/m)
Lacc (Ngaps.bl/2) | 1.0647 | m
r/Q | 566 | Ohms
G | 270 | Ohms
Operation temperature | 2 | K
Q0 at 2K (RBCS=3.2nW) | 8.4.1010 | -
Lorentz force detuning KL | 1 | Hz/(MV/m)²
Cavity design and tests performed at CEA-Saclay
Cavity manufactured by E. Zanon
J. Plouin (SLHiPP-4)

## Slide 14: First test in vertical cryostat (CEA)
The cavity has been cleaned in ultrasound bath and slightly chemically treated using a standard BCP mixture.
Previous tests
Two tests at 1.6 K
April 2014
@ Saclay
Some processing has been necessary from 10 to 12MV/m
Tests have been stopped 17.6 MV/m because high dose rate was measured out of the bunker (> acceptable rate in the Supratech area)
J. Plouin (SLHiPP-4)

## Slide 15: SPL cavity b = 0.65 at IPN-Orsay
FABRICATION
Kick-off meeting: Nov. 2011
Delivery #1 for field flatness tuning done @ IPN Orsay: March 2013
Cavity sent back to RI
Then final delivery after He tank welding: June 2013 (fabrication time=19 months!)
CAVITY PREPARATION
1st etching (BCP): 200 µm
Field flatness tuning
2nd etching (BCP): 20 µm
2-hour HPR through beam tubes only (6 passes)
No 600°C annealing nor 120°C baking
2nd etching pass: cavity with He tank
Cavity w/o He tank before field flatness tuning
J. Plouin (SLHiPP-4)
Test at 2 K in June 2014

## Slide 16: Niobium cavities from industry (RI)
4 Niobium cavities fabricated and delivered by RI (December 2013)
Test at 2 K in June 2014

## Slide 17: Niobium cavities at CERN
Tooling for EB welding of Nb cavity is fabricated.
cavity fabrication at CERN
Repair of first monocell
Material defects observed after electro-polishing.
Repaired with new e-beam welding machine from outside (W#1 and W#3) and inside (W#2)
Half-cells and beam tubes fabricated by spinning.
RF measurements.

## Slide 18: SPL mono-cell b =1 at CERN
A. Macpherson (SLHiPP-4)

## Slide 19: New e-beam welding machine

## Slide 20: Electro-Polishing (EP)
Cathode and tooling manufacturing
Improve main pump flow control and compressed air connection
Allow crane direct acces to the electropolishing hut
- Monocell TESTS:
A second set of electropolishing sessions were done to bring the total removed thickness to 200 microns.
It was possible to set different working temperatures and compare them with the simulation data
Working at lower temperatures results in less pitting.
Cavity is currently undergoing RF test
Paper TUP047 bat SRF with all multiphysics simulation details
Temperature | Total current inward / A | 
 | Simulation | Real cavity
10 °C | 21 | 18
15 °C | 37 | 36
25 °C | 70 | 57
- 5 Cell electropolishing preparation:
Tooling for EP

## Slide 21: Helium tank
Helium tank designed by CERN (Stainless steel).
5 items under fabrication by CEA (with SDMS).
Stainless Steel He tank (CEA)

## Slide 22: SPL Fundamental Power Coupler
Disk window Coupler
Cylindrical window Coupler
Two designs with the same:
  Double walled tube
  Matching waveguide without doorknob
  Contacts ring including DC capacitor
  Interface to
  cryomodule flange &
  RF + vacuum gasket
E. Montesinos (SLHiPP-4)

## Slide 23: Power Couplers Test program
A number of issues remain pending and will continue to be investigated/solved (!)
Initial test program has been modified (eased) accordingly
Nevertheless the available couplers remain fully compatible with SM18 tests program
Yesterday evening (6 pm, May 15, 2014), tests of the second pair of couplers were successfully completed!
Test Repetition rate 50 Hz | Initial kW | New kW
TWC | 1000 | 1000
SW 100 µs | 1000 | 1000
SW 200 µs | 1000 | 500
SW 500 µs | 1000 | 250
SW 1 ms | 1000 | 250
SW 2 ms | 1000 | 250
E. Montesinos (SLHiPP-4)

## Slide 24: Power Couplers: Next steps
We now have to EBW the couplers at the DT flange level to the cryomodule ‘flanging system’
Very delicate step in the process as it can destroy 4 years of construction and tests
Mock-ups are under construction to train the specialist
Last critical operation on couplers before assembly onto cryomodule
EBW
E. Montesinos (SLHiPP-4)

## Slide 25: Power Couplers: Next steps
Integration onto the cryomodule in CERN SM18 clean room
FPC TD being the support of the cavities
E. Montesinos (SLHiPP-4)

## Slide 26: Tests systems and cavity reception area (Bdg. 252)
Cell-by-cell tuning system with RF bead-pull and mechanical measurements.
Cavity tuner: measurement of cavity detuning versus mechanical deformation.
Tooling for test in vertical cryostat: fabricated and available at CERN
Reception area in bdg.252

## Slide 27: SPL cryomodule
27
SC Cavities
Design: CERN
Production: 5-cells, 1-cell in Nb and Cu produced by CERN and industry
He tank
Design: CERN
Production: Industry (CEA)
Mag. Shield
Design: CNRS (CERN spec)
Production: Industry
RF Power Coupler
Design: CERN (BE-RF, TE-MSC)
Production: CERN
Test: CEA (He, RF); CERN (N2)
Intercavity supports
Design: CERN
Production: CERN
Test: CERN (N2)
Vacuum vessel
Design: CNRS
Production: Under procurement
(construction before April 2015)
Tuner
Design: CEA
Production: CEA
R. Bonomi (SLHiPP-4)
Collaboration with ESS (Lund) with contributions from IN2P3 and CEA

## Slide 28: Mock-up: T Distribution
Test results, typical *
  No gas flow, steady state, cavities filled with LN2
288 K
(10 W)
28
77 K
103 K
93 K
80 K
77 K
77 K
77 K
147 K
207 K
256 K
* Data from April 2014.
R. Bonomi (SLHiPP-4)
Notes: Lets start from a typical temp distribution obtained last month during the test:
Cavities were kept cold, whereas dwt were not actively cooled
For example, we can highlight the t distrib obtained for the ics and for the dwt => ..

## Slide 29: Cryo-module Assembly tooling
CNRS-IPNO
Blocs Bétons
Système de levage
Cadre de manutention
Supports de réglage
Poutre principale
Vérins LHC

## Slide 30: SM18: new Clean Rooms & HPR
15m long Cleanroom for cryomodule assembly
15m long grey room for cryomodule preparation
Cavity HPR & drying
Personnel entrance
P. Maesen (SLHiPP-4)

## Slide 31: SM18: New Clean Rooms & HPR
P. Maesen (SLHiPP-4)

## Slide 32: SM18: ultra pure water production
Delivered and commissioned in Oct’13
To be placed in final position and restarted…
P. Maesen (SLHiPP-4)

## Slide 33: SM18: Horizontal bunkers and vertical cryostats
M7
M9
V3
V4
V5
V6
P. Maesen (SLHiPP-4)

## Slide 34: SM18: waveguide network
Integration in M7 well advanced (BE/RF, EN/MME (drawing office))
  Power distribution
  Cryomodule (incl. slope)
  New standard 2 K service module
Still to be done:
  Detailed integration of cryomodule repair scenarios
    (i.e. how to lift the top cover of the CM?)
  Cabling (RF and Cryo)
  Cryogenic valve box under design
P. Maesen (SLHiPP-4)

## Slide 35: SM18 High Power RF upgrade (704 MHz)
    1.5 MW Thales klystron – delivery beginning 2014
    Klystron modulator – delivery beginning 2014
    New Low Level RF at 704 MHz – by end of 2014
Collaboration with ESS (Lund)

## Slide 36: High Power IOT development (704 MHz)
    Two 1.5 MW IOTs being ordered by ESS
    Test set-up in preparation at CERN
    Full characterization in 2015-2016 (joint ESS-CERN)
Collaboration with ESS (Lund)

## Slide 37: SPL R&D schedule
2014
2015
Preparation of components
Assembly of CM

## Slide 38: Summary
Linac4 in construction. Fully operational at the end 2016.
Design and development of a new type of multi-cavity cryomodule,
Design and development of “cheap” high power couplers (8 built; 2 successfully tested today).
Extensive investment for superconducting cavities fabrication and test (e-beam welding machine, ep bench, optical bench…)
2 five-cell copper cavities, one bulk-niobium monocell produced,
4 five-cell bulk Niobium manufactured by industry (RI),
One five-cell bulk Niobium in fabrication at CERN with an R&D approach,
Equipment for testing at high RF power (704 MHz) a string of 4 cavities cooled at 2 K in SM18
A string of four SPL 704 MHz b =1 cavities will start being tested in a short cryo-module at the end of 2015.
Update of CERN competencies
in superconducting RF.

## Slide 39
THANK YOU
FOR YOUR ATTENTION!