## Slide 1: R&D Status/PXIE
Lionel Prost
Fermilab
PIP-II Collaboration Meeting
June 3-4, 2014
Ion Source/LEBT

## Slide 2: Outline
Beam line design
Ion Source commissioning at Fermilab
Configuration with one solenoid
  First measurements
Present configuration
  Status
Plans

## Slide 3
Beam line design
Ion Source commissioning at Fermilab
Configuration with one solenoid
  First measurements
Present configuration
  Status
Plans

## Slide 4: PIP-II IS & LEBT beam line
Optics have not changed since Fall 2012 Collab. Mtg.
  Space-charge dominated transport after chopper (in DC mode)
  Details of components evolve as their design progresses
Combined kicker and absorber i.e. when deflected, the beam impinges onto one of the kicker electrodes
No isolated diaphragm in solenoid #3 anymore

## Slide 5
Beam line design
Ion Source commissioning at Fermilab
Configuration with one solenoid
  First measurements
Present configuration
  Status
Plans

## Slide 6: Ion source assembly at CMTF
Faraday cup (inside)
Isolated cable tray (from HV cabinet to IS)
IS vacuum chamber
IS body
Water distribution system
Authorization to operate at CMTF on 11/22/13
Qing Ji came to help with the startup

## Slide 7: Ion source commissioning
Typical learning curve for a new machine i.e. unforeseen issues (mostly)
  HV sparks leading to Filament PS trips
  Isolation transformer failure (manufacturing defect  replaced by vendor + bought 1 spare)
  Mass flow controller mis-located at ground instead of HV
Duplicated many of the measurements made at TRIUMF and LBL
  Except emittance (scanner not ready)
E.g.: Beam current as a function of the Arc power
Not all IS parameters are the same for all data sets
Ion Source characteristics measured at CMTF are consistent with both TRIUMF and LBNL data

## Slide 8
Beam line design
Ion Source commissioning at Fermilab
Configuration with one solenoid
  First measurements
Present configuration
  Status
Plans

## Slide 9: First configuration with one solenoid
Solenoid
DCCT
Faraday Cup
‘Stand-alone’ isolated diaphragm a.k.a. donut
Solenoid isolated diaphragm connectors
Includes:
  A ‘stand-alone’ isolated diaphragm between the DCCT and the Faraday cup for beam size measurements
  Capability to pulse the extraction electrode

## Slide 10: Measurements
Beam size
  Mostly in pulsed mode
    Pulse width: 1 ms < tpulse < 2 ms
      Long pulse  DC-like (near the end)
    Frequency: 0.25 Hz < fpulse < 10 Hz
Emittance
  Estimated from beam size vs. solenoid current scans
  Neutralization effect
    Data taken within the beam pulse
Neutrals
  Estimates with calorimetric data
    DC beam

## Slide 11: Beam size measurement method
Beam size is obtained by moving the beam across the donut aperture
  Beam current in FC vs. Solenoid corrector current
  Long pulses (typically 200 ms) or DC
Current to FC as a function of the solenoid correctors for 6 solenoid currents, from 168 to 148A.
Data were taken with B. Marsh’s Java application.
Beam
Donut aperture
Solenoid corrector current [A]
Faraday cup current [mA]
04/25/14

## Slide 12: Data analysis procedure
Fit entire curves (i.e. from extinction to extinction) assuming a Gaussian or constant current density (a.k.a. Flat) distribution being sampled across a round aperture
  Fitting with up to 4 parameters
    Beam current
    Correctors calibration coefficient (i.e. mm/A)
    Center position
    Rms beam size
  All parameters but the beam size can be measured independently or as a subset of the ensemble of curves
    Then, can fit with only one parameter, i.e. the rms beam size
  ‘Goodness’ of the fit may indicate which distribution is a closer representation of the real distribution
Example of fitting of the curves for the solenoid current of 168 A with Gaussian distribution
Solenoid corrector current, A

## Slide 13: Solenoid scans
Beam size measurements in pulse mode acquiring data for several ‘time slices’ within the pulse
  10, 30, 50, 100 and 180 ms from the leading edge (delay)
Fitting with both distributions give similar results
  Typically within 10%
Displacement of the minimum beam size with the delay is a good indication of neutralization
  Neutralization time >100 ms
Results of fitting the data to Flat (solid lines) and Gaussian (symbols) distributions. Series are labeled by the delay in µs.
Beam current = 5 mA (DC-equivalent)

## Slide 14: Emittance estimation
The beam size as a function of the solenoid current is fitted to a model of a thin lens without space charge
  Not self-consistent approach
Emittance calculated with this procedure is higher by a factor of ~2 at the beginning of the pulse
  Emittance value consistent with previous data taken at TRIUMF and LBNL
For reference: Emittance measurements from acceptance tests at TRIUMF (DC beam)
Beam current = 5 mA (DC-equivalent)
Emittance vs. delay
~5 mA

## Slide 15: Estimation of the amount of energetic neutrals (H0)
With the beam well centered in the donut, its temperature still rises significantly
  Indicates particles loss
Neutrals
Donut
DCCT
Red and blue lines: Primary beam envelope (simulation)
Thermal characteristics of donut (measured) & measurements of the sum of currents (FC + donut) with solenoid on and off
  Neutrals amount to ~7% of the total beam current
  Assuming a Gaussian distribution, ~10% of these propagate downstream
    The longer the LEBT the smaller this number

## Slide 16
Beam line design
Ion Source commissioning at Fermilab
Configuration with one solenoid
  First measurements
Present configuration
  Status
Plans
Picture of the beam after spoiling vacuum (04/15/14)

## Slide 17: Present configuration
Installation of the emittance scanner (05/12)
  Design and fabrication in collaboration with SNS

## Slide 18: Current setup in picture
DCCT
Faraday Cup
‘donut’
Emittance scanner probe
Gate valve
Turbo pump

## Slide 19: Emittance scanner commissioning
Current emphasis of shift work
  ‘Mechanics’ of data acquisition work
  Expect to start sensible measurements this week or next
    Some calibration factors and other details need to be ironed out
Labview GUI
Emittance scanner on assembly rig

## Slide 20
Beam line design
Ion Source commissioning at Fermilab
Configuration with one solenoid
  First measurements
Present configuration
  Status
Plans
Solenoid #1 setup for magnetic measurements in TD

## Slide 21: Plan (FY14)
Finish characterization of the beam through ~1m of the LEBT (including beam dynamics through one solenoid)
  Emittance scanner commissioning
Installation of the full length LEBT
  Goal is to start commissioning mid- to late July
    All solenoids have been delivered and are being measured
    A lot of the infrastructure is ready or nearly ready (e.g.: water distribution system)
    Current ‘push’ on the design of the chopper

## Slide 22: Backup slides

## Slide 23: Issue
The beam size and angle of propagation of the beam exiting the ion source results in losses in the bellow preceding the first solenoid
  Bellow ID smaller than expected
  Beam centroid output angle larger than expected
Beam loss estimated to correspond to ~10 W
  Not a thermal issue but may cause sputtering/blistering
  Added a ‘shield’ at the exit of the IS vacuum chamber
With shield
Picture of the beam after spoiling vacuum (04/15/14)
04/11/14
5 mA
ISol = 160 A

## Slide 24: (Very) First configuration with one solenoid
Solenoid
DCCT
Turbo pump
Faraday Cup
Gate valve
Pulser
Isolated diaphragm connectors