## Slide 1: Overview of Booster PIP II upgrades and plans
C.Y. Tan
for Proton Source group
PIP II Collaboration Meeting
03 June 2014

## Slide 2: PIP II Booster parameters
50% higher flux than the planned PIP operations which is expected to double present flux level. (4.3e12 protons @15 Hz at the end of PIP I)
30% decrease in space charge tune shift @ 800 MeV.
Longitudinal emittance determined by Recycler slip stacking requirements.

## Slide 3: New injection point into Booster
New injection point at L11.
Old injection point at L1

## Slide 4: Overview of required R&D
  New injection point at L11.
    New injection girder.
    Space charge mitigation: painting.
    New stripping foil.
    H0 , H- absorber
  RF capture
    capture scheme: paraphasing or direct injection into buckets
    2nd harmonic cavities (considered but probably unnecessary).
  Transition crossing
    RF focusing method.
    RF focus free method (flattening of RF amplitude)
      2nd or 3rd harmonic cavities. (can also be used in RF focusing method)
    γt jump system
      requires resurrection/rebuild of old system.

## Slide 5: Overview (cont’d)
Damper upgrades and collimation system
    longitudinal quadrupole damping when going through transition.
      Will require voltage overhead in RF system
    longitudinal coupled bunch mode damping at high field.
      Will require an increase in RF power
    Transverse dampers for coupled bunch modes.
      Higher intensity may require more power for kickers.
    Evaluation of present collimation system w.r.t. expected PIP II loss
Beam quality at extraction
  emittances determined by Recycler admittances.
    18 π mm mrad (6 σ normalized)
    0.08 eV s (97%)

## Slide 6: New injection girder
Beam can enter either horizontally or vertically.
A new 3 bump system that can take 800 MeV beam (2x stronger)
Beam painting to mitigate space charge effects because of longer injection time (0.6 ms)
Carbon foil for stripping (15 turns vs 315 turns)
  Lifetime effects.
New beam absorber for H0 and H-
  Build inside a gradient magnet.
  Design new stronger and shorter gradient magnets to make space for an absorber. (Preferred)

## Slide 7: Foil
For a std. foil thickness 380 mg/cm2 (1.15 mm)
400 MeV -> 99.9% efficiency to protons
800 MeV -> 99.1% efficiency to protons
To match 400 MeV efficiency at 800 MeV foil thickness needs to increase to ~545 mg/cm2
At 800 MeV with 7E12 injected at 15 Hz
Injection power increases to ~ 13 kW.
For a 2% loss -> 260 Watts on downstream gradient magnet.
-> Need to provide injection absorber
current foil
current foil holder

## Slide 8: Stripping efficiencies at 800 MeV
stable
Strip immediately
Field in 4th chicane
Chart: Lorentz Stripping
| 2.0 | 2.25 | 2.5 | 2.75 | 3.0 | 3.250000000000001 | 3.500000000000001 | 3.750000000000001 | 4.000000000000002 | 4.250000000000002 | 4.500000000000002 | 4.750000000000002
800 MeV | 2.1253e-16 | 4.5164e-14 | 3.323e-12 | 1.1293e-10 | 2.1488e-09 | 2.6153e-08 | 2.2397e-07 | 1.4473e-06 | 7.4382e-06 | 3.1647e-05 | 0.00011501 | 0.00036595
400 MeV | 8.3176e-14 | 1.4018e-12 | 1.6667e-11 | 1.4863e-10 | 1.0428e-09 | 5.9777e-09 | 2.8851e-08 | 1.2014e-07 | 4.4043e-07 | 1.4449e-06 | 4.3013e-06 | 1.1754e-05

## Slide 9: Vertical Injection Concept
ORB 1-2: 22 mr
ORB 3-4: 33 mr
DC sep: 78 mr
H-
H0
aperture
H-
1
2
3
4
sep
foil

## Slide 10: Injection painting for space charge mitigation
Green: injected beam.
Red: phase space after painting.
Beam line matching conditions for two painting scenarios. Left paint in both planes in the ring (SNS) and right paint horizontal in ring and steer (angle mismatch) from beam line (JPARC).
Note: ellipses were calculated for 1GeV injection.

## Slide 11: Capture (adiabatic at 800 MeV)
0.6 ms injection time.
0.4 ms adiabatic ramp to full voltage (1 MV)

## Slide 12: Capture (bucket to bucket injection)
Chopping 180 deg
Chopping 120 deg
0.6 ms injection time.
Chopping is required to get the correct bunch pattern into the bucket.
2 mA for 0.6 ms gives 7.5e12 particles.
May need flattened front porch for injection

## Slide 13: Transition crossing
Transition crossing at 4.2 GeV
More RF for focusing during transition.
~25% more RF implies 3 – 4 more RF cavities using present design. (22 – 23 cavities)
Example shown here is the compensation of the effect of space charge that is defocusing before transition & focusing after transition.
Increase RF voltage before transition
Increase RF voltage again to damp out quadrupole oscillation.

## Slide 14: Perpendicular biased cavities
490
70
40
200
220
195
Ferrite
BeO
390
Designed by G. Romanov
Example here: 2nd harmonic cavity
Simulations of use at injection for PIP I and possible use as main RF cavity is underway.
Units in mm

## Slide 15: What was done recently
Measured m and Q (tan d) resonantly with a 1.5” OD sample of AL400: measure fres, then with c = f l
center conductor
short
L = 5”
l/4 = L * √(me)
AL400
outer conductor
1.5”
Work done by D. Wildman and R. Madrak

## Slide 16: Old (S11) and New(Resonant) Measurements
Chart: Effective permeability vs. Hint
| -1.704700000000017 | 17.96704999999998 | 36.47723 | 54.875 | 73.60999999999998 | 92.345 | 111.4547 | 129.815 | 148.55 | 186.02 | 223.49 | 261.7093999999996 | 298.8047 | 337.0240999999999 | 373.7447 | 410.84 | 448.3099999999999 | 485.7799999999999 | 523.9994 | 561.0946999999999 | 598.9394 | 635.6599999999994 | 673.8794 | 710.9747
resonant meas | 12.1398 | 9.9702 | 7.8864 | 6.5306 | 5.5766 | 4.8808 | 4.314 | 3.8977 | 3.5696 | 3.0682 | 2.7466 | 2.503 | 2.3296 | 2.1926 | 2.0791 | 1.9928 | 1.9099 | 1.8565 | 1.791 | 1.7478 | 1.7039 | 1.6693 | 1.6362 | 1.6063
theory curve, valid region | 4.6509 | 4.1301 | 3.7319 | 3.1775 | 2.8095 | 2.5433 | 2.3503 | 2.196 | 2.0777 | 1.9798 | 1.8974 | 1.8277 | 1.7671 | 1.7161 | 1.6706 | 1.6317 | 1.5957 | 1.5645
theory curve, invalid region (M < Ms) | 24.5783 | 12.3431 | 8.481 | 6.5534 | 5.4147 | 4.6509
S11, 76 MHz | 7.5139 | 7.3483 | 6.2086 | 4.8784 | 3.9382 | 3.353 | 2.9637 | 2.6792 | 2.4592 | 2.2955 | 2.1604 | 2.0566 | 1.9676 | 1.8934 | 1.8329 | 1.7811 | 1.7353 | 1.6962 | 1.6611 | 1.6285 | 1.6002
S11, 106 MHz | 4.3263 | 4.4645 | 4.6445 | 4.1113 | 3.4634 | 3.0006 | 2.6924 | 2.4768 | 2.3151 | 2.1943 | 2.0933 | 2.0116 | 1.9394 | 1.8772 | 1.8245 | 1.7778 | 1.737 | 1.7001 | 1.6668 | 1.6367 | 1.6102
Work done by D. Wildman and R. Madrak

## Slide 17: Dampers
Longitudinal coupled bunch and quadrupole mode dampers
  More RF volts is required whatever scheme is chosen.
    E.g. Increase the number of RF cavities from 18 to 21 using present design will give ~150 kV.
    Change from parallel biased cavities to perpendicular biased cavities could potentially increase volts/cavity from ~50 kV to ~60 kV and give 180 kV increase.
  PIP I is working on improving present cavity design and perpendicular cavity design.
Transverse and longitudinal dampers
  PIP I upgrading analog dampers to digital dampers.

## Slide 18: Collimators
PIP I plan is to reinvestigate present collimation operations and issues related to PIP I goals.
  No upgrade of collimation is presently planned.

## Slide 19: Loss requirements
Historically Booster losses is maintained <= 525 W ring wide.
Independently set beam loss monitor trip points at each long and short straight sections.
For PIP II
  Keep ring wide activation at the present level would be recommended
  Control loss points to be at collimators and beam dump
  Notching in Linac will help reduce losses. Presently 3 bunches are kicked out => 95% efficient.
    Ability to keep notch clean after multiple turns
    Synchronization of Linac and Booster for extraction kickers and notch

## Slide 20: Summary
There is an R&D effort in place. Preliminary work has been started to find solutions to potential problems that we have identified:
  New injection girder
  RF capture
  Transition
  RF cavities
Beam quality
  Determined by keeping instabilities under control.
  Constrained by Recycler requirements.