## Slide 1: LBNE Prototype Detector in the 35t Membrane Cryostat
Alan Hahn
FNAL

## Slide 2: Talk Outline
35 Ton Phase 2 Motivation
  Goals for 35 T Phase 2
Design Choices/Compromises
  Far Detector APA
  35T Prototype Detector
Summary

## Slide 3: 35t Motivation
During the (2012) reconfiguration of LBNE, we lost LAr-1, a 1 kT cryostat to be built at D0
  LAr-1 was meant to be our full system test of the FD Prototype components.
  Could hold 3 full scale APAs with 6 CPAs
    Each 7m high by 2.5m wide
  Able to track cosmic rays.
To regain partial design verification, we “re-purposed” the program of the 35 Ton Cryostat to include a “Phase 2”
  Phase 2, a facility to enable a subset of the LAr-1 prototyping goals.

## Slide 4: 35-Ton Phase 2 Goals
Build a complete functional reduced-scale sized TPC with Photon Detectors inside the 35-ton cryostat.
TPC components will closely resemble the full size counterparts.
  APAs will incorporate functional photon detectors
Goals of this prototype TPC
  Validate the design of nearly all TPC components (at a small scale); testing the integrity of all components and their interconnects in LAr.
  Study the performance of the wire wrapping readout scheme, and the impact of the gaps between APA modules.
  Study the electronics noise contribution from potential sources: acoustic, pump, flow driven wire or field cage motion, high voltage ripple coupling, coupling between digital and analog circuits, etc.

## Slide 5: LBNE Full Scale Anode Plane Assembly (APA)
Photon Detectors
2 APAs
Note: current PD design utilizes SiPMs, not PMTs as depicted in this drawing
APA Features
Photon Detectors are integral to APA
Grounded wire mesh to frame members
X (collection) wires strung from top edge, terminate at bottom edge
  X wires on front and back of APA are independent, NOT wrapped.
U, V (induction) wires are wrapped around APA, at ~45o
  All terminate at bottom edge
Grid wires on top layer
7 m
2.5m

## Slide 6: Wrapped U, V Wire planes
APA U, V wires wrap around frames
  X wires are unique to each side
  Can we reconstruct? (“dis-ambiguation”)
Photon Detectors are built into the APA.
  Can they help with dis-ambiguation?
  Can they trigger on Super Nova burst events?
From Fig 3.4 of CDR
~29 wire spacings
7 m
2.5 m

## Slide 7: 35 T Detector Implementation-- Obvious issues-- size
~75 cm access diameter

## Slide 8: 35T Prototype Detector Choices
Size restrictions
  Cryostat dimensions
  Entry diameter
However:
  Want two drift regions to check double-sided APA, but want at least one region with drift comparable to actual FD drift distance
    2.23m and 0.27m
  Want at least ~2m long wires to check for microphonic pickup
    Full size FD APA has wire supports every 2m
    35T “Long” APAs have unsupported “X” wires ~ this long
  Want to see any charge collection issues on edges between APAs

## Slide 9: 35T Detector 3D Solid Model (J. Fowler)

## Slide 10: Anode Plane Assembly (APA) Layout in 35T Cryostat
APA Support Structure
2 Long APAs
2 short APAs
Photon Detectors
In APAs (3 in each Long,
1 in each Short APA
Cosmic Ray
Counters
m
Cosmic Ray Counters
Cosmic Ray
Counters
~4m

## Slide 11: LBNE Style TPC in 35T Cryostat
2.23m drift region
27 cm short drift region
Photon Detectors
(8 total) in 4 APAs
J. Fowler
Cosmic Ray Counters (CRCs)
Field Cage not shown
Cathode Plane
Cathode Plane
CRCs
CRCs

## Slide 12: 35T Detector “Features”
TPC
  2048 instrumented wires with prototype FD digital readout
  500 V/cm drift field
    2.2 m drift in large drift volume (111 kV), 1.4ms e- max drift time
    0.27 m in small drift volume (14 kV), 0.2 ms e- max drift time
Photon Detectors
  Eight in total
    Three in each long APA
    One in each short APA
  Three different styles
    Four “4-bar” PDs with various wavelength shifter technologies
    Three “32 fiber” PDs
    One plate coated with TPB and with WLS fiber readout
DAQ
  Based on SLAC RCE (Reconfigurable Cluster Elements) Front Ends
  artDAQ Back Ends.
  NOVA timing module
External Cosmic Ray Counters on sides and top to guarantee events in drift regions we want to probe.

## Slide 13
35 T “Long” APA Fabrication – winding (L. Greenler, PSL)

## Slide 14: Field Cage (B. Yu)
Weight of a CPA is ~240 lbs. [ 110 kg
CPA Long Drift Side
(B. Sands)
HV donut part of this side assembly

## Slide 15: Front End Motherboard for 35-ton Phase 2 TPC (H. Chen)
15
15
15
15
15
Notes: 15

## Slide 16: 35T Phase 2 DAQ (G. Barr)
Photon
Detectors
(analog )
TPC Digital Stream
External
Cosmic Ray
Counters (logical)
“BR”=Board Readers
(Run Control)
(Online Monitoring)
(All cold Detector
Cabling comes through
flange board)
(trigger logic)
  (SiPM Signal
  Processor)

## Slide 17: 35 Ton Running Modes (M. Graham)
TPC
  Continuous Mode: continuous streaming (zero-suppressed in RCE) data
  Tagged mode: External Cosmic Ray Counters (CRC) tagger
  Burst mode: all (no 0-suppression) data from TPC
    Limited to a few drift times
  Single channel: all (no 0-suppression) for a single or few #’s of channels
Online Software on backend combines data from the detector systems & makes decision whether to keep data.
  In Continuous Mode, require that data has a PD or CRC signal

## Slide 18: Conclusions
35T Phase 2 Run will be a demonstration of the LBNE Style Detector, testing most of the concepts of the LAr Far Detector
Installation of Detector into Cryostat in late fall.
Cooldown and commissioning in early 2015 (CY)