## Slide 1: First Integrable Optics Experiment at IOTA
Sergey A. Antipov, The University of Chicago
Advisor: Sergei Nagaitsev

## Slide 2: Motivation: Linear Dynamics
Linear focusing lattice – betatron tunes of different particles are almost equal
  Hamiltonian depends on time
  Nonlinearities (both magnet imperfections and specially introduced) make single particle motion unstable due to resonances
  Stability depends on initial conditions
Phase space of 1D motion in linear lattice with 1 octupole nonlinearity
Resonance aisles
Chaotic motion
Particles lost
X (a.u.)
Px (a.u.)
Notes:   Regular trajectories for small amplitudes
  Resonant islands for larger amplitudes
  Chaos and particle loss for even larger amplitudes

## Slide 3: Motivation: Nonlinear Dynamics
Tunes depend on amplitude
Landau Damping increases with the spread of betatron oscillation frequencies. Larger tune spread –> beam more stable against collective instabilities.
  Can created by adding octupole magnets
If the system is integrable – no resonances
IOTA Goal: create practical nonlinear accelerator focusing systems with a large frequency spread and stable particle motion.
Notes:   McMillan (1967) – first successful 1-D example
  Perevedentsev, Danilov (1990 - 1995) – several 1D, 2D examples
  Cary etc (1994) – approximate integrability
  Danilov, Nagaitsev (2010) – practical 2D integrability

## Slide 4: Integrable Optics Test Accelerator
  Danilov, Nagaitsev, Phys. Rev. ST Accel. Beams 13, 084002 (2010)

## Slide 5: Need a Special Magnet
Can we do anything with just conventional magnets?
  Quadrupoles
  Octupoles
Cross-section and field lines

## Slide 6: Quasi-integrable optics
Octupole magnet strength ~ 1/β(s)3
Hamiltonian does not depend on s:
Questions:
  What about the 3rd degree of freedom?
  Imperfections
6D Simulations required
18 10cm-long octupole magnets
Chart: B3, G/cm3
s, m | 0.0001176 | 0.00018435 | 0.00029129 | 0.0004599 | 0.00071558 | 0.0010756 | 0.0015212 | 0.0019642 | 0.0022514 | 0.0022514 | 0.0019642 | 0.0015212 | 0.0010756 | 0.00071558 | 0.0004599 | 0.00029129 | 0.00018435 | 0.0001176
Chart: Beta, m
| -0.95 | -0.85 | -0.75 | -0.65 | -0.55000000000000004 | -0.45 | -0.35 | -0.25 | -0.15 | -0.05 | 0.05 | 0.15 | 0.25 | 0.35 | 0.45 | 0.55000000000000004 | 0.65 | 0.75 | 0.85 | 0.95
Beta, m | 2.0343 | 1.7589 | 1.5142 | 1.3 | 1.1165 | 0.96348 | 0.84109 | 0.74931 | 0.68812 | 0.65752 | 0.65752 | 0.68812 | 0.74931 | 0.84109 | 0.96348 | 1.1165 | 1.3 | 1.5142 | 1.7589 | 2.0343
Beta-function in NL magnet section
t = 0.4, c2 = 0.01 cm, l = 10 cm

## Slide 7: Frequency Map Analysis
Lifetrac code by D. Shatilov
  Tracking for ~103-104 turns
  FFT, find fundamental frequency
  Plot deviation
No deviation – sufficient but not necessary condition for particle stability
Model includes:
  Dipoles
  Dipole fringe fields
  Quadrupoles
  RF
  No sextupoles

## Slide 8: Frequency Map Analysis: 1 Section, Octupole Magnet
Tune spread: 0.03
Stable region: 2.5 x 2.5 mm

## Slide 9: Tracking
Hamiltonian is conserved
Motion is bounded

## Slide 10: Imperfections: stable region reduces insignificantly
No imperfections
Random error, σ = 0.1

## Slide 11: FMA: 1 Section, Quadrupole + Octupole
Tune spread: 0.05
Stable region: 2.5 x 1.8 mm

## Slide 12: Experimental Procedure
Two kickers, horizontal and vertical, place particles at arbitrary points in phase space
BPM measures beam position on every turn -> Poincare map:
As electrons lose energy due to synchrotron radiation in ~ 1sec or 107 turns, they will cover all available phase space
Do Fourier on ~ 1 ms, 104-turn-long samples –> betatron frequencies
Repeat
Study Qi(Ax, Ay) -> tune spread
Final goal – dependence of betatron frequency on amplitude

## Slide 13: Two Kickers Create an Arbitrary Kick in 2D
Horizontal + vertical stripline kickers
Rectangular pulses up to 25 kV ~ 100 ns duration.
Repetition rate < 1 Hz
Adjustable voltage 0 – Vmax
Fit inside quadrupole magnets to save space

## Slide 14: Beam Position Can Be Measured Precisely
20 horizontal and vertical BPMs
  Button type
  1 μm closed orbit resolution
  100 μm turn-by turn resolution
8 SR ports to measure beam size

## Slide 15: PCB-Based Octupole Magnet V. Vorobiev, PARTI-2013

## Slide 16: Sources of Error
Beta functions: 0.01 (relative)
Phase advance: 0.001
BPMs: 0.1 mm
Bunch transverse size: ~ 0.1 mm
Bunch length: 2 cm
FFT: ΔQ ~ 10-4
Energy loss during 1 ms sampling window
Errors in NL potential
Overall:

## Slide 17: Summary
It is possible to achieve tune spreads ~ 10-2 with just conventional magnet components and still retain large dynamic aperture
Search for optimal combination in terms of tune spread/size of dynamic aperture/complexity of the potential
Compare with full nonlinear potential
Next Steps

## Slide 18: Thank You for Your Attention