## Slide 1: Machine Learning and Accelerators: Neural Network Based Modeling and Control at ASTA
Auralee L. Morin
2nd Annual ASTA Users Meeting
9-10 June, 2014
CSU: Auralee Morin (Graduate Student), Sandra Biedron, Stephen Milton (Faculty)
Fermilab: Brian Chase, Pierpaolo Stabile, and many others
Notes: At the last Users meeting, I described a little bit about CSU’s interest in adaptive, machine-learning based control, and described what neural networks are, under what circumstances they are useful, and why accelerators are first of all, useful test-beds for nonlinear adaptive control techniques, but also are systems which could benefit significantly from the advancement of these Modeling and controls techniques. That presentation is online, so feel free to check it out. What I am going to do today is give you a peek at the model-building process we’ve used to generate a neural network plant model of the temperature regulation systems of the RF gun.

## Slide 2: Nonlinear Modeling Using Neural Networks
What are neural networks?
a neural network
a neuron (node)
Notes:   So, for those who aren’t familiar with neural networks in the context of nonlinear modeling, I’m just going to give you 30-second the highlight reel. Neural networks are nothing more than a linear combination of nonlinear activation functions. For nonlinear modeling, one can apply an optimization procedure to adjust the weights, biases, and (in some cases) activation function parameters such that an input-output mapping is generated

## Slide 3: Nonlinear Modeling Using Neural Networks
What are neural networks?
When are they useful?
  When there is a lot of available data
  When system dynamics are
      not well-known, or change over time
      not captured sufficiently well by analytic models
      are very complicated/time-consuming to model analytically (but could be in principle)
  When fast I-O is needed for a complicated model
a neural network
a neuron (node)
Notes:   So, for those who aren’t familiar with neural networks in the context of nonlinear Modeling, I’m just going to give you 30-second the highlight reel. Neural networks are nothing more than a linear combination of nonlinear activation functions. For nonlinear Modeling, one can apply an optimization procedure to adjust the weights, biases, and (in some cases) activation function parameters such that an input-output mapping is generated

## Slide 4: Nonlinear Modeling Using Neural Networks
What are neural networks?
When are they useful?
  When there is a lot of available data
  When system dynamics are
      not well-known, or change over time
      not captured sufficiently well by analytic models
      are very complicated/time-consuming to model analytically (but could be in principle)
  When fast I-O is needed for a complicated model
What are the disadvantages?
  Poor generalization
  Computationally intensive to train
  Long, iterative design procedure
  Good design requires substantial expert knowledge
a neural network
a neuron (node)

## Slide 5: Control Using Neural Networks
Two major classes of approaches
  NN model based
  Reinforcement learning/ adaptive critic

## Slide 6: Control Using Neural Networks
Two major classes of approaches
  NN model based
  Reinforcement learning/ adaptive critic
Where are they being pursued?
  Lots of interest in industrial process control
  Lots of academic papers on simple experiments, but still rarely used

## Slide 7: Control Using Neural Networks
Two major classes of approaches
  NN model based
  Reinforcement learning/ adaptive critic
Where are they being pursued?
  Lots of interest in industrial process control
  Lots of academic papers on simple experiments, but still rarely used
Major hurdles
  Achieving stability requires significant tradeoffs (and is usually not mathematically guaranteed)
  Adaptive NN-based control is computationally intensive
  Often, the most appealing solutions rely on controls techniques that have not yet reached maturity
  Lack of prior track record on complicated systems

## Slide 8: Control Using Neural Networks
Two major classes of approaches
  NN model based
  Reinforcement learning/ adaptive critic
Where are they being pursued?
  Lots of interest in industrial process control
  Lots of academic papers on simple experiments, but still rarely used
Major hurdles
  Achieving stability requires significant tradeoffs (and is usually not mathematically guaranteed)
  Adaptive NN-based control is computationally intensive
  Often, the most appealing solutions rely on controls techniques that have not yet reached maturity
  Lack of prior track record on complicated systems
So, why bother?

## Slide 9: Control Using Neural Networks
Two major classes of approaches
  NN model based
  Reinforcement learning/ adaptive critic
Where are they being pursued?
  Lots of interest in industrial process control
  Lots of academic papers on simple experiments, but still rarely used
Major hurdles
  Achieving stability requires significant tradeoffs (and is usually not mathematically guaranteed)
  Adaptive NN-based control is computationally intensive
  Often, the most appealing solutions rely on controls techniques that have not yet reached maturity
  Lack of prior track record on complicated systems
So, why bother?
 Starting to look promising for improving the control of complicated MIMO processes
 Not a panacea, but very useful when applied intelligently

## Slide 10: Initial Studies at ASTA
Start simple  NN temperature control of the RF gun
Figure courtesy P. Stabile
Notes: Want to get a comprehensive benchmark for how the model and controllers will perform
Want to look at both NN-only and NN-combined with traditional control approaches

## Slide 11: Model Design: What is Involved

## Slide 12: Model Design: What is Involved
Design training/validation/testing data

## Slide 13: Model Design: What is Involved
Design training/validation/testing data
Determine what input parameters to include

## Slide 14: Model Design: What is Involved
Design training/validation/testing data
Determine what input parameters to include
Determine what preprocessing is needed
  Standardization and scaling range (e.g. -1 to 1, -0.5 to 0.5)
  Dimensionality reduction (PCA, CCA), dead-time removal (if desired)

## Slide 15: Model Design: What is Involved
Design training/validation/testing data
Determine what input parameters to include
Determine what preprocessing is needed
  Standardization and scaling range (e.g. -1 to 1, -0.5 to 0.5)
  Dimensionality reduction (PCA, CCA), dead-time removal (if desired)
Determine which activation functions to use

## Slide 16: Model Design: What is Involved
Design training/validation/testing data
Determine what input parameters to include
Determine what preprocessing is needed
  Standardization and scaling range (e.g. -1 to 1, -0.5 to 0.5)
  Dimensionality reduction (PCA, CCA), dead-time removal (if desired)
Determine which activation functions to use
Determine an appropriate sampling rate for the inputs

## Slide 17: Model Design: What is Involved
Design training/validation/testing data
Determine what input parameters to include
Determine what preprocessing is needed
  Standardization and scaling range (e.g. -1 to 1, -0.5 to 0.5)
  Dimensionality reduction (PCA, CCA), dead-time removal (if desired)
Determine which activation functions to use
Determine an appropriate sampling rate for the inputs
Find the appropriate lag space

## Slide 18: Model Design: What is Involved
Design training/validation/testing data
Determine what input parameters to include
Determine what preprocessing is needed
  Standardization and scaling range (e.g. -1 to 1, -0.5 to 0.5)
  Dimensionality reduction (PCA, CCA), dead-time removal (if desired)
Determine which activation functions to use
Determine an appropriate sampling rate for the inputs
Find the appropriate lag space
Find an appropriate topology
  number of hidden layers
  number of nodes in each layer
  interconnections between nodes

## Slide 19: Model Design: What is Involved
Design training/validation/testing data
Determine what input parameters to include
Determine what preprocessing is needed
  Standardization and scaling range (e.g. -1 to 1, -0.5 to 0.5)
  Dimensionality reduction (PCA, CCA), dead-time removal (if desired)
Determine which activation functions to use
Determine an appropriate sampling rate for the inputs
Find the appropriate lag space
Find an appropriate topology
  number of hidden layers
  number of nodes in each layer
  interconnections between nodes
Determine which training algorithm to use (and parameters—objective function, learning rate, etc.)

## Slide 20: Model Design: What is Involved
Design training/validation/testing data
Determine what input parameters to include
Determine what preprocessing is needed
  Standardization and scaling range (e.g. -1 to 1, -0.5 to 0.5)
  Dimensionality reduction (PCA, CCA), dead-time removal (if desired)
Determine which activation functions to use
Determine an appropriate sampling rate for the inputs
Find the appropriate lag space
Find an appropriate topology
  number of hidden layers
  number of nodes in each layer
  interconnections between nodes
Determine which training algorithm to use (and parameters—objective function, learning rate, etc.)
Design an appropriate adaptation procedure, if applicable

## Slide 21: Model Design: What is Involved
Design training/validation/testing data
Determine what input parameters to include
Determine what preprocessing is needed
  Standardization and scaling range (e.g. -1 to 1, -0.5 to 0.5)
  Dimensionality reduction (PCA, CCA), dead-time removal (if desired)
Determine which activation functions to use
Determine an appropriate sampling rate for the inputs
Find the appropriate lag space
Find an appropriate topology
  number of hidden layers
  number of nodes in each layer
  interconnections between nodes
Determine which training algorithm to use (and parameters—objective function, learning rate, etc.)
Design an appropriate adaptation procedure, if applicable
 15-fold validation: especially important if re-training!

## Slide 22: Model Design: What is Involved
Design training/validation/testing data
Determine what input parameters to include
Determine what preprocessing is needed
  Standardization and scaling range (e.g. -1 to 1, -0.5 to 0.5)
  Dimensionality reduction (PCA, CCA), dead-time removal (if desired)
Determine which activation functions to use
Determine an appropriate sampling rate for the inputs
Find the appropriate lag space
Find an appropriate topology
  number of hidden layers
  number of nodes in each layer
  interconnections between nodes
Determine which training algorithm to use (and parameters—objective function, learning rate, etc.)
Design an appropriate adaptation procedure, if applicable
 15-fold validation: especially important if re-training!
 For a NN model to be useful in control, also need to keep real-time implementation in mind
  Speed of communication channels and actuators
  Speed of adaptation procedures, speed of NN I-O processing
  Data sampling rate vs. execution speed

## Slide 23: Model Design: What is Involved
Design training/validation/testing data
Determine what input parameters to include
Determine what preprocessing is needed
  Standardization and scaling range (e.g. -1 to 1, -0.5 to 0.5)
  Dimensionality reduction (PCA, CCA), dead-time removal (if desired)
Determine which activation functions to use
Determine an appropriate sampling rate for the inputs
Find the appropriate lag space
Find an appropriate topology
  number of hidden layers
  number of nodes in each layer
  interconnections between nodes
Determine which training algorithm to use (and parameters—objective function, learning rate, etc.)
Design an appropriate adaptation procedure, if applicable
 15-fold validation: especially important if re-training!
 For a NN model to be useful in control, also need to keep real-time implementation in mind
  Speed of communication channels and actuators
  Speed of adaptation procedures, speed of NN I-O processing
  Data sampling rate vs. execution speed
112 candidates x 15-fold validation  1680 NN to train

## Slide 24: Model Design: What is Involved
Design training/validation/testing data
Determine what input parameters to include
Determine what preprocessing is needed
  Standardization and scaling range (e.g. -1 to 1, -0.5 to 0.5)
  Dimensionality reduction (PCA, CCA), dead-time removal (if desired)
Determine which activation functions to use
Determine an appropriate sampling rate for the inputs
Find the appropriate lag space
Find an appropriate topology
  number of hidden layers
  number of nodes in each layer
  interconnections between nodes
Determine which training algorithm to use (and parameters—objective function, learning rate, etc.)
Design an appropriate adaptation procedure, if applicable
 15-fold validation: especially important if re-training!
 For a NN model to be useful in control, also need to keep real-time implementation in mind
  Speed of communication channels and actuators
  Speed of adaptation procedures, speed of NN I-O processing
  Data sampling rate vs. execution speed
112 candidates x 15-fold validation  1680 NN to train
40 minutes to train (on average)

## Slide 25: Model Design: What is Involved
Design training/validation/testing data
Determine what input parameters to include
Determine what preprocessing is needed
  Standardization and scaling range (e.g. -1 to 1, -0.5 to 0.5)
  Dimensionality reduction (PCA, CCA), dead-time removal (if desired)
Determine which activation functions to use
Determine an appropriate sampling rate for the inputs
Find the appropriate lag space
Find an appropriate topology
  number of hidden layers
  number of nodes in each layer
  interconnections between nodes
Determine which training algorithm to use (and parameters—objective function, learning rate, etc.)
Design an appropriate adaptation procedure, if applicable
 15-fold validation: especially important if re-training!
 For a NN model to be useful in control, also need to keep real-time implementation in mind
  Speed of communication channels and actuators
  Speed of adaptation procedures, speed of NN I-O processing
  Data sampling rate vs. execution speed
112 candidates x 15-fold validation  1680 NN to train
40 minutes to train (on average)
47 days

## Slide 26: Data Obtained for the Initial Model Design
~24 hours of data total

## Slide 27: Data Obtained for the Initial Model Design
~24 hours of data total
~14 hours of pseudo-random input (without regulation)

## Slide 28: Data Obtained for the Initial Model Design
~24 hours of data total
~14 hours of pseudo-random input (without regulation)
~5 hours with changing RF power to the gun (with regulation)  cavity conditioning

## Slide 29: Data Obtained for the Initial Model Design
~24 hours of data total
~14 hours of pseudo-random input (without regulation)
~5 hours with changing RF power to the gun (with regulation)  cavity conditioning
The rest is steady-state regulation with existing controller

## Slide 30: Closer View of Cavity Temperature
Time Steps [2 seconds each]
Cavity Temperature [°C ]

## Slide 31: Model Design: Input Parameter Selection
Choose parameters which make sense a priori
Get rid of redundant parameters
Where uncertain, investigate candidate models with 15-fold validation
Highly Correlated Parameters
Notes: Can also use PCA and CCA to reduce dimensionality, but this adds computation time and isn’t always accurate depending on the system
Here, we have few enough variables that we can avoid it

## Slide 32: Model Design: Input Parameter Selection
Chosen Parameters
  Flow Control Valve Setting
  Heater Setting
  LCW Temperature
  Cavity Temperature

## Slide 33: Model Design: Input Parameter Selection
Chosen Parameters
  Flow Control Valve Setting
  Heater Setting
  LCW Temperature
  Cavity Temperature
Other candidate models examined
  Adding return temperature as an input (with appropriate delay)
  Excluding previous cavity temperatures as an input
  Reducing the number of previous cavity temperatures used as input

## Slide 34: Model Design: Input Parameter Selection
Chosen Parameters
  Flow Control Valve Setting
  Heater Setting
  LCW Temperature
  Cavity Temperature
Other candidate models examined
  Adding return temperature as an input (with appropriate delay)
  Excluding previous cavity temperatures as an input
  Reducing the number of previous cavity temperatures used as input
  Did well, but not as well as the originally proposed model

## Slide 35: Initial Training, Validation, and Testing Data
With more challenging
test data to follow

## Slide 36: Model Design: Variable Dead-Time Removal
Measurements supply a starting point  but the delays vary
Empirical study with NN gives an optimal solution
25 candidates
15-fold validation
Refined Search
Rough Search
Time Removed [s]
Time Removed [s]
Root Mean Squared Error [°C ]
Notes: Large system dead-time, can remove this, but what is the most appropriate shift to use?
Lots of ways to estimate this a priori if needed, especially for linear systems
However, we have the advantage of being able to just take a look at the system empirically
Can then zero-in on the appropriate value by looking at the error index Note recursive process had found a good number of hidden layers to use, then did this study 60 seconds chosen better to have more information than less

## Slide 37: Model Design: Embedding Dimension
12 candidates
15-fold validation
Number of Previous Time Steps Used as Inputs (each time step is now 2 seconds)
Root Mean Squared Error [°C ]

## Slide 38: Number of Hidden Layers and Nodes
55 candidates for two-layer network
30 other candidates (not shown): recurrent, single-layer
Nodes in Hidden Layer 1
Root Mean Squared Error [°C ]
Nodes in Hidden Layer 2

## Slide 39: Performance Over Training and Validation Set
0.0094 RMSE validation set
0.0092 RMSE training set
Time Steps [2 seconds each]
Cavity Temperature [°C ]

## Slide 40: Testing Regions

## Slide 41: Testing Regions
Region 1: pseudo-random impulses

## Slide 42: Testing Regions
Region 1: pseudo-random impulses
Region 2: steady-state with regulation

## Slide 43: Testing Regions
Region 1: pseudo-random impulses
Region 2: steady-state with regulation
Region 3: cavity conditioning, slow change in RF power

## Slide 44: Testing Regions
Region 1: pseudo-random impulses
Region 2: steady-state with regulation
Region 3: cavity conditioning, slow change in RF power
Region 4: cavity conditioning, faster change in RF power

## Slide 45: Performance in Testing Region 1
Time Steps [2 seconds each]
Cavity Temperature [°C ]
0.0100 RMSE

## Slide 46: Performance in Testing Region 2
Time Steps [2 seconds each]
Cavity Temperature [°C ]
0.0096 RMSE

## Slide 47: Testing Regions 3 and 4
Changes to RF Power
RF Power
(N:PMTR9)
Notes: Note the 2nd image contains the 1st region also

## Slide 48: Performance on Testing Region 3
Time Steps [2 seconds each]
Cavity Temperature [°C ]
0.0156 RMSE

## Slide 49: Performance on Testing Region 4
Time Steps [2 seconds each]
Cavity Temperature [°C ]
0.0549 RMSE

## Slide 50: Performance on Testing Region 4
Time Steps [2 seconds each]
Cavity Temperature [°C ]
0.0549 RMSE

## Slide 51: Performance on Testing Region 4
Time Steps [2 seconds each]
Cavity Temperature [°C ]

## Slide 52: Performance on Testing Region 4 with Adaptation
Time Steps [2 seconds each]
Cavity Temperature [°C ]
0.0099 RMSE

## Slide 53: What about large changes and different operating regimes?

## Slide 54: What about large changes and different operating regimes?
Several options:
  Online adaptation
    Slow and potentially unstable for large, rapid changes
    Loss of previous learning

## Slide 55: What about large changes and different operating regimes?
Several options:
  Online adaptation
    Slow and potentially unstable for large, rapid changes
    Loss of previous learning
  Use RF power as an input and train across the operating regimes
    Would need a lot of data for many transition types  time intensive + likely not feasible to capture adequately
    Likely would need to a more cumbersome NN structure

## Slide 56: What about large changes and different operating regimes?
Several options:
  Online adaptation
    Slow and potentially unstable for large, rapid changes
    Loss of previous learning
  Use RF power as an input and train across the operating regimes
    Would need a lot of data for many transition types  time intensive + likely not feasible to capture adequately
    Likely would need to a more cumbersome NN structure
  Train several NNs with data gathered in different operating regimes
    Can switch models in control routines
    Can adapt online for small adjustments
    Many small models instead of one large, potentially problematic model

## Slide 57: Current and Next Steps
Fully characterize model performance under challenging conditions
  If the model won’t perform well, a model-based controller certainly won’t
  Need to test in real-time while doing I-O though ACNET
  Need to test different updating schemes
  Need to test regime-switching schemes
Improve implementation of control script in Matlab
  Real-time execution of NN, I-O with ACNET, optimization procedure, data preprocessing
  Several computationally intensive processes
   tested ACNET and NN I-O previously with a very limited direct inverse controller, but this did not involve any updating or optimization routines
Improve execution speed for Model Predictive Controller optimization
  Instantaneous linearization
  Different algorithm
Simulations of controller performance
Test controller output only
Test controller operation in training regime