## Slide 1: Protons in IOTA Ring
Eric Prebys, Fermilab APC

## Slide 2: Motivation
The primary motivation for nonlinear integrable optics is to reduce the sensitivity to harmonic instabilities and thereby enable stable beams with higher space charge or beam-beam tune shifts.
This cannot be directly measured with the electron beam.
  electron beam must be used as pencil beam to probe tune space.
Eventually, we can experiment with space charge compensation techniques (e-lens, etc)
DOE review recognized this as a high priority
  “…the high priority R&D goal for Fermilab is to develop the standalone IOTA ring, including its proton source. A revised cost estimate that includes these additional items [injection, instrumentation, experiments] should be provided…prior to finalizing a funding decision.”

## Slide 3: Where to get protons
Luckily, we have an extra RFQ just lying around…
The HINS (“High Intensity Neutrino Source”) was developed as the front end of a pulsed “Project X” 8 GeV proton linac
Because of cooling problems, it never reached its design pulse rate
ProjectX (now PIP-II) specification was changed to a CW front end
  HINS->PXIE
HINS RFQ available for our use

## Slide 4: RFQ Design and Specifications
Pulsed 4-vane RFQ:

## Slide 5: HINS Layout (During Operation)
Meson Hall
Spoke resonators will not be needed for acceleration (maybe debuncher)_

## Slide 6: Rate Limitation
HINS was designed to operate at a 1% duty factor
Large tune shifts were seen at the .1% level (~Hz x ~mA)
A design flaw caused water leaks at ~30 cooling channel couplings within the RFQ, such that vacuum could not be maintained
  -> No cooling
Increased temperature resulted in the observed tune shifts.
Bad for them, but no problem for us.
As the RFQ heats up, this flange bulges, causing a parasitic mode to mix and shift the resonant frequency

## Slide 7: HINS Parameters
matched to IOTA momentum, but β=.073!
Big. Will probably need debuncher (not yet costed)
Why no one will steal this RFQ from us

## Slide 8: Single Pulse Performance*
Aside from the rate problems, the RFQ met specifications:
Initial diagnostic configuration
V. Scarpine, et al
unnormalized emittance ~2 π-mm-mrad
Bunching efficiency

## Slide 9: Performance well modeled
TRACK*
*J-P Carniero

## Slide 10: Injection Plan
Proton injection will initially be done with a single turn, using the same kicker and lambertson as electron injection
  Sufficient Aperture
  Kicker pulse must be variable width
  Possible upgrade to ion injection later
Note: dipole supplies unipolar
  Must physically switch polarity to operate in proton mode!
Switch dipole:
OFF=electrons ON=protons

## Slide 11: Design Issues
Dispersion suppression (these quads not in current design)
Matching: no problems foreseen
May need to add debuncher to reduce energy spread

## Slide 12: Achromatic Dogleg
First pass with original (15°) injection line
Note: new design has shorter line/larger bend
  Might be challenging to make it achromatic

## Slide 13: Modified Injection
In the most recent version of the IOTA design, the injection angle has been increased, and the transfer line shortened
Still need to address this

## Slide 14: Taking stock of what we have and what we haven’t
A lot of miscellaneous hardware will be reused by the PXIE program
  A lot of stuff disappeared from the HINS hall between my first and second visit
  We believe we have an “understanding” now.
  PXIE might be finished before we need the stuff, but we’re not counting on that.
What we have
  Klystron and all supporting hardware
  Re-circulator, hybrid, other misc. RF hardware
  RFQ
  Proton source (sans 50 kV supply)
  Support girder
  quads (assuming we can borrow them again
What we haven’t
  50 kV supply for proton source
  Vacuum lines and pumps (picked clean by vultures)
  Coax from upstream gallery to RFQ

## Slide 15: Challenge: RFQs need lots of stuff
Not shown: charging supply (big). Where can we put this stuff?
R. Webber

## Slide 16: Location of RFQ Supply Hardware
Original (bad) idea: Put all the hardware inside the IOTA ring
Might be able to make it work, but lots of problems
  Interference with magnet power supplies
  Placement and access
  etc.
Luckily, the elimination of the second two cryomodules leaves room in the upstream ASTA gallery…

## Slide 17: New Layout
Put all high power RF hardware in the upstream gallery and run coax to the RFQ itself
Planning to move equipment from the HINS test area, but may be able to reduce cost by
  Using the unused charging supply->pulse transformer chain for CM 2 and 3
  Using extra 325 MHz klystron currently in storage
source, RFQ and injection girder
Charging supply,modulator, pulse transformer, and klystron

## Slide 18: Cost Estimate
As requested at the last review
  Assume installation over two years
Item | unit cost | FY16 qty | FY17 Qty | FY16 total | FY17 total | Total
3" coax | $50 | 200 |  | 10,000 | 0 | 10,000
3" hardware |  |  |  | 2,500 | 0 | 2,500
heliac | 3 | 600 |  | 1,800 | 0 | 1,800
heliac hardware |  |  |  | 180 | 0 | 180
50 kV ion system | 79000 |  | 1 | 0 | 79,000 | 79,000
RFQ vacuum | 200000 | 1 |  | 200,000 | 0 | 200,000
misc. vacuum | 50000 |  | 1 | 0 | 50,000 | 50,000
Hydrogen system | 20000 |  | 1 | 0 | 20,000 | 20,000
Misc. cabling | 150000 | 0.5 | 0.5 | 75,000 | 75,000 | 150,000
controls/interlocks | 20000 | 0.5 | 0.5 | 10,000 | 10,000 | 20,000
Installation costs | 100000 | 0.5 | 0.5 | 50,000 | 50,000 | 100,000
T&M Electrical | 100000 | 0.5 | 0.5 | 50,000 | 50,000 | 100,000
T&M piping | 50000 | 0.5 | 0.5 | 25,000 | 25,000 | 50,000
 |  |  |  | 424,480 | 359,000 | 783,480
 |  |  | 23.5% overhead | 99,753 | 84,365 | 184,118
 |  |  |  | 524,233 | 443,365 | 967,598
Contingency |  |  |  | 157,270 | 133,010 | 290,279
Total: |  |  |  | 681,503 | 576,375 | 1,257,877

## Slide 19: Possible Future Upgrade: H- injection
Install a stripping foil in the 30° bend?
Still investigating bump configuration
Not currently scoped.

## Slide 20: To Do
Model proton beam in IOTA ring
Integrate proton transfer line design into overall injection design
Finalize details regarding which hardware will be used.
  Move HINS klystron support gear or use extras for 1.3 GHz?
  Move klystron or use spare?