## Slide 1: Fabrication of Remaining Components
Allan DeMello
Lawrence Berkeley National Laboratory
MICE RF Workshop
Fermilab
June 2, 2014

## Slide 2
Fabrication RF Vacuum Vessel Assembly
Vacuum Vessel
  2 vacuum vessel segments with ports
  1 central sleeve
  2 Vacuum manifolds
  8 RF coupler spools
  2 Hyspan module to module bellows
Support Structure
  Structural stainless steel rectangular tube weldment
Gussets
  16 gussets used to fix the vacuum vessel to the coupling coil
    Waterjet from stainless plate

## Slide 3
The RF Vacuum Vessel
  We have some experience with the fabrication of the single cavity vacuum vessel
  MICE vacuum vessel with be challenging to integrate with the coupling coil magnet
Notes: 3

## Slide 4
RFCC Support Stand
  Stainless steel weldment
  We have some experience with the fabrication of the single cavity vacuum vessel stand
Notes: 4

## Slide 5
Fabrication of Cavity Components
  9 cavities available at LBNL (two styles)
  Cavity work still needed
    Measure frequency of all cavities
    Determine most common frequency
    Plastically deform some cavities too match frequency
    Machine stiffener ring of cavity to center on RF ports
    Electro-polish inside surface
Cavities components needed
  Tuner arms – 24 available at Mississippi
    Final machining of mounting pads needed
  24 actuators needed
    All machined parts needed
    All bellows available at Mississippi
  8 couplers needed
    8 RF windows available at LBNL
  24 aluminum-bronze struts needed
  8 Proportion Air pneumatic controllers needed
  8 Be windows available at LBNL

## Slide 6
RF Couplers
  2 couplers fabricated at LBNL for MTA cavity
  Drawings are updated to reflect the “as built” coupler
  8 RF couplers needed
  8 RF windows available at LBNL

## Slide 7
RF Tuner Arms
  24 tuner arms are available from Mississippi
  Final machining of the mounting pad needed

## Slide 8
RF Tuner Actuator
  6 actuators fabricated at LBNL for MTA cavity
  Updated drawings are complete to reflect the “as built” actuator
  24 actuator needed
  8 Proportion Air pneumatic control valves needed

## Slide 9
RF Tuner Actuator
  Actuator insertion problem
  Trimming end of shaft to solve

## Slide 10
Cooling Circuit Assembly
    Finalize cooling tube connection design
    Change feedthru flange to a rotatable
    Assemble components onto cavities
    Extra tube on cavity may need extension

## Slide 11
Cavity Suspension Struts
    Strut material re-designed from stainless steel coated with dry lubricant to aluminum bronze
    24 struts needed
    All rod ends and jam nuts available at LBNL