## Slide 1: Study on Magnesium Diboride SC Links for HiLumi-LHC Workshop on Radiation Effects in Superconducting Magnets and Materials 2015 (RESMM'15)
A. Bignami, F. Broggi, C. Santini
RESMM’15 East Lansing May 12th 2015

## Slide 2
LASA Laboratorio Acceleratori Superconduttività Applicata
Andrea.Bignami@mi.infn.it
RESMM’15 East Lansing May 12th 2015
Andrea Bignami

## Slide 3: Outline
HiLumi-LHC
WP 6 Cold Powering
Point 7 (P7) Studies Approach
Point 1 (IP1) “ “
Simulations and Results
Data Analysis and Conclusions

## Slide 4
Previous Experiences on Magnet Energy Deposition (I)
Study of a new Nb3Sn design for the LHC insertion quad started in 1995, suggested by the Milan group (L.Rossi)
Ended in 1998
(1999 final report)

## Slide 5
Previous Experiences on Magnet Energy Deposition (II)
NED (EU) - Candia (INFN); EUCARD – HHH
Study of the LHC Phase II upgrade
AMTW Accelerator Magnet Technology Workshop on beam generated heat deposition and quench levels in LHC magnet, CERN, March 2005
3rd CARE-HHH-APD Workshop LHC-LUMI-06
‘Towards a Roadmap for the Upgrade of the CERN & GSI Accelerator Complex’
IFIC, Valencia, Spain – 16-20 October 2006
CARE-HHH-APD Mini-Workshop IR'07 Frascati, November 2007

## Slide 6
Previous Experiences on Magnet Energy Deposition (III)
After the LHC accident there was a stop in the upgrade studies
Start again with the SIT (Superconducting Irradiation Test) because of lacking on informations and data on radiation effects on the magnet material Nb3Sn
Ti5
Nb3Sn cable
SimpleGeo Plot

## Slide 7: Hi-Lumi-LHC Project

## Slide 8
Task 1
Coordination
CERN/INFN
Task 2
Cryogenics
CERN
Task 3
Electr. Transf.
Cryostat
Univ. South
Task 4
Energy Dep.
Material
INFN
CERN activity
Integration
Civil engineering
Interfaces
(mech, vacuum, electr)
Vacuum
SC cables/SC link
Cryostat of SC link
Current leads
Protection
CERN activity
Prototypes construction
Cryostat
- Prototypes test
- System design
- Series specification
- Series construction
- Integration
- Operation
Fluka team
WP6 Structure (Coordinator A. Ballarino (CERN),
Deputy coordinator F. Broggi (INFN))
“Cold Powering”

## Slide 9
Cold Powering via Superconducting Links
Advantages of remote powering:
Safer long-term operation of powering equipment (power converters, current leads and associate auxiliary devices) located in a radiation-free environment;
Safer access of personnel to equipment for maintenance, repair, diagnostic and routine tests interventions;
Reduced time of interventions on power converters, current leads and DFBs if the powering equipment is located outside of the tunnel areas – gain in machine availability ;
- Free space in the beam areas which becomes available for other equipment.
Courtesy of Amalia Ballarino
2nd Joint HiLumi LHC-LARP Annual Meeting
Frascati 14-16 November 2012

## Slide 10: Real Link
ext  65 mm
18 MgB2 wires
 = 6.5 mm
Cu
MgB2 ,  = 0.85 mm
Cable layout
6x20kA , 7x3kA, 4x0.4kA, 8x.12kA
Courtesy A. Ballarino
This implementation of the cable is the one used in all the simulations.
Fluka Model

## Slide 14: P7 Dose
The maximum dose is about 40 kGy integrated over a period of 30 fb-1
If also we extrapolate proportionaly to 3000 fb-1 we will obtain only 4 MGy over the whole period of exercise

## Slide 15: P7 Dpa
The dpa is about 10-7 over all the cable. This value give us no concern, because it is almost 1 order of magnitude smaller than the one in IP1

## Slide 17: Connection Module IP1
Aside the Beam Pipe, near the D1, has been implemented the Connection Module (CM), in which are simulated the Horizontal (SCL-H) and the Vertical (SCL-V) that will be connected with the magnets power supplier.

## Slide 18: Powering Scheme and Links Layout
For this configuration the link coming from the surface will arrive just after D1 (at about 80 m from IP) and will run aside the quads

## Slide 19: New Beam Screen IP1
For this simulation has been used a new version of the Beam Screen, with major shelding at 45 degrees, in order to protect the components from the debries that follows the focusing-defocusing path.

## Slide 20: IP1 Dose
The maximum dose in the cable, normalized to 3000 fb-1, is about 0.1 MGy, a value that does not represent a concern for the normal operations.

## Slide 21: IP1 Dpa
The maximum dpa in the horizontal cable, still normalized to 3000 fb-1, is about 10-6, also in this case a value that does not represent a concern for the normal operations.
The values for the vertical cable are about the same.

## Slide 22: Conclusions
The dose value in the links will not be a concern for the normal operation of the machine over a work time of 3000 fb-1
Also the DPA value should not represent an issue.

## Slide 23: What’s Next
Simulations for Point 5 It can be guessed a similar situation

## Slide 24: Acknowledgment
Thank You for Your attention
F.Cerutti , L.S. Esposito, E.Skordis
(CERN FLUKA Team)