## Slide 1: Status of the FRIB Fragment Separator Superconducting Magnets
Earle Burkhardt FRIB Magnet Systems Department Manager

## Slide 2: Outline
Overview
  Current construction status
  LINAC layout
Fragment separator layout
  Superconducting magnets in high radiation environment
Target facility
Magnet design
Change from HTS to LTS for dipoles in hot cell

## Slide 3: Team
Team members from the FRIB Experimental Systems Division
  Georg Bollen
  Tom Borden
  Dan Cole
  Shailendra Chouhan
  Rick Swanson
  Reg Ronningen
  Dali Georgobiani
  Earle Burkhardt

## Slide 4: FRIB - Facility for Rare Isotope Beams at Michigan State University
Rare isotope production via in-flight technique with primary beams up to 400 kW, 200 MeV/u uranium
Fast, stopped and reaccelerated beam capability
Upgrade options
  Energy 400 MeV/u for uranium
  Isotope separation on-line
    Multi-user capability
World-leading next-generation rare isotope beam facility

## Slide 5: FRIB Beams Will Enable New Discoveries
Available today
New territory to be explored with FRIB
about 3000 known isotopes

## Slide 6: Conventional Facilities Site Layout

## Slide 7: FRIB Construction Progress [1]
Structural steel erection for surface building underway
Backfill: 46,178 tons = 65% complete
Resteel: 1,799/2,800 tons = 64%
Concrete: 24,468/43,000 yards = 53%
Caissons have been completed
Ongoing installation of hangers and piping in linac tunnel
Forming and placing resteel for the west wall of the hot cell
Performing work on tunnel exhaust shaft
Placing resteel for hot cell wall
Newly painted linac tunnel
View of target area from northeast

## Slide 8: FRIB Construction Progress [2] FRIB Concrete as of 29 April 2015
= Tunnel slabs poured
= Tunnel walls poured
= Tunnel lid poured
= Backfilled to grade

## Slide 9: FRIB Driver Accelerator Layout

## Slide 10: Fragment Separator
Scope
  In-flight separation of rare isotopes with high acceptance and high resolution
    Leverage rare isotope production at 400 kW beam power
    Provide purest-possible rare isotopes beam to maximize science reach
Technical specifications
  High-acceptance preseparator provides first beam purification step, provides defined location(s) for primary beam dump
  2 additional separation stages to guarantee high beam purity
  Provide future upgrade opportunities for isotope harvesting

## Slide 11: Fragment Separator Magnets
New designs for cold iron quadrupoles and dipoles
Known technology
Low risk
Highest radiation environment
Life-of-facility concerns
High radiation heat loads
Front end of pre-separator
Vertical section
Existing NSCL A1900 magnets reconfigured
B2-Georgobiani

## Slide 12: Fragment Separator Mechanical Design
All components in high radiation area in vacuum vessels (~200 t)
Target
Resistive octupole
SC dipoles
Beam dump
North hot cell wall
Steel shield blocks
Beamline from linac
5m
Wedge assembly
Metal shield
RT quadrupole
Room temperature Multipole
Target
vacuum vessel
Beam dump
vacuum vessel
Wedge
vacuum vessel
SC quadrupoles
SC quadrupoles

## Slide 13: Target Facility Design
End of beam delivery system
Fragments

## Slide 14: Target Facility Design Interior Layout
Waste Handling Hatch
Target Facility Magnet Power Supplies
Access control from NSCL building
Hot Cell
Labyrinth to Beam Line
High Bay Loading Dock
Access control from loading dock

## Slide 15: Target Facility Hot Cell
The system will maintain activated preseparator beam line components located in the hot cell and manage activated waste
Hands on access with beam off and shielding in place
Remote operations with shielding removed or beam on
Magnets designed with remote handling capabilities
  Serviced in this hot cell
20 ton crane
Bottom loading port
(access to waste handling gallery)
Window workstation
Vision system
In-cell tooling
Temporary waste storage
RH equipment lift
Hot cell lighting
Utility embeds

## Slide 16: Fragment Separator Magnet Design
Meshed 3D model of FSQ9
Full 3D TOSCA model for detailed optimization
  Detailed flux distribution, forces, quench analysis
Example: quadrupole FSQ9
  Field gradient exceeds requirement by 12%
  Effective length within 5% of goal
  Integrated strength exceeds requirement

## Slide 17: Fragment Separator Magnet Design Magnet Field Quality Example: FSQ9
3D model shows pure quadrupole field at 0.1% level
  Simulated field quality exceeds requirements
  Similar, but longer magnet FSQ10 has even better field quality
 | FSQ9 (center, R = 12 cm) |  | FSQ9 (integrated, R = 12 cm) | 
Order | Amplitude | Relative Amp.[%] | Amplitude | Relative Amp.[%]
2 | -11432.5 | 100 | -712519 | 100
6 | -12.2 | 0.1 | -345 | 0.05
10 | -6.9 | 0.06 | -29 | 0.004
14 | -4.4 | 0.04 | 7.1 | -0.001
18 | -3.1 | 0.03 | 24 | -0.003
Harmonic analysis results for FSQ9
Relative strength of FSQ9 higher order harmonics (center and integrated)

## Slide 18: Warm iron quad (half)
Connection box
Link
Yoke key
Quad Coil
Support
Multipole coils

## Slide 19: Warm Iron Quad

## Slide 20: Warm Iron FRIB Quadrupole Features
Liquid Helium Supply Port
Electrical Leads &
Helium Return
Support Links
MSU SC Magnet
Coil Backbone Support
Support Links Limited to 10 W Heat Load Total
Warm iron quadrupole coils are not supported by the yoke iron like the cold iron quad design
  Coils need a support structure to deal with coil forces of up to 40,000 kgf/linear m

## Slide 21: Detailed Magnet Models for Simulations Basis for Reliable Prediction of Radiation Effects
Power deposition in magnet structures drives the detailed design of magnet components, non-conventional utilities, cooling water loops, cryogenic requirements
Continuous improvements of target, beam dump, and wedge vacuum vessel models that contain updated magnet components (geometry, dimensions, materials, structures)
catcher
slits
wedge
collimator
Beam dump 2
shield
Q_D1137
Q_D1147
Q_D1158
Q_D1170
magnet supports
Wedge vacuum vessel

## Slide 22: Calculations of Radiation Power Deposition
Power deposition in shielding drives detailed shielding design, such as concrete placement near the vacuum vessels
Power deposition in magnet yokes and coils drives the detailed design of magnet components, non-conventional utilities, cooling water loops
Radiation power
deposition from
Ca-48 beam at
239.5 MeV/u
(baseline energy)

## Slide 23: Calculations of Radiation Power Deposition
Power deposition drives detailed vacuum vessel and external shielding design
  Power deposition maps are used as a diagnostic tool to make sure there is no excessive heating
Radiation power deposition from 48Ca beam at 549 MeV/u (upgrade energy)

## Slide 24: Magnet Thermal Shield Power Deposition Study Supports Cryogenics Detailed Design
40 K thermal shield power deposition information also provided to the magnet designers and engineers for improvements towards detailed magnet shield cooling design and shield optimization
Calculated heat loads become requirements for the cryogenic system
Beam (at 400 kW) | 48Ca, 240 MeV/u | 48Ca, 549 MeV/u
Magnet | Deposited power, W | 
Q_D1024 | 12.7 | 120
Q_D1035 | 200 | 325
Power deposition in the target vacuum
vessel magnet 40 K thermal shields
Power deposition in the front (a) and back (b) parts of Q_D1035 thermal shield
a
b

## Slide 25: Magnet Yoke Power Deposition Study Supports Cooling Loop Design
Cooling will be provided to all magnet yokes in the hot cell
Cooling may not be required for some magnet yokes
Detailed heat load information is used to design water cooling loops
Detailed heat load information also provided to the magnet designers and engineers for improvements towards final magnet designs
Beam (at 400 kW) | 48Ca, 240 MeV/u | 48Ca, 549 MeV/u
Magnet | Deposited power, W | 
Q_D1013 | 60 | 330
Q_D1024 | 0.4 | 3
Q_D1035 | 4 | 50
S_D1045 | 550 | 7420
Power deposition in the target vacuum vessel magnet yokes
    This analysis has been published in T40204-CA-000104 “Radiation Energy Deposition in Preseparator Magnets and Lifetime Estimates”; the numbers presented here are updated due to latest model changes reflecting design details
First 3 quads and resistive multipole

## Slide 26: Magnet Yoke Power Deposition Study Determines Cooling Loop Design
Power deposition is highest after the beam dump
Cooling is required for most magnet yokes
Detailed heat load information is used to design water cooling loops
Detailed heat load information also provided to the magnet designers and engineers for improvements towards detailed magnet designs
Beam (at 400 kW) | O-18 | Ca-48
Energy, MeV/u | 637 | 239.5
Magnet | Deposited power, kW | 
Q_D1013 | 0.80 | 0.11
Q_D1024 | 0.30 | 0.04
Q_D1035 | 0.32 | 0.04
S_D1045 | 1.60 | 0.11
DV_D1064 | 1.84 | 0.19
S_D1092 | 16.2 | 3.20
DV_D1108 | 11.8 | 2.50
Q_D1137 | 1.54 | 7E-3
Q_D1147 | 0.08 | 2E-3
Q_D1158 | 0.03 | 8E-4
Q_D1170 | 0.02 | 5E-4
before beam dump
after beam dump

## Slide 27: Fragment Separator Remote-Handling Equipment
Technical design/specification of equipment to be procured complete, procurements released
  Master slave manipulators
    Wall tubes, shield plugs and manipulators delivered
  Shield windows
    Windows and liners have been delivered, shield plugs also delivered
  20-ton crane ordered
Remote tooling/handling design follows component design
  Tooling design for Superconducting (SC) quadrupoles and dipole magnets substantially complete and reviewed
Cold-test facility operational
  Making use of master slave manipulators for design and procedure validation

## Slide 28: Change from HTS to RT and LTS Technology Reduce Cost and Risk, Increase Performance
Main motivation for HTS was high radiation on coils
  Life-of-facility coils attractive feature
  No heat load at 4.5 K
HTS quad R&D at BNL very successful
  However, complexity of using prototype as final magnet greater than anticipated
Initial estimation of cost of HTS tape for 30° dipoles was too low
  Expectation was for cost to decrease and performance to increase
  Initial design operated close to critical current (Ic); however improvement in Ic less than expected
  In order to maintain safe critical current margin, cost of HTS tape increased significantly
Necessary quench protection still in early stage of development for dipole magnet
  BNL plan to use quadrupole quench protection for HTS dipoles may not be viable because of larger inductance
  Significant development needed to prove effectiveness of quench protection system
    Would need large inductance magnet in order to test this

## Slide 29: Change from HTS to RT for FSQ1 RT Has Low Risk
Initially, room-temperature design was considered
  Relatively low-field  RT magnet a viable option
    RT option not possible for other quadrupoles
  2D design complete and meets requirements
    Better field quality than current HTS prototype magnet
  Water cooling loop in target vessel has enough spare capacity
Design approach
  Copper conductor with metal oxide insulation
RT quad could be built outside
In the long term, HTS is the most attractive option

## Slide 30: Planned Change from HTS to LTS for 30° Dipole LTS is Suitable Technology
LTS coils provide adequate lifetime for operation in radiation environment
  Possible if moving coils back 5 cm into yoke
    Significant reduction in radiation
    Cyanate ester epoxy provides at least decade long lifetime (assuming worst-case beam)
    Aluminized Kapton as radiation resistant MLI
Additional LTS advantages
  Very established technology, similar to magnets already fabricated in house
  Fast charging ramp-rate makes beam tuning more efficient
Original coil location
New coil location
d
d+10cm
Pole tips
Coils

## Slide 31: Radiation Transport Analyzed to Determine Life-time of Magnets
Heat map of zone close to Target
Hot Cell Dose Rates

## Slide 32: Planned Change from HTS to LTS for 30° Dipole Cryogenic Performance is not an Issue
Heat loads at 4.5 K greatly reduced
  Worst-case beam (16O 294.4 MeV/u)
    Original: ~250 W per dipole (500 W total)
    New: ~81 W per dipole (162 W total)
  Cryogenic plant capacity can handle the additional 4.5 K heat loads
Worst case for coil lifetime
  Original: 5 years
  New: 12 years
  Manageable, and could still replace LTS dipoles with HTS in the future
Original coil location
New coil location
Summary of FRIB Cryogenic Heat Loads T30200-TD-000244
Additional 100W
  Worst-case for 30° dipoles will increase neutron heating on 4.5 K stage, but decrease heating on 38 K stage
  Overall cooling is manageable
  A1900 on existing refrigeration system
Estimates for worst-case beam

## Slide 33: Change from HTS to LTS for 30° Dipole Other Issues Addressed
Magnetostatic design
  Field uniformity
    Pole tip profile remains essentially unchanged  very little impact
  Operating current – LTS will meet requirements after moving coils out 5 cm
    Amp-turns will need to increase slightly, but NbTi @ 4.5 K has much better critical current density (Jc) than HTS tape @ 38 K
Remote handling concept for removal of cryostat-pole tip package unchanged
  20 ton maximum weight limit not exceeded
    HTS design
      cryostat + pole tips  7.4 tons; keystone  9.0 tons
    LTS design estimate
      cryostat + pole tips  9.0 tons; keystone  10.1 tons

## Slide 34: Schedule
Winding 4 focusing solenoids in house
CIQTs and warm iron quads will be assembled in parallel paths
  CIQTs
    Winding of multipole coils has begun
    CIQT4 is first followed by CIQT1 ~6 weeks later
  Warm iron quads
    FSQ5a and FSQ5b will be assembled at same time
  Dipoles are last magnets to be assembled
    Fabrication scheduled to begin December 2016

## Slide 35: Summary
Magnets in the hot cell
  Highest radiation environment
Magnet designs mostly complete
HTSLTS change still being finalized
  Dipole design being optimized
  Transition to HTS coils in future upgrades