## Slide 1: Nonlinear Dynamics with Space-Charge in a Small Electron Recirculator
Santiago Bernal on behalf of UMER group,
IREAP, University of Maryland, College Park, MD
IREAP
AAC14, San José, CA, July 16th, 2014
Work Supported by the U.S. Department of Energy

## Slide 2
OUTLINE
UMER LAYOUT AND PARAMETERS
TRANSVERSE DYNAMICS:
  Betatron Resonances with low and high current
  Envelope-Mode Excitation with quadrupole kicker
  Halo (DMA diagnostics) and Envelope Matching
  Nonlinear, IOTA-like Optics with space charge
LONGITUDINAL DYNAMICS:
  Longitudinal Focusing extended to high current
  Solitons observed/simulated
  Multi-Stream Instability observed/simulated

## Slide 3
University of MD Electron Ring (UMER)
IREAP

## Slide 4
University of Maryland Electron Ring (UMER):
Research on Space-Charge Dominated Beams with Applications to
Intensity-Frontier Advanced Accelerators
Energy:  10 keV, b = 0.20
Current, I:  100 mA
Emittance*, ε:  3.0 m
Lattice period, S: 0.32, 0.64, 1.28 m
Zero-current l0: ≈ 1.8, 3.6, 7.2 m
Av. beam radius, a:  10 mm
Pulse length: 25-100 ns
Lap time: 197 ns
*norm., rms
Q
Q
Q
Q
D
D
WCM
Ind. Mod.

## Slide 5
5
BEAM PARAMETERS (all @ 10 keV)
 | 0.6 mA | 6.0 mA | 60 mA*
en,rms [mm] | 0.4 | 1.3 | 0.16
aave [mm] | 1.6 | 3.4 | 1.0
n/no | 0.85 | 0.62 | 0.96
Dncoh. | 0.005 | 0.05 | 0.00
Dnincoh. | 0.94 | 2.4 | 0.25
Tune nox= noy= 6.6, std. lattice; Vacuum Pipe Radius = 25.4 mm
Additional beam currents: 21, 78 and 104 mA
*Similar results for alternative lattice if nox= noy= 4.2
Notes: The main parameters for beam transport appear in blue.

## Slide 6: TRANSVERSE DYNAMICS

## Slide 7
BETATRON RESONANCES AND BEAM CURRENT*:
0.6 mA beam behaves more coherently than 6.0 mA
*S. Bernal et al, Proc. NA-PAC 2013, Pasadena, CA, Sep. 2013
Transmitted peak beam current
at 10th Turn vs. Bare Tunes:
6.0 mA
Measured vs. Calculated (ELEGANT) Tunes
Calculated (ELEGANT) Beam Envelope with space charge

## Slide 8
ENVELOPE RESONANCE EXCITATION
(W. D. Stem et al, IPAC 2013 and N-PAC 2013)
Transv. Envelope OFF (quadrupole) resonance, NEAR resonance and ON resonance (WARP code results)
Norm. Mode Freq. vs. Tune Depression
(WARP and theory)
6.0 mA
21 mA
Tune Depression
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1.0
0.0
1.0
1.5
2.0
Norm. Frequency, w/w0
6
Electrostatic
Quadrupole
Phase advances of breathing (even) and quadrupole (odd) envelope modes:
Can resonantly excite envelope modes with fast electrostatic quadrupole.
Frequency split depends on tune depression s/s0 , which depends on beam energy, current and emittance.

## Slide 9
x
y
32mm
Halo study using high dynamic range diagnostics
[H. D. Zhang et al, Phys. Rev. ST Accel. Beams 15, 072803 (2012)]
Micro-mirror
architecture
120
Line plot of sequential images with different mask sizes
Mask sizes
Mask: block by DMD
Screen edge
Achieve dynamic range up to 10-5
mismatched 6mA beam
Notes: The red line represent the , even in log scale, the fluctuation is big, only after applying the mask and retaking the picture, the fluctuation shrink, and we can see here a dynamic range of 105 can be achieved. This is a reconstructed picture showed a full dynamic range in log scale.
with smoothing and background subtraction

## Slide 10
Halo Formation from Mismatch
(H. D. Zhang, B. L. Beaudoin, and R. A. Kishek, N-PAC 2013)

## Slide 11
NONLINEAR OPTICS AT UMER: Studies of IOTA-like Optics + Sp. Charge
(See plenary talk by Sergei Nagaitsev, and WG7 talk by Kiersten Ruisard tomorrow)
*
W
Beta Functions in Modified UMER Alternative Lattice (ELEGANT)
(Courtesy of Kiersten Ruisard)
*
L
UMER Alternative Lattice
Generally, nonlinear systems are more stable than linear ones.
Nonlinear focusing leads to amplitude-dependent tunes (tune spread) and nonlinear decoherence*.
Nonlinear decoherence helps mitigate resonances and halo formation. Effect similar to Landau damping.
Role of space charge?
*S. D. Webb et al, to be published.

## Slide 12: LONGITUDINAL DYNAMICS

## Slide 13: UMER Design Performance Exceeded by a Factor of 10 at Low Current But High Inj. Sp. Charge Tune Shift (0.9)
13
Cell On (140 V)
46th Turn
Cell Off (0 V)
LONGITUDINAL
FOCUSING
0.6 mA, 10 keV
Signal from wall-current monitor at RC10
Notes: 13
highest space charge circulated in a ring! 100 turns design criterion

## Slide 14: Barrier Bucket Focusing of 0.55mA Beam
Courtesy of Brian Beaudoin

## Slide 15: First Experimental Observation of Soliton Wave Trains in Electron Beams
Nonlinear steepening balances wave dispersion
Persistent large-amplitude waves that retain their shape
J. Charles T. Thangaraj, Ph.D. Thesis, (2009) and
Y. C. Mo et al, Phys. Rev. Lett. 110, 084802 (2013)
Evolution of Large-Amplitude Perturbation
Turn 1
Turn 2
Turn 3
Turn 8
Notes: 15
Originally studied by John Scott Russell (1800s) for interest of design of ship hulls

## Slide 16: Observation of a Multi-Stream Instability
No longitudinal focusing – Beam expands and wraps around ring
Beam becomes “DC”
Onset of instability
sonset = 952.7m
turnsonset = 82.7
B.L. Beaudoin, et al, IPAC 2013
6 mA beam
h = 0.5
Experimental
<cs
Phase Space
11.52
0

## Slide 17: Comparison between Theory, Simulation and Experiment
h = fill factor = injected pulse length / ring lap-time
Experiment
Simulation (WARP)
Theory
Onset of Instability
L0

## Slide 18
SUMMARY/CONCLUSIONS
UMER is a compact, flexible machine for research and training in intensity-frontier beam physics.
We are studying the centroid and collective transverse
dynamics of both emittance and space-charge dominated beams: betatron resonances, envelope mode excitation, and halos.
IOTA-like nonlinear focusing in UMER is being studied
for low and high space-charge intensities (ELEGANT and
WARP codes).
Research on longitudinal dynamics in UMER has revealed important results on bunch containment and space charge waves including soliton wave trains and multi-stream instability.
Notes: The red line represent the , even in log scale, the fluctuation is big, only after applying the mask and retaking the picture, the fluctuation shrink, and we can see here a dynamic range of 105 can be achieved. This is a reconstructed picture showed a full dynamic range in log scale.
with smoothing and background subtraction