## Slide 1: Quasi-Integrable Optics Experiment at IOTA
Sergey A. Antipov, The University of Chicago
Sergei Nagaitsev, Alexander Valishev, FNAL

## Slide 2: Motivation: linear dynamics
Linear focusing lattice – betatron tunes of different particles are almost equal
In ideal case, particle motion is unconditionally stable
Phase space trajectories of perfectly linear 1D motion in normalized coordinates
Notes:   Regular trajectories for small amplitudes
  Resonant islands for larger amplitudes
  Chaos and particle loss for even larger amplitudes

## Slide 3: Motivation: linear dynamics
Linear focusing lattice – betatron tunes of different particles are almost equal
  Nonlinearities (both magnet imperfections and specially introduced) make single particle motion unstable due to resonances
  Hamiltonian depends on time
  Stability depends on initial conditions
Phase space of 1D motion in linear lattice with 1 octupole nonlinearity
Resonance aisles
Chaotic motion
Particles lost
X (a.u.)
Px (a.u.)
Notes:   Regular trajectories for small amplitudes
  Resonant islands for larger amplitudes
  Chaos and particle loss for even larger amplitudes

## Slide 4: Motivation: nonlinear dynamics
Tunes depend on amplitude
Landau Damping increases with the spread of betatron oscillation frequencies. Larger tune spread → beam more stable against collective instabilities.
  Can created by adding octupole magnets
If the system is integrable – no resonances
IOTA Goal: create practical nonlinear accelerator focusing systems with a large frequency spread and stable particle motion.
Notes:   McMillan (1967) – first successful 1-D example
  Perevedentsev, Danilov (1990 - 1995) – several 1D, 2D examples
  Cary etc (1994) – approximate integrability
  Danilov, Nagaitsev (2010) – practical 2D integrability

## Slide 5: Nonlinear lattice with two invariants
  Danilov, Nagaitsev, Phys. Rev. ST Accel. Beams 13, 2010
  Element of periodicity:
  Two invariants of motion:
      1) Hamiltonian
      2) I2(x,px,y,py)
Nonlinear potential, in elliptic coordinates

## Slide 6: Integrable Optics Test Accelerator
40 m circumference
4 30° and 60° dipoles
39 quadrupoles
2 drifts for nonlinear magnets

## Slide 7: IOTA parameters
Electron Energy | 150 MeV
Number of particles | 109
Ring Circumference | 40 m
Length of NL magnets | 1.8 m
Phase advance per NL section | 0.3
Synchrotron damping time | ~ 1 sec
Equilibrium beam size | ~ 0.1 mm
RF harmonic number | 4
Bunch length | 5 cm

## Slide 8: Need a special magnet
Can we do anything with just conventional magnets?
  Quadrupoles
  Octupoles
Cross-section and field lines

## Slide 9: Quasi-integrable Optics
Octupole magnet strength ~ 1/β(s)3
Hamiltonian does not depend on s:
Questions:
  What about the 3rd degree of freedom?
  Imperfections
6D Simulations required
18 10cm-long octupole magnets
Chart: B3, G/cm3
s, m | 0.0001176 | 0.00018435 | 0.00029129 | 0.0004599 | 0.00071558 | 0.0010756 | 0.0015212 | 0.0019642 | 0.0022514 | 0.0022514 | 0.0019642 | 0.0015212 | 0.0010756 | 0.00071558 | 0.0004599 | 0.00029129 | 0.00018435 | 0.0001176
Chart: Beta, m
| -0.95 | -0.85 | -0.75 | -0.65 | -0.55000000000000004 | -0.45 | -0.35 | -0.25 | -0.15 | -0.05 | 0.05 | 0.15 | 0.25 | 0.35 | 0.45 | 0.55000000000000004 | 0.65 | 0.75 | 0.85 | 0.95
Beta, m | 2.0343 | 1.7589 | 1.5142 | 1.3 | 1.1165 | 0.96348 | 0.84109 | 0.74931 | 0.68812 | 0.65752 | 0.65752 | 0.68812 | 0.74931 | 0.84109 | 0.96348 | 1.1165 | 1.3 | 1.5142 | 1.7589 | 2.0343
Beta-function in NL magnet section
t = 0.4, c2 = 0.01 cm, l = 10 cm

## Slide 10: 6D simulations
Lifetrac code by D. Shatilov
  Tracking
  Frequency map analysis
Model includes:
  Dipoles, dipole fringe fields
  Quadrupoles
  RF
  Octupoles
  No sextupoles
Betatron and synchrotron motion
Chromaticity

## Slide 11: Frequency map analysis: 1 section, octupole magnet
Tune spread: 0.03
Stable region: 2.5 x 2.5 mm

## Slide 12: Tracking
Hamiltonian is conserved
Motion is bounded
Simulated time – 1sec: no particles lost within stable region

## Slide 13: FMA: 1 section, quadrupole + octupole
Tune spread: 0.05
Stable region: 2.5 x 1.8 mm

## Slide 14: Experimental procedure
Two kickers, horizontal and vertical, place particles at arbitrary points in phase space
Measure beam position on every turn to create Poincare map
As electrons lose energy due to synchrotron radiation, they will cover all available phase space
Can control the strength on the nonlinearity
Final goal – dependence of betatron frequency on amplitude

## Slide 15: Two kickers create an arbitrary transverse kick
Horizontal + vertical stripline kickers
Rectangular pulses up to 25 kV ~ 100 ns duration.
Repetition rate < 1 Hz
Adjustable voltage 0 – Vmax
Courtesy A. Didenko

## Slide 16: Beam position can be measured precisely
20 horizontal and vertical BPMs
  Button type
  1 μm closed orbit resolution
  100 μm turn-by turn resolution
8 SR ports to measure beam size
A. Valishev, IOTA Design

## Slide 17: Octupole imperfections: stable region reduces insignificantly
No imperfections
Octupole error, σ = 0.1

## Slide 18: Lattice imperfections: stable region reduces insignificantly
No imperfections
Δβ = 1%, ΔΦ = 3·10-3

## Slide 19: Sources of error
Lattice imperfections
  Beta functions: 0.01 (relative)
  Phase advance: 0.001
Octupole magnet errors
  Less than 0.1
Bunch transverse size
  ~ 0.1 mm, RMS
Other:
  BPM resolution
  FFT
  Energy loss
Overall:

## Slide 20: Summary
It is possible to achieve tune spreads ~ 10-2 with just conventional magnet components and still retain large dynamic aperture
Search for optimal combination in terms of tune spread/size of dynamic aperture/complexity of the potential
Compare with full nonlinear potential
Next steps

## Slide 21: Thank You for Your Attention

## Slide 22: Backup slides

## Slide 23: Thick octupoles
While dynamic aperture is limited, the attainable tune spread remains large
Courtesy A. Valishev

## Slide 24: Optic functions in the nonlinear section
Equal beta functions in x and y
Zero dispersion