## Slide 1: Optimization of the Data Acquisition Software (PxSuite DAQ) for the Silicon Strip Telescope at FTBF
Clifford Denis
SIST Intern, Fermilab
Ramapo College of New Jersey
08/04/2014

## Slide 2: Background
What is the Silicon Strip Telescope?
  Created by the Detector Instrumentation Group (DIG) at Fermilab
  Built to track particles’ trajectories
  Used at the Fermilab Test Beam Facility (FTBF) to provide tracking information for different Detectors Under Test
What are the main components?
  The Silicon Strip Detector
  The CAPTAN Boards (DAQ Hardware)
  The PxSuite (DAQ Software)

## Slide 3: Si-Strip and DAQ layout

## Slide 4: The Si-Strip Telescope

## Slide 5: The Si-Strip Telescope and DAQ
The Strip Station
  Two strip planes mounted orthogonally
  A strip plane is made of 639 strips, each 60 microns wide and 9cm long
  Overlap area of ~4x4cm2
The CAPTAN Board (DAQ Hardware)
  Compact And Programmable daTa Acquisition Node
  Octagon-shaped electronic board designed for acquisition, processing and control of data in High Energy Physics
  Can be customized connecting other electronic devices (including additional CAPTANs) through the main buses

## Slide 6: The Si-Strip Telescope and DAQ
Fig. 3 - The Strip Station
Fig. 4 - The CAPTAN Board

## Slide 7: The PxSuite
The Configuration Files
  Used to configure the telescope and the DAQ hardware
  Sample actions include: setting the clock source, the clock speed, enabling and disabling strips, setting the threshold sensitivity of the strips
The PxSuite (DAQ Software)
  Written in C++, HTML and JavaScript
  Interface that lets the user program and interact with the hardware through a web-based graphical user interface

## Slide 8: Diagram of the PxSuite DAQ Software

## Slide 9: The Issues
Accessibility
  Some parts of PxSuite code not so easy to read
  Lacking methods to perform direct operations on registers
Performance
  Taking a lot of time to communicate to the hardware

## Slide 10: Accessibility
  Created methods that perform specific operations.
    Directly modify individual bits of the register STRIP_CSR (setting the BCO clock state, enabling the stream, etc.)
    Directly set the frequency according to the clock source (External or Internal).
    Communicate directly with the configuration files, therefore avoiding the need to modify the source code itself (getting the state of the clock from configuration file, etc).

## Slide 11: Performance
Implemented methods that minimize the response time.
  Send commands concurrently, therefore reducing the time the program has to wait for an acknowledgment from the hardware.
  Compare sent and received buffers, making sure they are correctly interpreted.
  Create a register from the hardware’s acknowledgment while starting data acquisition.

## Slide 12: Example of Code

## Slide 13: Conclusions and Future Work
Future Work
  There are more registers to work on, a lot more!
  PxSuite can probably be made even faster
Conclusions
  PxSuite code is now easier to read
  PxSuite performs faster than before

## Slide 14: THANKS!!!
Lorenzo Uplegger (Supervisor)
Ryan Rivera (Second Supervisor)
Kelly Stifter (co-worker)
Daniel Parella (co-worker)
Fermilab and the SIST committee

## Slide 15: Any questions?