## Slide 1: Engineering studies for the Conceptual design of the LBNO Facility
F. Sanchez Galan (CERN)
on behalf of the CERN Secondary Beam Working Group,
With contributions from B. Biskup, D. Brethoux, M. Calviani, N. Charitonidis, DAES,
I. Efthymiopoulos, B. Feral, J.A. Osborne, RAL, D. Smargianaki, C. Strabel, P. Velten, V. Venturi, H.Vincke.

## Slide 2
Outline
Lay out, overview
Horn, reflector, target, striplines
Target chamber
Decay pipe
Hadron stop
Timeline
Conclusions

## Slide 3
F = 3 m water cooled steel tube, surrounded by 150 cm concrete;
291 kA @ 50 GeV 281 kA @ 400 GeV
167 kA @ 50 GeV 198 kA @ 400 GeV
Helium tanks
~9 m3 cooled graphite, followed by iron blocks;
Near detector
Lay-out, overview

## Slide 4: Lay-out, overview
Underground layout designed in close contact with Radioprotection (See talk H. Vincke).
Horn, target, reflector, striplines
Integration of services.

## Slide 5: Lay-out, overview
He vessel at target chamber
Integration of services
Target, Horn and reflector and ancillary systems design and integration.
Openings for maintenance operations

## Slide 6: Horn and reflector
Target integration.
Insertion to horn & plug-in at the hot cell
Work done in collaboration with RAL

## Slide 7: Target
Target design was splitted between CERN-STI Phase 1 (400GeV) and RAL (50 GeV)

## Slide 8: Target
Work done in collaboration with RAL
Steady-state results, Trod 1387 C, inner C pipe 202, inner Be pipe 126 C

## Slide 9: Target
Transient results, T1 608 C, T2 362 C, T3 807 C
Maximum equivalent stress around 20 MPa during cycles, below the stress range fatigue limit for Graphite.
Maximum displacements around 0.45 mm

## Slide 10: Monolithic (peripherally cooled) target à la T2K
Helium cooling velocity streamlines
Maximum velocity = 398 m/s
Graphite core
T2K
Beam 30GeV, 750kW Target 23kW, 8 MPa stress
Ti-6Al-4V shell
M.Fitton C.Densham

## Slide 11: T2K-like Target & horn (50 GeV)
Target exchange system
Helium cooled solid graphite rod
Design beam power: 750 kW (heat load in target c.25 kW)
Beam power so far: 230 kW
1st target & horn just replaced after 4 years operation, 7e20 p.o.t.
π
π
p
RAL

## Slide 12: Horn, target integration
Work done in collaboration with RAL
Target helium feeds
Horn plug-in helium & water feeds

## Slide 13: Horn, target integration
Target integration
Work done in collaboration with RAL

## Slide 14: Horn and reflector, ancillary systems.
Plug-in systems, RH vertical movement.
He and water feeds /outlets
Striplines connection.

## Slide 15: Striplines remote connection
Vertical insertion
Clamping with a vice system

## Slide 16: Striplines thermal analysis
With a ‘normal’ He cooling, maximum temperatures are within acceptable values: below 50 C for phase 1 and below 100 C for phase 2

## Slide 17: Striplines remote connection
There’s a good margin to improve cooling if required.

## Slide 18: Horn and reflector
Thermo-structural analysis
Energy deposition for the entire horn: 56.75 kW
Max energy deposition: at target end ~ 110 W/cm3

## Slide 19: Horn thermal analysis
Phase 1 : Beam from SPS @ 400 GeV
6 s cycle
two extractions/cycle separately by 50 ms
beam pulse during 10 us in each extraction
3.5 1013 protons/extraction (7.0 1013 protons/cycle)
average beam power 750 kW
Phase 2 : Beam from HP-PS @ 50 GeV
- 1 s cycle
- single extraction per cycle
- beam pulse during 4 us
- 2.5 1013 protons/cycle
- average beam power 2.0 MW
Phase 1
Phase 2

## Slide 20: Horn thermal analysis

## Slide 21: Horn thermal analysis
The maximum temperature in steady state is 83°C for the 400GeV beam and 73°C for the 50GeV beam
For the 50GeV beam, the temperature remains always below 75°C, even during a pulse.
For the 400GeV beam, the temperature reaches 162°C during a short time.
Convection:
Inner conductor 10 kW/m2 K
Outer conductor 100 W/m2 K

## Slide 22: Horn structural analysis
Images from P. Sabbagh, DAES
Maximum lateral displacement
3.9 mm during pulse
Maximum vertical displacement
0.5 mm during pulse

## Slide 23: Horn structural analysis
Chart: Mode Nr.
 | 59.776 | 59.79 | 60.524 | 60.538 | 61.246 | 61.252 | 61.276 | 61.285 | 62.516 | 62.522 | 62.552 | 62.56 | 62.789 | 62.791 | 62.795 | 62.797 | 63.113 | 63.117 | 63.139 | 63.146 | 63.226 | 63.257 | 63.392 | 63.396 | 63.418 | 63.425 | 63.631 | 63.633 | 63.639 | 63.642 | 64.085 | 64.116 | 69.466 | 69.488 | 69.496 | 69.514 | 93.404 | 94.277 | 97.314 | 100.12 | 117.47 | 117.72 | 119.69 | 119.71 | 121.18 | 121.2 | 122.59 | 122.6 | 122.65 | 122.66
Vibration modes start at 93 Hz (main in the range 93-120 Hz)

## Slide 24: Horn structural analysis
Stress values are acceptable
The equivalent stress reaches for 400GeV 100MPa in the internal part of the horn, 132MPa in the exit cover and 30MPa in the front cover.
At 50GeV, those values are much smaller (31MPa, 119MPa and 28MPa respectively).

## Slide 25
Maintenance of horn + target
9th NBI @ Fermilab, 23-26 Sept 2014 F. Sanchez Galan

## Slide 26
Maintenance of horn + target
Concrete shielding wall has to be opened
9th NBI @ Fermilab, 23-26 Sept 2014 F. Sanchez Galan

## Slide 27
Maintenance of horn + target
Top concrete blocks have to be removed partially
Helium vessel has to be opened
Top iron blocks & cooling plates removed
All operations have to be done remotely
9th NBI @ Fermilab, 23-26 Sept 2014 F. Sanchez Galan

## Slide 28
Maintenance of horn + target
horn & target loaded on gantry crane
Water and electrical connectors are automatically released during lifting operation
9th NBI @ Fermilab, 23-26 Sept 2014 F. Sanchez Galan

## Slide 29
Maintenance of horn + target
horn & target transportation back to
Transport cavern
9th NBI @ Fermilab, 23-26 Sept 2014 F. Sanchez Galan

## Slide 30
Maintenance of horn + target
horn & target transportation back to
Transport cavern
9th NBI @ Fermilab, 23-26 Sept 2014 F. Sanchez Galan

## Slide 31
Maintenance of horn + target
horn & target transportation directly to morgue
9th NBI @ Fermilab, 23-26 Sept 2014 F. Sanchez Galan

## Slide 32
Maintenance of horn + target
horn & target lowered in the morgue
9th NBI @ Fermilab, 23-26 Sept 2014 F. Sanchez Galan

## Slide 33
Maintenance of horn + target
horn & target transportation to the hot cell
9th NBI @ Fermilab, 23-26 Sept 2014 F. Sanchez Galan

## Slide 34
Maintenance of horn + target
horn & target transportation using remotely operated “lifting table” vehicle – omnidirectional.
https://www.youtube.com/watch?v=2O8Cj0XiRIM#t=152
9th NBI @ Fermilab, 23-26 Sept 2014 F. Sanchez Galan

## Slide 35
Maintenance of horn + target
horn & target with transport vehicle
9th NBI @ Fermilab, 23-26 Sept 2014 F. Sanchez Galan

## Slide 36
Maintenance of horn + target
horn & target to hot cell
9th NBI @ Fermilab, 23-26 Sept 2014 F. Sanchez Galan

## Slide 37
Maintenance of horn + target
horn & target inside hot cell
9th NBI @ Fermilab, 23-26 Sept 2014 F. Sanchez Galan

## Slide 38: Heat loads in shielding elements
A detailed model of the whole geometry has been done in Fluka, including:
Target chamber shielding elements

## Slide 39: Heat loads in shielding elements
Internal elements: horn, reflector, striplines

## Slide 40: Heat loads in shielding elements
Decay tunnel

## Slide 41: Heat loads in shielding elements
Hadron stopper

## Slide 42: Heat loads in shielding elements
870 kW Iron
0.8 kW Al
80 kW Horn+striplines
5 kW Target
30 kW Reflector+striplines

## Slide 43
Around 4% of the generated Heat is removed by the Helium, 96% by water cooling
Temperature profiles: Target Chamber (4/4)

## Slide 44: Decay pipe
3 m diameter
Water cooled
Helium bag

## Slide 45: Decay pipe cooling
With the chosen configuration (32 cooling channels, contact surface 20 mm) the decay pipe temperature is around 42 C. The highest temperatures (around 75 C) are reached in the surrounding concrete.

## Slide 46: Decay pipe
Upstream shutter allows to keep He inside the decay pipe when opening the target chamber vessel
5 m long tube sectors welded, U water connections (T2K-like).

## Slide 47: Hadron stop (CNGS-like dump)

## Slide 48: Hadron stop (CNGS-like dump)

## Slide 49: Hadron stop (CNGS-like dump)
Aluminium water cooled sinks
Graphite core
Steel shielding
Energy deposition (FLUKA)

## Slide 50: Temperature estimations: Hadron stop
Graphite block, Al water cooled plates (CNGS-like)

## Slide 51: Temperature estimations: Hadron stop
Heat generation (from Fluka)
Maximum temperature at graphite 110 C for the 50 GeV case

## Slide 52: Temperature estimations: Hadron stop
Heat generation (from Fluka)
Maximum temperature at graphite 118 C for the 400 GeV case

## Slide 53: Temperature estimations: Hadron stop
Temperature in the graphite is far below 400°C (criteria for graphite) and the temperature in the aluminium plates remains around 30°. Even with a reduced water flow the margin is adequate.

## Slide 54: Possible CN2PY timeline

## Slide 55: Conclusions
Helium bags at target and decay pipe reduce RP issues. Remote operation foreseen for maintenance operations.
Acceptable values of cooling parameters, well known manufacturing methods available. No show stoppers.
Integration of elements and general services outlined.
A sound technical design for the secondary beam lines.
Ready for detailed design..

## Slide 56: Spare slides

## Slide 57
Preferred manufacturing method : Cylindrical sections with hydro formed or welded-U channels along each decay pipe section length, connected by U pipes between sectors. To be welded in-situ.
 | Surface Area Coverage | Operating Temperature | Ratio of Cooling Area to Cost
Hydra~Cool | Excellent | Excellent | Excellent
Machined in Trace | Excellent | Excellent | Poor
Dimple Plate | Excellent | Excellent | Good
Double Walled | Excellent | Excellent | Poor
Welded C Channel | Good | Good | Good
Wrapped Tube | Poor | Poor | Poor
Effectiveness of Hydro forming Versus Alternative Water Cooling
Pictures & table from www.lesker.com
Picture from CNGS

## Slide 59
Hydra~Cool Features
Hydra~Cool is a technically superior and cost effective method of water cooling vacuum chambers.
This revolutionary new method of water-cooling is made by welding a trace to a chamber and then using water pressure to hydro-form the water channel. By utilizing radius bends instead of square corners, it improves water flow and eliminates low flow and stagnant areas. When coupled to a full penetration weld, this reduces the chances of crevice crack corrosion and extends the working life of the chamber.
Hydra~Cool gives you the ability to approximately double the surface area being cooled over conventional ‘C’ channel style water cooling. This high surface area coverage possible with this method also makes it an affordable alternative to double walled cooling.

## Slide 60: Minimal requirements for water cooling ( Heat transfer coefficient )
A heat transfer coefficient of 2 kW/m2/K was considered in all calculations.
For a 20 mm Din pipe, this is achievable with speeds above 0.35m/s (pressure drop around 1 mbar per meter)
For a 20x4mm rectangular channel, this is achievable with speeds above 0.35m/s (pressure drop around 1 mbar per meter)