## Slide 1: Total Loss Monitor Radiation Safety System
Neutrino Beams and Instrumentation Workshop 2014
A. Leveling
9/26/14

## Slide 2: background:
At Fermilab, high power beams are being planned for existing facilities which have insufficient passive shielding, e.g.,
  Muon Campus(13 W -> 8 kW)
  Booster (~35 kW -> 80 kW)
  Main Injector (700 kW -> 2 MW)
Supplemental shielding addition is not possible and/or very costly and/or impractical
Historically, Fermilab has used passive shielding in conjunction with interlocked radiation detectors to provide comprehensive protection necessary to meet the requirements of the Fermilab Radiological Controls Manual (FRCM)

## Slide 3: Motivation for TLM:
Large numbers of additional interlocked detectors (chipmunks) would be required for some installations, e.g.,:
  Muon campus (42->200 - mu2e experiment)
  Booster (48->? – PIP/PIP-II)
AD received encouragement from the Fermilab ESH&Q Section in May 2011 to pursue development of a long detector system

## Slide 4
3 parallel TLM detectors
125’
250’
350’
Pbar
A2B7
magnet
TLM provides
continuous, in-tunnel
coverage
Chipmunks provide
discrete, above-ground
coverage
Examples of Chipmunk and TLM installations
Scheme works fine for known limiting apertures

## Slide 5: TLM system diagram
Detector works in ion chamber mode
  800 volt detector bias
Argon/CO2 detector gas
  Nominally 25 cc/min
Electrometer output is calibrated in units of nC/TTL pulse
Heartbeat provided by 10 Tohm resistor (83 pA = 5 nC/min)

## Slide 6: TLM system design requirements:
Limit beam losses to the level of 1 watt/meter
The TLM electrometer must be able to collect charge with a 100% duty factor, i.e., no dead time for integrator reset
TLM system must connect directly to the existing Radiation Safety System (RSS), via existing radiation interlock cards
Include a rigorous testing program and calibration schedule
The response of the TLMs must be characterized and /or predictable for a wide range of beam loss conditions
The TLM system must be fail safe; i.e., the (RSS) must be disabled if:
  TLM chassis loses power
  Motherboard voltages go out of tolerance
  TLM detector is disconnected from its electrometer
  TLM heartbeat is lost (provided by 83 pA leakage current)
  TLM bias voltage falls outside tolerance
  The TLM gas flow is lost, (nominally 25 cc/min)

## Slide 7: Setting TLM trip levels:
Determine the worst case beam loss condition by:
  Evaluation of the possibilities, then
    MARS simulation(s), and/or
    Measurement
The worst case condition includes consideration of:
  Beam enclosure geometry
  Maximum beam intensity lost (MBL)
  Beam energy
  Amount of shielding present

## Slide 8: Setting TLM trip levels:
Posting and controls for region determined allowable beam intensity lost (ABL)
The TLM response to the worst case condition (TLMmax) is determined by:
  Measurement, or
  By MARS simulation
TLM trip level is set by scaling:
  Trip Level = TLMmax x ABL / MBL

## Slide 9: TLM trip level philosophy:
The trip level has to be safe AND it has to allow normal losses with reasonable margin for variances in operation
  Avoid spurious/unnecessary system trips
TLM cannot distinguish between single point, localized losses and losses distributed over its entire length
  This implies the trip levels are conservative
Trip levels are to be determined by the laboratory’s well-developed, shielding assessment process

## Slide 10: Possible applications:
Limit effective dose rate outside of radiation shields
  Implicitly includes control of radiation skyshine
Limit beam loss to 1 W/m
Limit surface water, ground water, and/or air activation

## Slide 11
Chart: Normalized 178.5' TLM Response 400 MeV protons 2 detector gases at 2 Intensities
| 8.2100000000000009 | 20 | 50 | 100 | 200 | 500 | 1000 | 1500 | 2000
argon, 3E12ppp | 0.12111 | 0.18323 | 0.21345 | 0.22184 | 0.22953 | 0.2266 | 0.22818 | 0.23553 | 0.25106
argon, 0.5E12ppp | 0.31465 | 0.18285 | 0.22142 | 0.22474 | 0.25031 | 0.24564
argon-CO2, 3E12ppp | 0.045112 | 0.088863 | 0.12597 | 0.14516 | 0.15547 | 0.15708 | 0.15962 | 0.16048 | 0.16042
argon-CO2, 0.5E12ppp | 0.08201 | 0.096111 | 0.12386 | 0.12746 | 0.14661 | 0.16367 | 0.15311 | 0.16616 | 0.17301

## Slide 12: Example application: NuMI groundwater protection
NuMI beam power
800’ TLM response
Scarecrow in NuMI tunnel
(existing GW protection)
A seven day operating period August 20 -> September 4, 2014

## Slide 13
Example application: Booster shielding
Booster beam power
180’ TLM response
Proposed TLM trip limit
A thirty-eight day operating period July 14 -> August 21, 2014

## Slide 14: Timeline:
Development began in May 2011
Extensive detector response testing October 2011 to present
Preliminary approval granted by Fermilab ESH&Q in May 2014
Full demonstration application begins October 2014
  Entire Booster Ring covered by 8 systems
  In parallel with the existing system of 48 chipmunks
  One redundant detector cable
Accelerator Division will seek final approval of the system in CY2015

## Slide 15: Extra slides

## Slide 16: Detector Cable
HJ5-50, HELIAX® Standard Air Dielectric Coaxial Cable, corrugated copper, 7/8 in,
black PE jacket

## Slide 17
Booster TLM installation plan

## Slide 18
TLM response to 8 GeV proton beam loss at A2B7 magnet at Accumulator
Argon detector gas

## Slide 19
Chart: Booster 178.5' TLM Plateau 400 MeV Protons 2 detector gases at 2 Intensities
| 8.2100000000000009 | 20 | 50 | 100 | 200 | 500 | 1000 | 1500 | 2000
argon, 3E12ppp | 39.76 | 59.52 | 69.8 | 72.6 | 73.2 | 74 | 74 | 77 | 82
argon, 0.5E12ppp | 17 | 9.76 | 11.52 | 11.8 | 13.6 | 13.4 | 13 | 13 | 14
argon-CO2, 3E12 ppp | 13.906 | 27.7712 | 39.4332 | 44.8607 | 48.7146 | 49.275 | 49.55 | 49.2375 | 50.1
argon-CO2, 0.5E12 ppp | 4.859 | 5.6568 | 7.1498 | 7.2911 | 8.5719 | 9.4125 | 8.825 | 9.2375 | 10.1

## Slide 20: Critical shielding thickness
A layer of shielding which must be present to limit the delivered dose over an interval at which the TLM system can respond
The resulting dose that could be delivered must fall below limits established by the Fermilab Radiological Controls Manual for the desired posting and occupancy condition