## Slide 1: Long-Baseline Neutrino Experiment
9th Neutrino Beam & Instrumentation Workshop
September 23-26th 2014
LBNE Lattice & Line Design
John A. Johnstone
Fermilab
JJohnstone@fnal.gov
September 24th, 2014

## Slide 2: Ovtline
Design Overview
  Trajectory
  Magnets
  Optics
    Lattice Functions
    Beam Envelope & Magnet Apertures
    Final Focus & Spot Size Tuning
    MI-10 Extraction
Summary
Other Stuff
  Sensitivity to Gradient Errors
  Trajectory Control
  Power Supply Ripple Effects
  Known Interferences
  Magnet Parameters

## Slide 3: MI-10 Tunnel → LBNE Enclosure Transfer
Q204
Q205
CARRIER PIPE
RECYCLER
LBNE Q204
INJECTOR
Transport from the existing MI tunnel enclosure into the new LBNE enclosure showing the carrier pipe connecting the MI-10 & LBNE enclosures (left), and separation of Q204 at the u/s end from the Main Injector & Recycler Rings (right).

## Slide 4: Primary Beam & Hill Cross-section
THE PRIMARY BEAMLINE EXTRACTS PROTONS FROM MI-10 & TRANSPORTS TO THE TARGET ABOVE GRADE
BLC apex elev. @ 30 ft above grade
Target elev. @ 10 ft above grade

## Slide 5: Aerial View of LBNE Trajectory
?

## Slide 6: Trajectory
Beam is extracted vertically from MI-10 via 5 horizontal kicker modules d/s of MI quad Q100, and 3 Lambertsons plus a C-magnet straddling MI Q102.
A rolled dipole steers the beam through the enclosure wall, while bisecting the MI & Recycler magnet elevations.
In the LBNE tunnel the beam is bent 7.2o horizontally to align with SURF in South Dakota, and upwards by 143 mr. A second series of vertical dipoles bend the beam down through 244 mr to complete vertical alignment to SURF, with φ = -101 mr.
Target elevation is fixed at 750 ft (~10 ft above grade) & maximum BLC elevation is 770 ft (~3 stories above grade).
Distance from MCZERO to center of LAr FD = 1286873.765 m ±

## Slide 7: LBNE – the Ride
33 kt LAr
WCD
*
*
~732 m
MI-10
TARGET
Beam Direction

## Slide 8: Magnet Complement
All major magnets are well-understood, proven designs
  In the main body of the line all dipoles are Main Injector-style IDA/IDB (6m) & IDC/IDD (4m) magnets
  Quadrupoles are all of the MI-style 3Q120 (3.048 m) or the shorter 3Q60 version (1.524m)
  New IDS trims have 3” pole tip gap & design spec of 250 μr (RMS).
  IDA/IDB sagitta = 11.7 → 18.6 mm c.f. 16 mm design nominal
  IDC/IDD sagitta = 5.2 → 8.3 mm c.f. 7 mm design nominal
Magnet | Common Name | Steel Length | Strength at 120 GeV | Count
Kickers | NOvA extraction type | 1.295 m | 0.0589 T | 5
ILA | MI Lambertson | 2.800 m | 0.532 / 1.000 T | 3
ICA | MI C Magnet | 3.353 m | 1.003 T | 1
IDA/IDB | MI Dipole 6 m | 6.100 m | 1.003 – 1.604 T | 13
IDC/IDD | MI Dipole 4 m | 4.067 m | 1.003 – 1.604 T | 12
QQB | MI 3Q120 quadrupole | 3.048 m | 9.189 – 16.546 T/m | 17
QQC | LBNE 3Q60 quadrupole | 1.524 m | 11.135 – 17.082 T/m | 4
IDS | LBNE trim dipoles | 0.305 m | Up to 0.365 T | 23

## Slide 9: Optics
To avoid losses the beam size in the LBNE transfer line can not exceed that of the Main Injector circulating beam.
The ultra-clean transport requirements virtually compel the lattice to be configured from distinct optical modules.
  Every focusing center has a dual-plane BPM & dipole corrector
  Every half-cell has space reserved for a multi-wire or other diagnostics.
Spot-size on target must be tunable over a wide range: from  ~ 1.0 → ~4.0 mm to accommodate a beam power upgrade to 2.4 MW.
Physics dictates it must also be continuously tunable over the range 60 → 120 GeV/c for optimizing the neutrino oscillation spectrum.
___________________________________________________________________________________________________
Subsequent discussions , unless stated otherwise, assume nominal MI beam parameters of 99= 30 m (normalized) & p99/p = 11.e-4, with σ* = 1.50 mm.
Satisfying the above conditions requires that the final focus β* be tunable over a range x32 (!).

## Slide 10: Lattice Functions
Horizontal (solid) and vertical (dashed) lattice functions of the LBNE transfer line
The final focus is tuned for x = y = 1.50 mm at 120 GeV/c with β* = 86.33 m and nominal MI beam parameters ε99 = 30 μm & Δp99/p = 11x10-4

## Slide 11: Beam Envelopes & Magnet Apertures
The beamline can transport, without losses, the worst quality beam that the MI could conceivably transfer.
Dipole apertures, shown in blue, include the effects
of sagitta & rolls.
Quadrupole apertures are red.
The 99% envelopes (dashed) represent nominal MI beam parameters
[ 99 = 30 m & p99/p = 11.e-4 ];
The 100% envelopes (solid) correspond to the MI admittance at transition .
[ 100 = 360 m & p100/p = 28.e-4 (t = 21.600) ]

## Slide 12: Final Focus & Spot-Size Tuning
The extremes shown correspond to: 60 GeV/c with σ* = 1.0mm; β* = 19.184m and βmax = 104m (lower), and; at 120 GeV/c with σ* = 3.20mm; β* = 393 m and βmax = 483 m (upper). Horizontal values are displayed as solid curves & vertical values are dashed.
In principle the spot –size can be tuned to σ* = 4.00mm, but the 3.20mm limit arises from the 360π mm-mr horizontal acceptance of the final down bend.
60 GeV : σ* = 1.0mm
120 GeV : σ* = 3.2mm
y

## Slide 13: MI-10 Extraction
WCD
*
*
~732 m
MI Q104 looking upstream

## Slide 14: Extraction Element Configuration
LBNE extraction Lambertsons and C-magnet straddling MI quad Q102
LBNE extraction elements and their configuration are clones of those found at other MI extraction points.

## Slide 15: Closed Orbit & Extraction Trajectory through MI-10
Circulating & extracted beam trajectories through MI-10
Closed Orbit Bump Quad Offsets
(mm)
Q100 2.064
Q102 2.358
Q104 2.171
Q106 2.164
Extracted Beam Elements
Q100 2.064 mm
Kickers 5 x -190.0 μr (0.693 kG/module)
Q102 2.358 mm
LAM1 0.523 T
LAM2&3 0.998 T
C-MAG 0.998 T

## Slide 16: Beam-Beam Separation in Quad 102
Closed orbit bump is created by transverse offsets of focusing quads.
Kickers create 36.2 mm separation at the 1st Lambertson entrance between circulating & extracted beams.
Circulating & extracted beams through Lam1 & Q102
Large Aperture Quad
55/8 x 55/8 Star Chamber

## Slide 17: MARS Extraction Tracking
Normalized 100% beam emittance is ε100 = 360π mm-mr
10,000 points are selected on a surface in 4-dimensional (x,x’;y,y’) phase space
Extraction tracking is from the u/s end of Q100 to the end of the 3rd Lambertson

## Slide 18: Beam-Beam Separations from MARS
There is sufficient aperture to provide loss-free extraction of a normalized εN = 360π µm emittance beam (10.6 σ)

## Slide 19: Summary
Ω
Beam is extracted at MI-10 & transported to a target above grade.
The lattice design is comprised entirely of proven MI-style magnets.
MI-10 extraction configuration & the beamline provide for loss-free transmission of a 10.6σ beam.
The final focus is continuously tunable from σ* = 1.00 → 4.00 mm over the entire momentum range 60 → 120 GeV/c

## Slide 20: Other Stuff
  Sensitivity to Gradient Errors
  Trajectory Control
  Power Supply Ripple Effects
  Known Interferences
  Magnet Parameters

## Slide 21: Sensitivity to Gradient Errors
21
Not An Issue!
Experience has shown the MI-style 3Q120 quadrupoles to be of very high accelerator qualityϮ
  (G/G)  0.08% or less, which can be reduced even further for the FODO section with only rudimentary sorting.
  A simple thin-lens calculation predicts that even the largest error-wave generated in the 99% beam envelope [3.74mm at  = 59.6m] would be < 70 microns.
_________________________________________________________________
Ϯ Magnet Test Facility measurement data base.

## Slide 22: Trajectory Control
22
Misalignments (including BPM’s)
  (x,y) = 0.25 mm
  (roll) = 0.50 mr
Dipole Field Errors
  (B/B) = 10e-4
Uncorrected/corrected trajectories with random misalignments and dipole field errors
The plot begins at the u/s end of the 1st Lambertson.
New IDS design spec is 250 μr (RMS).

## Slide 23: Known Interferences
  C-magnet – MI Beamtube 
  Q201A/B – MI Q103 
  HT201A – MI Beamtube 
  VT203 – MI Tunnel Wall 
  Q204 – LBNE Enclosure Wall 
  V217A/B Overlap 
  LBNE – Recycler Co-existence

## Slide 24: LBNE– Recycler Co-existence
Coraggio ! Avanti !

## Slide 25: Magnet Parameters
DIPOLE TYPE (#) | L (m) | B (T) | TILT (deg) |  | QUAD NAME (#) | TYPE | L (m) | G (T/m)
MI-10 EXTRACTION  LBNE |  |  |  |  |  |  |  | 
LAM1 | 2.8000 | 0.53242 | 90.000 |  |  |  |  | 
 |  |  |  |  | Q102 | 3Q84 | 2.134 | +16.16016
LAM12 (2) | 2.8000 | 1.00000 | 90.000 |  |  |  |  | 
V100 | 3.3528 | 1.00284 | 90.000 |  |  |  |  | 
MATCH FROM MI  LBNE FODO LATTICE & 143 mr UP BEND |  |  |  |  |  |  |  | 
 |  |  |  |  | Q201202 | 3Q60 | 1.524 | 11.13509
IDA/B | 6.09981 | 1.22335 | +62.844 |  |  |  |  | 
 |  |  |  |  | Q203 | 3Q120 | 3.048 | +12.48756
 |  |  |  |  | Q204 | 3Q120 | 3.048 | 9.18907
 |  |  |  |  | Q205 | 3Q120 | 3.048 | +13.06221
IDC | 4.06654 | 1.38347 | 44.126 |  |  |  |  | 
IDB | 6.09981 | 1.38347 | 44.126 |  |  |  |  | 
 |  |  |  |  | Q206 | 3Q120 | 3.048 | 13.52413
IDA | 6.09981 | 1.38347 | 44.126 |  |  |  |  | 
IDD | 4.06654 | 1.38347 | 44.126 |  |  |  |  | 
 |  |  |  |  | Q207 | 3Q120 | 3.048 | +16.16931
IDC | 4.06654 | 1.10813 | 48.179 |  |  |  |  | 
IDB | 6.09981 | 1.10813 | 48.179 |  |  |  |  | 
FODO CELLS |  |  |  |  |  |  |  | 
 |  |  |  |  | Q208 | 3Q120 | 3.048 | 15.83240
IDA | 6.09981 | 1.10813 | 48.179 |  |  |  |  | 
IDD | 4.06654 | 1.10813 | 48.179 |  |  |  |  | 
 |  |  |  |  | Q209 | 3Q120 | 3.048 | +15.83240
IDC | 4.06654 | 1.00297 | 56.109 |  |  |  |  | 
IDB | 6.09981 | 1.00297 | 56.109 |  |  |  |  | 
 |  |  |  |  | Q210 | 3Q120 | 3.048 | 15.83240
IDA | 6.09981 | 1.00297 | 56.109 |  |  |  |  | 
IDD | 4.06654 | 1.00297 | 56.109 |  |  |  |  | 
 |  |  |  |  | Q211213 (3) | 3Q120 | 3.048 | ±15.83240
244 mr ACHROMATIC DOWN BEND & FINAL FOCUS ON TARGET |  |  |  |  |  |  |  | 
IDC | 4.06654 | 1.60431 | +90.000 |  |  |  |  | 
IDB | 6.09981 | 1.60431 | +90.000 |  |  |  |  | 
 |  |  |  |  | Q214 | 3Q120 | 3.048 | 13.96520
IDA | 6.09981 | 1.60431 | +90.000 |  |  |  |  | 
IDD | 4.06654 | 1.60431 | +90.000 |  |  |  |  | 
 |  |  |  |  | Q215 | 3Q120 | 3.048 | +16.54570
IDC | 4.06654 | 1.60431 | +90.000 |  |  |  |  | 
IDB | 6.09981 | 1.60431 | +90.000 |  |  |  |  | 
 |  |  |  |  | Q216 | 3Q120 | 3.048 | 15.26976
IDA | 6.09981 | 1.60431 | +90.000 |  |  |  |  | 
IDD | 4.06654 | 1.60431 | +90.000 |  |  |  |  | 
 |  |  |  |  | Q217 | 3Q120 | 3.048 | +13.81046
IDC/D | 4.06654 | 1.60431 | +90.000 |  |  |  |  | 
 |  |  |  |  | Q218 | 3Q60 | 1.524 | 17.08214
IDA/B | 6.09981 | 1.60431 | +90.000 |  |  |  |  | 
IDA/B | 6.09981 | 1.60431 | +90.000 |  |  |  |  | 
IDC/D | 4.06654 | 1.60431 | +90.000 |  |  |  |  | 
 |  |  |  |  | Q219 | 3Q120 | 3.048 | 10.53138
 |  |  |  |  | Q220 | 3Q120 | 3.048 | +15.80329
 |  |  |  |  | Q221 | 3Q60 | 1.524 | 13.39482

## Slide 26
Backoff Interference Pictures

## Slide 27: C-magnet – MI Beamtube

## Slide 28: Q201A/B – MI Q103 & HT201A – MI Beamtube

## Slide 29: VT203 – MI Tunnel Wall

## Slide 30: Q204 – LBNE Enclosure Wall

## Slide 31: V217A/B Overlap