## Slide 1: The IsoDAR Target at KamLAND for NBI2014 and now for something completely different…
L. Bartoszek
BARTOSZEK ENGINEERING
With contributions from the DAEdALUS/IsoDAR collaboration
9/25/14
I SODAR
@ kamland

## Slide 2: What is IsoDAR?
IsoDAR is:
A search for sterile neutrinos
A Decay At Rest neutrino source next to the KamLAND detector (or one like it)
A step in the development of the DAEdALUS experiment
  The IsoDAR cyclotron is the injector for the DAEdALUS cyclotron
  10 milliamps of 60 MeV protons, 600 kW on the target, CW

## Slide 3
_
Proton beam  9Be  n  captures on 7Li  8Li  ne
Scintillator
few
meters
A source of
protons
Be target
embedded
in sleeve
The proton-producing machine (cyclotron) is separate from the neutron-producing target to avoid:
  Activation of the machine so it can be serviced
  Unwanted backgrounds to the antineutrino flux
many
meters
Schematic of IsoDAR

## Slide 4: IsoDAR Configuration at KamLAND
Plan view
Elevation view
Cyclotron
Target
KamLAND detector
Beam Transfer Line

## Slide 5: The IsoDAR Cyclotron and Ion Source
~ 6 meters
Ion Source
Low Energy Beam Transfer Line
Cyclotron

## Slide 6
Cross-section of the KamLAND target
Concrete
Graphite in container
7Li (FLiBe) in tank
Beam line and window assembly
Target assembly

## Slide 7: What is FLiBe?
"Purified Flibe" by Bckelleher - Own work. http://commons.wikimedia.org/wiki/File:Purified_Flibe.JPG#mediaviewer/File:Purified_Flibe.JPG
“FLiBe is a salt made from a mixture of lithium fluoride (LiF) and beryllium fluoride (BeF2). It has been used in the Molten Salt Reactor Experiment.
The low atomic weight of lithium, beryllium and to a lesser extent fluorine make FLiBe an effective neutron moderator. As natural lithium contains ~7.5% lithium-6, which tends to absorb neutrons producing alpha particles and tritium, nearly pure lithium-7 is used to give the FLiBe a small cross section.”
--from the Wikipedia
We need the isotopically pure Li-7 to absorb neutrons, become Li-8, and decay producing anti-electron neutrinos.

## Slide 8
BEAM
Close-up section view of beryllium water vessel
All the metal inside the Li/FLiBe is beryllium to allow neutrons to get into the FLiBe. Arrows indicate water flow.
This is the target disk of Be <2cm thick, 20 cm diameter
4” pipe
Be block
FLiBe
FLiBe

## Slide 9
Outside view of target, everything opaque
31.8 tons of concrete in the outer block (not counting the concrete in the target module.)

## Slide 10
Concrete shield made transparent showing the graphite container
We need to decide if we need dense bricks of nuclear graphite, or can we get away with packing graphite powder around the FLiBe tank? The bricks will be more expensive but denser.

## Slide 11
Graphite and its container made transparent showing the Li/FLiBe tank
At this point, FLiBe looks more benign than elemental Lithium. Either one can be cast inside this tank, but to cast the lithium the whole thing has to be done in an inert atmosphere making it much more complicated.

## Slide 12
FliBe tank made transparent showing the beam line module and the target module

## Slide 13
Beam line module turned off showing only target in place

## Slide 14
Target turned off showing beam line module in place
In this design either module can be in or out completely independently of the other. The design philosophy was to put layers of FLiBe and graphite in each module to avoid gaps.
There may be a problem with the beam window in this design getting too hot, or the air gap contributing to air activation. We are looking at evacuating the space around the target.

## Slide 15
Showing the Beam line module ready for insertion into the target
The module as shown weighs 178 lbs. It will need a rail system to guide it into the opening.
The beam raster magnets that exist in the hole in the concrete need to be removed to replace this module. How hot will it be to expose the Be target core? Need remote handling?

## Slide 16
Section view of the beam line module showing the FliBe and graphite
Be tubes and thin window
Li/FLiBe slug
Graphite slug
Steel tube brazed to Be tube
We need to look at the energy deposition in the thin window and check whether air activation will be an issue. This work is in progress.

## Slide 17
View showing the target module (“torpedo”) ready for insertion
Target module weighs 609 lbs. It needs to be retracted into a coffin for disposal. It will also need a rail system for guidance.
We are just starting to look at the remote handling issues and are very open to comments from the experts.

## Slide 18
View of the different sections of the target torpedo
All beryllium
Steel for parts not in contact with water, stainless steel for water pipes

## Slide 19
Section view of the Target torpedo
This flange contains the graphite
Li/FliBe
graphite
concrete
Boundary between beryllium and steel sections
Beryllium water vessel with integrated target disk
4” pipe water inlet
2.5” pipe water outlets

## Slide 20
Outside view of Li/FLiBe casting tank
The capped off ports are where you would insert molten metal/FLiBe
This is a steel fabrication (with a central beryllium tube) that weighs 1,042 lbs.

## Slide 21
Section view of the FLiBe tank showing the beryllium tube brazed in the center to create the center section that the beam line and target modules insert into

## Slide 22: Summary of Be manufacturing techniques
Beryllium fabrication and joining techniques:
  The joints shown are either brazed or electron beam welded
  The vessel is a powder metallurgy product
  The tubes could be extrusions

## Slide 23: The thermal problem
The IsoDAR target does not resemble existing NuMI, T2K or MiniBooNE targets
It resembles a scaled up version of the target described in:
Brandon’s paper was about an accelerator and target designed for Boron Neutron Capture Therapy at MIT.

## Slide 24: Submerged Jet Impingement cooling
We need to remove 300 kW of heat from Be and 300 kW in water deposited by 10 mA of protons at 60 MeV
Technique is to flow sub-cooled water fast over a hot surface to sweep away bubbles coming from boiling
  Normal forced convection in water achieves h ≈ 5 kW/m2-K
  Submerged jet impingement achieves h ≈ 250 kW/m2-K (50X better cooling)

## Slide 25: What has been achieved previously:
“Submerged jet-impingement cooling has been tested in order to remove heat at fluences approaching 6 kW/cm2.”
“A 17 mm diameter (.67”) jet of water impinging normally on a target has effectively removed 5.07 kW/cm2…”
We will scale up the concept in prototype to measure larger scale cooling parameters
  Other geometries have been used to extract similar levels of heat so there are existence proofs

## Slide 26: Parameters based on paper
Optimum diameter for the cooling nozzle is ½ that of the area being cooled.
  This means our nozzle diameter is 10 cm (4 inch sched 40 pipe)
Optimum Z/D spacing is 1
  The nozzle is a Z distance equal to D back from the back side of the target disk
If the water velocity is 35 m/s, then we need 4,500 GPM flow through the 4 inch pipe.
  We are studying erosion

## Slide 27
Schematic of a simple plumbing system
Components to produce a static water pressure increase not shown
Beam

## Slide 28: Summary
We have a lot of work to do to mesh a small accelerator complex into the mine tunnel at KamLAND
Any advice you can give us on remote handling and activation issues is most appreciated