## Slide 1: Challenges Summary
‘New’ Collider Projects that are already on their way:
Super KEKB
HL-LHC
Collider Projects for the near Future (> 10 years):
Linear Collider projects: ILC & CLIC
FCC-ee
CepC project
 DA, beam-beam, space charge, e-cloud, lifetime
 SC magnets, SC RF [Crab Cavities & HHRF]
 cost, power, positrons
 beam lifetime, SC RF, cost
 beam lifetime, SC RF, cost
Super KEKB
Contents
Collider Projects for the immediate Future (< 10 years):
Electron-Ion collider (MEIC, eRHIC, LHeC)
 ERL & pol.

## Slide 2: Challenges Summary
Collider Projects for the long-term Future (> 20 years):
HE-LHC
FCC-hh
FCC-he
Chinese SppC project
Collider Projects for the very long-term Future:
Muon collider
Collider based on Plasma-Wakefield acceleration
 SC magnets (11T, 16T, 20T?)
 SC magnets, cost
 SC magnets, cost, power consumption
 SC magnets, cost
 target, cooling, fast cycling magnets, cost…
 ?????
Contents

## Slide 3: Past, Present, Future
e+e‑ Linear Colliders
HE e+e‑ Storage Rings
HE pp Colliders
Tendency!
Ambitious Scope
High Costs
Long R&D times
(e.g. HL-LHC magnets > 25 years)
➜ Global Projects!
FCC-hh16T magnets)
Notes: But no funding!

## Slide 4
SuperKEKB
40 times higher luminosity
2.1x1034 --> 8x1035 cm-2s-1
KEKB to SuperKEKB
Colliding bunches
Nano-Beam scheme
extremely small by*
low emittance
Beam current double
Redesign the lattice to squeeze the emittance
TiN-coated beam pipes with antechambers
New S.C. final focusing magnets near the IP
New e+ Damping Ring
e- 2.6A
e+ 3.6A
Injector Linac upgrade
DR tunnel
Reinforce RF systems
New HER wiggler section

## Slide 5: SuperKEKB: Injector
40-times higher Luminosity
  Twice larger storage beam  Higher beam current at Linac
  20-times higher collision rate with nano-beam scheme
     Low-emittance even at first turn  Low-emittance beam from Linac
     Shorter storage lifetime  Higher Linac beam current
Linac challenges
  Low emittance e-
    with high-charge RF-gun
  Low emittance e+
    with damping ring
  Higher e+ beam current
    with new capture section
  Emittance preservation
    with precise beam control
  4+1 ring simultaneous injection
Notes: Higher Injection Beam Current
  To Meet the larger stored beam current and shorter beam lifetime in the ring
  4~8-times larger bunch current for electron and positron
  Reconstruction of positron generator, etc
Lower-emittance Injection Beam
  To meet nano-beam scheme in the ring
  Positron with a damping ring
  Electron with a photo-cathode RF gun
  Emittance preservation by alignment and beam instrumentation
Quasi-simultaneous injections into 4 storage rings
  SuperKEKB e–/e+ rings, and light sources of PF and PF-AR
  Improvements to beam instrumentation, low-level RF, controls, timing, etc

## Slide 6: Super KEKB:
Main challenges:
Dynamic aperture with strong beam-beam
IR optics with large momentum acceptance
Space charge effects (-> DA)
Small vertical beam size and y/x emittance ratio (0.3%)
e-cloud
beam lifetime (5min) and operation with ‘top-off’
experiment background

## Slide 7: Goal of High Luminosity LHC (HL-LHC):
The main objective of HiLumi LHC Design Study is to determine a hardware configuration and a set of beam parameters that will allow the LHC to reach the following targets:
Prepare machine for operation beyond 2025 and up to 2035
Devise beam parameters and operation scenarios for:
# enabling at total integrated luminosity of 3000 fb-1
# implying an integrated luminosity of 250 fb-1 per year,
# design oper. for m ≤ 140 ( peak luminosity of 5 1034 cm-2 s-1)
> Ten times the luminosity reach of first 10 years of LHC operation!!

## Slide 8: HL-LHC goal could be reached in 2036
How can we realize this jump
and steady accumulation of
Integrated Luminosity?

## Slide 9: The critical zones around IP1 and IP5
More than 1.2 km of LHC !!
Plus technical infrastructure
(e.g. Cryo and Powering)!!
ATLAS
New triplet Nb3Sn
required due to:
-Radiation damage
-Need for more aperture
Changing the triplet region is not enough for reaching the HL-LHC goal!
2. We also need to modify a large part of the matching section
e.g. Crab Cavities &
D1, D2, Q4 & corrector
3. For collimation we also need to change the DS in the continuous cryostat: 11T Nb3Sn dipole
CMS

## Slide 10: LHC low-β quads: steps in magnet technology from LHC toward HL-LHC
LHC (USA & JP, 5-6 m)
70 mm, Bpeak 8 T
1992-2005
LARP TQS & LQ (4m)
90 mm, Bpeak 11 T
2004-2010
LARP HQ
120 mm, Bpeak 12 T
2008-2014
LARP & CERN
MQXF
150 mm, Bpeak 12.1 T
2013-2020
Ca. 20 years for Nb3Sn magnet development!
HEPAP Accelerator Sub-Panel Road Trip, August 2014
> 10 years development for NbTi magnets

## Slide 11: Progress with Triplet magnets:
CERN short coil
with Cu cable
HEPAP Accelerator Sub-Panel Road Trip, August 2014
LARP HQ
120 mm, Bpeak 12 T
2008-2014
Short  4m
LARP & CERN MQXF
150 mm, Bpeak 12.1 T
2013-2020

## Slide 12: The HL-LHC Nb-Ti magnet zoo…
D1 (KEK)
Nested Orbit corrector (CIEMAT)
HO correctors: superferric (INFN)
D2 (INFN)
Q4 (CEA)
D2 corr

## Slide 13: 3 Crab Cavity prototypes:
Concept of RF Power system
4-rod in SM18 for RF measurements [Lancaster UK]
4-rod prepared for rinsing @ CERN
RF-Dipole Nb prototype [ODU-SLAC]
DQWR prototype (17-Jan-2013) [BNL]

## Slide 14: And excellent results: e.g. RF dipole > 5 MV ¼ w and 4-rods also tested (1.5 MV)
Quench
4.2 K result
2 K result
Initial goal was 3.5 MV however V > 5-6 MV would ease integration
5
JP Delahayen ODU 2013

## Slide 15: Latest cavity designs toward accelerator
RF Dipole: Waveguide or
waveguide-coax couplers
Double ¼-wave: Coaxial couplers with
hook-type antenna
3 Advanced Design Studies with
Different Coupler concepts
HEPAP Accelerator Sub-Panel Road Trip, August 2014
4-rod: Coaxial couplers with different antenna types
Present baseline: 4 cavity/cryomod
TEST in SPS under preparation for 2017
Concentrate on two designs in order to be ready
for test installation in SPS in 2016/2017 TS
Validation with beam operation is vital!!!

## Slide 16: HL-LHC: Main Challenges
Developing new SC magnet technology (Nb3Sn):
> 20 years of dedicated R&D!!
New triplet magnets optimized for >12T and large aperture
New 11T dipole magnets (field quality!)
Developing new SC RF technology:
1989 proposed for KEKB
Elliptical design for KEKB in 1991
Operational in 2007  18 years for elliptical cavity
2001: proposed as an option for HL-LHC
LHC requires compact resonators and excludes elliptical design
2008 validation workshop for HL-LHC
Novel design approaches (double quarter wave resonators and 4-rod)
       welding, rinsing and surface treatment!
Operation in hadron storage ring  noise!!
 > 20 years development time for HL-LHC cavities!
HEPAP Accelerator Sub-Panel Road Trip, August 2014

## Slide 17: LHeC options:
RR LHeC:
new ring in
LHC tunnel,
with bypasses
around
existing
experiments
RR LHeC
e-/e+ injector
10 GeV,
10 min. filling time
LR LHeC:
Straight or
Recirculating
Linac;
RCL with
Energy Recovery
Operation
HEPAP Accelerator Sub-Panel Road Trip, August 2014
17
Oliver Brüning, CERN

## Slide 18: LHeC: Baseline Linac-Ring Option
Two 1 km long SC
linacs in CW operation (Q > 1010)
requires Cryogenic
system comparable
to LHC system!
Super Conducting Linac with Energy Recovery
& high current (> 6mA)
Relatively large return arcs
ca. 9 km underground tunnel installation
total of 19 km bending arcs
same magnet design as for RR option: > 4500 magnets
1033 cm-2 s-1 Luminosity reach | PROTONS | ELECTRONS
Beam Energy [GeV] | 7000 | 60
Luminosity [1033cm-2s-1] | 1 | 1
Normalized emittance gex,y [mm] | 3.75 | 50
Beta Funtion b*x,y [m] | 0.1 | 0.12
rms Beam size s*x,y [mm] | 7 | 7
rms Beam divergence s’*x,y [mrad] | 70 | 58
Beam Current [mA] | 430 (860) | 6.6
Bunch Spacing [ns] | 25 (50) | 25 (50)
Bunch Population | 1.7*1011 | (1*109) 2*109
Bunch charge [nC] | 27 | (0.16) 0.32
1034 cm-2 s-1 Luminosity reach | PROTONS | ELECTRONS
Beam Energy [GeV] | 7000 | 60
Luminosity [1033cm-2s-1] | 16 | 16
Normalized emittance gex,y [mm] | 2.5 | 20
Beta Funtion b*x,y [m] | 0.05 | 0.10
rms Beam size s*x,y [mm] | 4 | 4
rms Beam divergence s’*x,y [mrad] | 80 | 40
Beam Current [mA] | 1112 | 25
Bunch Spacing [ns] | 25 | 25
Bunch Population | 2.2*1011 | 4*109
Bunch charge [nC] | 35 | 0.64

## Slide 19: LHeC: Summary
Challenge SC RF technology:
800 MHz high Q0 cavities for CW op. with high gradient (> 18MV)
Challenge Energy Recovery Technology:
Beam-Beam interaction and parasitic operation to HL-LHC
Positron source
Multi-turn ERL, high energy, high beam current operation
Strong points:
Complementary to HL-LHC  HL-LHC as precision machine
Full exploitation of LHC infrastructure
Higgs production
Moderate cost  intermittent project option
gamma-gamma collider option

## Slide 20
European Strategy for Particle Physics
High-priority large-scale scientific activities
After careful analysis of many possible large-scale scientific activities requiring significant resources, sizeable collaborations and sustained commitment, the following four activities have been identified as carrying the highest priority (the point below is the one relating to very high energy machines)
d) To stay at the forefront of particle physics, Europe needs to be in a position to propose an ambitious post-LHC accelerator project at CERN by the time of the next Strategy update, when physics results from the LHC running at 14 TeV will be available. CERN should undertake design studies for accelerator projects in a global context, with emphasis on proton-proton and electron-positron high energy frontier machines. These design studies should be coupled to a vigorous accelerator R&D programme, including high-field magnets and high-gradient accelerating structures, in collaboration with national institutes, laboratories and universities worldwide.
Output: Post-LHC high energy frontier machines
Notes: Used as motivation/marching orders for FCC (high energy frontier hadrons and high field magnets) and CLIC (high energy frontier e-e+ and high gradient accelerating structures)

## Slide 21: International linear collider
200-500 GeV cm (extendable to 1 TeV)
  L ~ 1.8×1034 cm-2s-1 (@ 500GeV)
  7.8 Billion ILCU + 23 Million p-hrs
>20 years R&D worldwide
  A truly global effort
  Over 2,000 man years
  >300 M$ globally
Cost driver: SRF technology
  17,000 1.3 GHz Nb cavities
  1,800 cryomodules
Mature SRF technology

## Slide 22: ILC - a global project
courtesy: A. Yamamoto (KEK)

## Slide 23
LCLS-II
◉
DESY
◉
LAL/
Saclay
◉
INFN Milan
◉
◉
◉
◉
SLAC
FNAL/ANL
Cornell
JLab
◉
KEK
US and EU (industrial) production and test capacity.
Perfectly placed for start of ILC construction end
of this decade.
Kitakami proposed site
Largest deployment of this technology to date
100 cryomodules
800 cavities
17.5 GeV (pulsed)
US infrastructure for
35 cryomodules
280 cavities
4 GeV (CW)
preliminary data; results are not published

## Slide 24: ILC: Summary
Challenges:
SC RF production [cost]
Accelerating field [energy reach]
Maximum energy (cost): 500 GeV CM (Higgs)  1TeV CM
Positron production
Main strong points:
European XFEL as technology demonstrator
Feedback options

## Slide 25: CLIC
total length (main linac) ~11 (500 GeV) - 48 km (3 TeV)

## Slide 26: Compact LInear Collider (CLIC)
3 TeV cm layout
0.5 TeV: 8,300 MCHF (ℒ ~ 1.4×1034)
Ga ~ 100 MV/m
LC represents a PARADIGM shift
4.2-100A

## Slide 27: Compact LInear Collider (CLIC)
3 TeV cm layout
0.5 TeV: 8,300 MCHF (ℒ ~ 1.4×1034)
Ga ~ 100 MV/m
LC represents a PARADIGM shift
4.2-100A

## Slide 28: CLIC: Main activities and goals for 2018
Physics studies related to energy frontier capabilities and potential new physics as it emerges from LHC
Detector R&D compatible with CLIC specifications
High Gradient structure development and significantly increased test-capacity for X-band RF-structures
System-test programmes in CTF3, at ATF and FACET, as well as system-tests in collaborative programmes with light-source laboratories
Technical systems developments, related among others to complete modules, alignment/stability, instrumentation and power sources
A re-baselined staged project plan, cost and power optimisation, increased industrialisation effort for cost-drivers
Notes: Number 3: high gradient structure, need 8 per 2m, gradient 100 MV/m
Number 4: CTF3 is at CERN, ATF at KEK, FACET at SLAC

## Slide 29: CLIC Summary:
Main Challenges
Power consumption
Cost
Generation and preservation of low emittance beams (alignment)
Collision of beams with nm scale transverse size at the IP
Accelerating field and break down rate
Main strong points
Potential high energy reach: > TeV scale CM energies
Drive beam power concept

## Slide 30
Herwig Schopper, LEP - The Lord of the Collider Rings at CERN 1980 - 2000, Springer 2009
with a foreword by Rolf-Dieter-Heuer
Circular e+/e- Collider Options:
Up to a cm energy of ~350 GeV circular colliders with sc RF provide a competitive option

## Slide 31
ultimate precision
at Z, WW, ZH ;
sensitive to New
Physics in multi-TeV range
ultimate energy reach
up to 1 or 3 TeV ;
direct searches
for New Physics
constant power (≤2 x ILC500)
constant by
Design luminosity vs. energy

## Slide 32: Circular Lepton Colliders: Higgs & more
Ecm 208 GeV
C 27 km
L/ip 0.01×1034 cm-2s-1
Ib 3.0 mA
PSR 22 MW
Ecm 90-350 GeV
C 100 km
L/ip 28-1.7×1034 cm-2s-1
Ib 1450-7 mA
PSR 100 MW
Ready for physics: 2030+ ?
FCC-ee [CERN]
Ecm 240 GeV
C 50 km (80km?)
L/ip 1.8×1034 cm-2s-1
Ib 17 mA
PSR 100 MW
Ready for physics: 2028+
CepC [IHEP]

## Slide 33
Chinese Circular e+/e- Collider
Qinhuangdao (秦皇岛）
50 km
70 km
easy access
300 km from Beijing
3 h by car
1 h by train
Yifang Wang
CepC, SppC

## Slide 34
Parameter | Unit | Value | Parameter | Unit | Value
Beam energy [E] | GeV | 120 | Circumference [C] | km | 50.0
Number of IP[NIP] |  | 2 | SR loss/turn [U0] | GeV | 2.96
Bunch number/beam[nB] |  | 50 | Bunch population [Ne] |  | 3.52E+11
SR power/beam [P] | MW | 50 | Beam current [I] | mA | 16.89
Bending radius [r] | m | 6200 | momentum compaction factor [ap] |  | 4.00E-05
Revolution period [T0] | s | 1.67E-04 | Revolution frequency [f0] | Hz | 5995.85
emittance (x/y) | nm | 6.9/0.021 | bIP(x/y) | mm | 800/1.2
Transverse size (x/y) | mm | 74.30/0.16 | xx,y/IP |  | 0.097/0.069
Beam length SR [ss.SR] | mm | 2.12 | Beam length total [ss.tot] | mm | 2.42
Lifetime due to Beamstrahlung | min | 80 | lifetime due to radiative Bhabha scattering [tL] | min | 53.98
RF voltage [Vrf] | GV | 6.87 | RF frequency [frf] | GHz | 0.7*
Harmonic number [h] |  | 116747 | Synchrotron oscillation tune [ns] |  | 0.196
Energy acceptance RF [h] | % | 5.71 | Damping partition number [Je] |  | 2
Energy spread SR [sd.SR] | % | 0.13 | Energy spread BS [sd.BS] | % | 0.07
Energy spread total [sd.tot] | % | 0.15 | ng |  | 0.21
Transverse damping time [nx] | turns | 81 | Longitudinal damping time [ne] | turns | 40
Hourglass factor | Fh | 0.704 | Luminosity/IP [L] | cm-2s-1 | 1.77E+34
Main parameters for CEPC
*Main ring rf frequency is changed to 650MHz and booster rf frequency is set to 1.3Ghz
The injection linac frequency is chosen 2856MHz

## Slide 35: Comparison of key design parameters
Parameter | LEP2 | FCC-ee |  |  | ILC |  | 
 |  | Z | H | t | H | 500 | 1 TeV
E (GeV) | 104 | 45 | 120 | 175 | 125 | 250 | 500
<I (mA)> | 4 | 1400 | 30 | 7 | 0.000021 | .000021 | .000027
P SR/b,tot [MW] | 22 | 100 | 100 | 100 | 5.9 | 10.5 | 27.2
PAC [MW] | ~200 | ~260 | ~270 | ~300 | ~129 | ~163 | ~300
hwall→beam [%] | ~30 | 30-40 | 30-40 | 30-40 | 4.6 | 6.4 | 9.1
Nbunch/ring (pulse) | 4 | 16’700 | 1’330 | 98 | 1312 | 1312 | 2450
fcoll (kHz) | 45 | 50000 | 4000 | 294 | 6.6 | 6.6 | 9.8
b*x/y (mm) | 1500/ 50 | 500 / 1 | 500 /1 | 1000/1 | 13 | 11 | 11
ex (nm) | 30-50 | 29 | 1 | 2 | 0.04 | 0.02 | 0.01
ey (pm) | ~250 | 60 | 2 | 2 | 0.14 | 0.07 | 0.03
xy (ILC: ng) | 0.07 | 0.03 | 0.09 | 0.09 | (1.12) | (1.72) | (2.12)
nIP | 4 | 4 | 4 | 4 | 1 | 1 | 1
L0.01/IP | 0.012 | 28 | 6.0 | 1.8 | 0.65 | 1.05 | 2.2
L0.01,tot (1034 cm-2s-1) | 0.048 | 112 | 24 | 7.2 | 0.65 | 1.05 | 2.2

## Slide 36: Circular e+/e- Summary:
Main Challenges
Tunnel
SC RF
Short beam lifetime & top-up operation  Super KEKB
Main strong points
Impressive performance track record for circular colliders
Potential synergy (tunnel) with future hh Collider project
Energy reach compatible with Higgs and top physics
Positron source requirements

## Slide 37
 | S-KEKB | SLC | CLIC (3 TeV) | ILC (H) | FCC-ee (H)
e+ / second | 2.5 x 1012 | 6 x 1012 | 110 x 1012 | 200 x 1012 | 0.05 x 1012
e+ source – rate requirements
X 18
X 33
/ 120
L. Rinolfi
ILC e+ source has no precedent; its performance can be verified only after ILC construction (needs >150 GeV e- beam)
ILC e+ source design

## Slide 38: HE-LHC:
2-GeV Booster
Linac4
SPS+
HE-LHC
20-T dipole magnets
higher energy
transfer lines

## Slide 39: HE-LHC and high energy hh Collider
HE-LHC
Use of existing tunnel infrastructure!
Can perhaps bring a factor 2-3 increase in CM collision energy
Magnet technology (15 T – 20 T)?!?
Investment (time & money) versus physics case?!?!
FCC-hh: High Energy Hadron Collider in larger tunnel
Still at early R&D and study stage (16T - 20 T magnets?)
(magnets, beam power and machine protection, injectors...)
New tunnel would provide synergies with other machines
(e.g. FCC-ee as a Higgs factory)

## Slide 40: FCC:
FCC-hh
20-T dipole magnets
FCC-ee

## Slide 41
Future Circular Collider (FCC) study ; goals: CDR and cost review for the next European Strategy Update (2018)
International collaboration :
pp-collider (FCC-hh)  defining infrastructure requirements
including HE-LHC option: 16-20 T in LHC tunnel
e+e- collider (FCC-ee/TLEP) as potential intermediate step
p-e (FCC-he) option
100 km infrastructure in Geneva area
~16 T  100 TeV in 100 km
~20 T  100 TeV in 80 km
M. Benedikt

## Slide 42
2014 |  |  |  | 2015 |  |  |  | 2016 |  |  |  | 2017 |  |  |  | 2018 |  |  | 
Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4
Kick-off, collaboration forming,
study plan and organisation
Release CDR & Workshop on next steps
Workshop & Review
 contents of CDR
Workshop & Review identification of baseline
Ph 2: Conceptual study of baseline “strong interact.”
Workshop & Review, cost model, LHC results  study re-scoping?
Ph 3: Study
consolidation
Report
Prepare
4 large FCC Workshops distributed over participating regions
Ph 1: Explore options
“weak interaction”
FCC global design study – time line
  presently discussions with potential partners (MoUs)
  first international collaboration board meeting at CERN on 9 & 10 September 2014
M. Benedikt

## Slide 43
FCC WBS top level
preliminary
M. Benedikt
> 600 work units

## Slide 44: Chinese Accelerator based High Energy Physics:
BEPC II
LC
BEPC
History of BEPC and BEPC II
CEPC+SppC
CEPC: Ecm=240GeV e+e- Circular Collider
SppC: Ecm=50-100TeV pp Collider
HIEPAF: High Intensity Electron Positron Accelerator Facility
CEPC+SppC will be constructed with international collaboration and participation

## Slide 45: Strategy on Future High Energy Colliders of China:
1) On “The 464th Fragrant Hill Meeting”, Chinese High Energy Physics Community arrived at the following consensus:
a) China supports ILC and will participate to ILC construction
with in-kind contributions and requests R&D fund from government
b) After the discovery of Higgs, as next collider after BEPCII in China, a circular e+e- Higgs factory（CEPC）and a Super proton-
proton Collier (SppC) afterwards in the same tunnel is an important option and historical opportunity.
2) During the meeting of Chinese High Energy Physics Association on “China High Energy Physics based on Particle Accelerators”, Feb. 28, 2014, it was concluded that:“Circular e+e- Circular Higgs Factory(CEPC) +Super pp Collider (SppC) is the first choice for China’s future high energy physics accelerator.
International collaboration and participation are necessary for implementation of the larger tunnel option and the SppC

## Slide 46
Time Line Summary:
1980
1990
2000
2010
2020
2030
2040
LHC
Constr.
Physics
Proto.
Design,
R&D
HL-LHC
Constr.
Design,
R&D
LHeC/SAPPHiRE?
Constr.
Physics
Design,
R&D
Physics
SppC/
FCC-hh FCC-he
Constr.
Design,
R&D
CepC/
FCC-ee
Constr.
Physics
Design,
R&D
Physics
Constr.
Design, R&D
ee
Constr.
Physics
Design, R&D
Physics
ILC
CLIC

## Slide 47: Muon Collider Concept:
Proton source:
Up to 4 MW,
with 2±1 ns long bunches
Goal: Produce a high intensity m beam whose 6D phase space is reduced by a factor of ~106 from its value at the production target
Collider up to 6-10TeV 2 detectors:
√s = 3 TeV
Circ: 4.5km L = 3×1034 cm-2s-1
Fast acceleration mitigating muon decay
M.A.Palmer: Muon Accelerators for High Energy Physics Applications: nSTORM, NuMAX & Beyond…
MC on FNAL site

## Slide 48: Muon Colliders: extending high energy frontier
Circular
Muons
Linear
FCC 80-100km
Multi-TeV lepton collider (≤10 TeV cm)
No beamstrahlung
 superb energy resolution
No synchrotron radiation
 relatively small footprint (but no damping!)
Possibilities for cost and MW savings
Challenges: MANY!
J.P.Delahaye, IPAC14

## Slide 49: Summary Common Key R&D Areas and Challenges
Developing new SC magnet technology (Nb3Sn):
> 20 years of dedicated R&D!!
New triplet magnets optimized for >12T and large aperture
New 11T dipole magnets (field quality!)
Developing new SC magnet technology (Nb3Sn):
> 20 years of dedicated R&D!!
New triplet magnets optimized for >12T and large aperture
New 11T dipole magnets (field quality!)
Both R&D Areas have potential
impact beyond HEP
(e.g. SC-RF for High Power p-Linacs and SC magnets for medical applications etc.)
➜ Global Technology Needs with very large lead times!

## Slide 50: Sergei from Quo Nhon

## Slide 51: PP colliders – HF SC Magnets
courtesy: L. Rossi (CERN)
13

## Slide 52: SC Magnet Technology
First the SC cable, then the magnet
Nb3Sn
  HL-LHC with 11-12T
  16 T for HEP
  Almost a commodity!
    15-20 t per year for MRI
    ITER needs 500 t
  ca x5 cost LHC Nb-Ti
HTS (needed  20 T)
 on going R&D!
  Bi-2212: cost today 2-5x Nb3Sn
  YBCO: cost today 10x Nb3Sn
source: L. Rossi

## Slide 53: Beautiful Place for a Science Center
Best beach & cleanest air
Summer capital of China
Starting point of the Great Wall
Wine yard

## Slide 54: LHeC Design Challenges:
54
Ring-Ring:
Maximum beam energy & L are limited by SR radiation power
 ca. 100 MW for a luminosity of L = 5 1033 cm-2 s-1 @ 60 GeV
Linac-Ring:
Maximum beam energy & L are limited by beam power
 > 1000 MW for a luminosity of L = 1034 cm-2 s-1 @ 60 GeV!!!!
Recirculating Linac with Energy Recovery operation!!!
  Multiple use the SC RF structures (a la CBAF @ JLab)
  Decelerate the beam after collisions in the same structures to recover the beam energy  the SC RF acts as a storage unit for the beam power.
  The beam is dumped only at low energies and the beam power can be transferred to the next beam passing through the linac!