## Slide 1: Mu2e CD-2 Review Extinction Monitoring
Peter Kasper
L4 Manager for the Extinction Monitor
10/22/2014

## Slide 2: Extinction Monitor Requirements
Monitor the extinction of beam hitting the target.
  That is the final extinction of interest to the analysis
  Out of time beam that misses the target does not easily produce background tracks
Requirements are discussed in Mu2e-DOC-894
  Should be operating at all times during data acquisition.
  Data should be available for online monitoring.
  Data must be synchronized to the spill, so time evolution of out-of-time beam can be studied.
  Should measure the proton pulse characteristics in addition to the extinction.

## Slide 3: Extinction Monitor Requirements (cont’d)
From Mu2e-DOC-894:
Specification | Value
Sensitivity (90% C.L.) | 10-10
Extinction accuracy | 10%
Integration time | 6×1016 POT (~3 hours at design intensity)
Timing resolution (RMS) | <10 ns
Dead-time | <10 ns
Rate-dependent error over dynamic range | <10%
Initial readiness | When the production target is ready
Access time (assuming monthly access is needed) | 4 hrs
Radiation hardness (minimum protons delivered before replacement is required) | 4×1020 POT

## Slide 4: Principle of Operation
Since we are only interested in protons hitting the target we monitor the rate of secondary particles produced by interactions on the target
With ≈ 3 x 107 protons/bunch it is not possible to measure a 10-10 extinction with a single bunch, nor is it feasible to count every proton.. Hence we must integrate over many bunches.

## Slide 5: Principle of Operation … Filter + Detector
Filter
  Selects a sample of suitable secondary particles and delivers them to the detector
  Sets the per proton signal rate in the detector
  Shields the detector from unwanted interaction products
Detector
  Measure “in-time” and “out-of-time” signal rates with equal or known relative efficiency
  Must have LOW “out-of-time” backgrounds compared to “out-of-time” signal rate

## Slide 6: Location
Detector room is located above and behind the beam dumpz
Target
(too small to see)
Production solenoid
Proton absorber and extinction monitor filter
Detector Room
3D model courtesy of Bartoszek Engineering

## Slide 7: Filter Layout
Primary beam absorber
Exit collimator
Filter magnet
Entry collimator
Detector room

## Slide 8: Filter Design
Locates detector outside target hall
  Easy access for detector maintenance
  Lots of room for shielding
  Low radiation levels for detector + electronics
Entry collimator
  Located in concrete above the primary beam dump
  Admits forward produced high momentum secondaries
Filter magnet
  Permanent dipole oriented to transmit ~4.5 GeV/c secondaries
Exit collimator
  Admits signal particles through a 2m thick shield wall

## Slide 9: Pixels: the Basis of the Measurement
High granularity
  Atlas style FE-14 sensor chips with 26,880 pixels per chip
  Pixel size is 250 x 50 μm
  4 upstream planes with 4 x 3.5 cm active area
  4 downstream planes with 4 x 5.1 cm active area
Low Noise
  Signal/noise = 15,000 / 121 electrons
Radiation hard to 300 Mrad (expect <1 Mrad/yr)
Huge cost saving by “piggy-backing” on LHC R&D and production

## Slide 10: Detector Magnet
Magnet
  Permanent dipole 0.14 T.m.
  Main purpose is to prevent electrons produced in stopped muon decays from forming tracks

## Slide 11: Trigger Counters
6 fast scintillator counters
  Provide a trigger for the pixels
  Also measure the time structure of the beam
Location of upstream trigger counters with respect to the pixel planes
The layout downstream of the magnet is a mirror image of the upstream

## Slide 12: Muon ID Detector
Added in response to the down select review (discussed shortly)
Measures the muon content of the extinction signal
Muon content expected to be small for a real signal but backgrounds from cosmic rays or from interactions upstream of the production solenoid will be largely muons

## Slide 13: Performance … Sensitivity
To set a 90% CL upper limit of 1x10-10 extinction after 6x1016 POT requires a signal rate of 5x10-7 tracks/POT
The expected rate of 8.3x10-7 tracks/POT (≈ 25 tracks/bunch) meets this requirement
Background (cosmics, noise, etc) < .03 tracks/hour
  ~ .1 track/(6x1016 POT)
  ~ 2x10-12 extinction
  this can be measured and subtracted!
Track distributions surviving filter
p
π

## Slide 14: Performance … linearity
The track reconstruction efficiency is expected vary by < 1% over a generous range of bunch intensities
The linearity requirement of 10% is comfortably met.
Track reconstruction efficiency:

## Slide 15: Changes since CD-1
At the time of CD-1, we were considering two possible designs for the monitor:
  The pixel-tracking based design presented here.
  A design proposed by UC Irvine, based on scintillators
An independent review committee was appointed by the spokespersons
The committee concluded that both designs could in principle satisfy the specification, but that the pixel-based design entailed lower risk.
The “Muon catcher” calorimeter was also added to this design to measure the muon content of the out of time signal as a test for false positives.

## Slide 16: Quality Assurance
The most important issue in the construction is alignment, which will be monitored continuously throughout the civil construction and detector installation tasks.
Fabrication will be largely subcontracted, and will adhere to the subcontractor requirements in the “Fermilab Quality Assurance Plan”.
The pixels themselves will be qualified according to the standard ATLAS quality control procedure
  (See JINST Vol 7. p. 11010 (2012)).

## Slide 17: ES&H
The external monitor will not be accessible during operation, but simulations show there will not be any significant activation present when beam is off.
The target hall will however, not be easy to access and hence the entry collimator has been designed so that any necessary alignment adjustments can be done from the downstream end
Alignment cams
Cam shaft
Gear boxes

## Slide 18: Summary
We have designed an extinction monitoring system that meets the requirements of the Mu2e experiment.
We are confident that we have met the requirements for CD-2 approval of this system.
  Preliminary design complete
  Project ready to baseline