## Slide 1: Mu2e Tracker Electronics
Vadim Rusu
Front End Electronics L3 Manager
10/22/2014

## Slide 2: Outline
Requirements
Design and Implementation
Prototypes
Cost

## Slide 3: Electronics requirements
Amplification and digitization of the straw signals
Transmit the digitized data to DAQ
Record both ends of the straw (time division – 3cm resolution)
Measure pulse height for dE/dx
Supply HV to anode wires (and HV disconnect)
Run triggerless mode (soft trigger may be implemented at the DAQ level)
B field perturbation <1G in the active region
Rad hard (2×1012 n/cm2)
10kW power
<12×96 dead channels in 5 years at 90% CL

## Slide 4: Tracker Front End Scheme

## Slide 5: Tracker Front End Scheme
Preamp
475.06.04.01
Digitizer
475.06.04.02
ROC
475.06.04.03

## Slide 6: Implementation
Entire electronics chain implemented in commercially available components
  Reduced risk
  Reliable cost estimates (manufacturer quotes and catalog)
  Upgradeable (ride technology wave)
  Flexibility
    All key functionalities implemented in FPGAs
    Reconfigurable

## Slide 7: Preamp requirements
Bandwidth 100-300MHz
Typical electron pulse >5x noise floor
Dynamic range x10 typical electron pulse
  Clip larger pulses to avoid x-talk downstream from large proton pulses
Shaping – return to baseline <200ns
  >50% efficiency for typical electron pulse after a typical proton pulse
>100kOhm R from the HV bus
  <1nA leakage through blocking capacitor
  HV remote disconnect
Doc-db 3879

## Slide 8: Preamp implementation
41472 preamps (2x straws)
Small/simple PCBs at the end of the straw
Low power (~15mW)
Configurable gain and threshold
Input stage
  Low noise/high fT SiGe technology discrete BJT
  Active 300Ohm termination to avoid reflections
  ESD Transient protection
Output stage
  Differential output (good CMRR avoids ground loops)
  Termination and pull-up at digitizer input
Advanced stage of prototyping
Mukherjee/V. Rusu
FNAL

## Slide 9: Preamp performance
250MHz -3dB point
2mV RMS output noise
10mV typical electron pulse response
Dynamic range 150mV
~50ns shaping time

## Slide 10: Digitizer requirements
<70ps ΔT resolution (time division)
1ns drift time resolution
  1700ns range (at least a microbunch)
7 bits ADC resolution
  X10 typical electron pulse range
50MS/s sampling rate
LVDS data to ROC (200Mb/s line)
  Data to ROC
    Header, 2x TDC, 8 ADC samples
150mW/straw
Doc-db 3879

## Slide 11: Digitizer scheme
Doc-db 4085
J. Wu/V. Rusu
FNAL

## Slide 12: Digitizer implementation
41472 TDC channels and 20736 ADC channels
Commercial off-the-shelf components
  Fast comparator and shaper
  ADC (Maxim19527)
  “TDC in FPGA”
Digitizer PCB
  16 straws/digitizer
Advanced Prototype
Doc-db 4085

## Slide 13: Digitizer performance
Test bench measurements
Doc-db 4085

## Slide 14: Readout Controller Requirements
Received data from Digitizers
Buffering
  Continue data transfer in inter-spill time
Transmits to DAQ
  230Mbps each ROC to DAQ
Relies slow controls to front-end
  Preamp settings
  HV control (fuses)
  Monitor environmental variables
Doc-db 3973

## Slide 15: ROC Implementation
SmartFusion FPGA (rad hard line from Microsemi)
DDR3 on board for buffering
2.5 Gbps full-duplex fiber optics
  Ring architecture
Advanced prototype
Doc-db 3973
U of Houston – E. Hungerford
FNAL - G. Deuerling

## Slide 16: ROC/Digi Prototype
Successfully established comm between ROC and digi
LVDS data received on the ROC FPGA
  USB readout – almost ready to try optical fiber

## Slide 17: Assembly
Tight fit, but it does fit.
ROC
DIGITIZERS
TRANSCEIVERS

## Slide 18: Infrastructure (Signal transmission)
Investigated a long (55’’) motherboard
  Recommendation from Digitizer Review (April 2014)
  Cost ineffective (+high assembly costs)
Preamp mobo + ROC mobo
  Effectively a transmission line board(s)
    All components (preamp, digi, ROC) mezzanines
    HV, slow controls on board

## Slide 19: Transmission boards
Rice U.
M. Corcoran
T. Nussbaum

## Slide 20: Assembly

## Slide 21: Infrastructure (Power distribution)
Five low voltage levels needed (<5V)
48V power line from outside the cryostat
  Allows for lower current (B field)
DC-DC converters outside the stations step down to a suitable voltage
Regulators inside the gas volume for actual distribution

## Slide 22: ES&H
  High voltage is moderate by Fermilab standards 1500V, <1mA and ~10mJ stored energy on any one line
  Power is from 48V supplies which have passive (limited capacity) and active (monitor and trip) current limit

## Slide 23: Cost Table
 | Base Cost (AY K$) |  |  | Estimate Uncertainty (on remaining costs) | % Contingency on ETC | Total Cost
 | M&S | Labor | Total |  |  | 
475.06 Tracker |  |  |  |  |  | 
475.06.04 Tracker Front End Electronics |  |  |  |  |  | 
475.06.04.01 Preamp | 563 | 98 | 661 | 216 | 35% | 877
475.06.04.02 Digitizer | 793 | 387 | 1,180 | 255 | 26% | 1,435
475.06.04.03 Readout Controller | 316 | 88 | 403 | 161 | 42% | 564
475.06.04.04 Test Stands | 4 | 19 | 23 | 11 | 145% | 34
Grand Total | 1,676 | 591 | 2,267 | 643 | 32% | 2,910

## Slide 24: Cost Breakdown
Base Cost (AY K$)
Chart: 
| 475.06.04.01 Preamp | 475.06.04.02 Digitizer | 475.06.04.03 Readout Controller | 475.06.04.04 Test Stands
Total | 660739.5449 | 1180157.6746 | 403065.2172 | 22934.9453
Chart: 
| L Labor | M Material | N Non-Fermi Labor
Total | 590606.4677 | 1614632.572 | 61658.3423

## Slide 25: Quality of Estimate
Chart: 
| L1 Actual / M1 Existing P.O. | L3 / M3 Advanced | L4 / M4 Preliminary | L5 / M5 Conceptual
Total | 178883.0905 | 702538.4181 | 383700.1969 | 1001775.6765
Base Cost (AY K$)

## Slide 26: Labor & Material by FY
Chart: Annual Cost $K
| 42277 | 42643 | 43008 | 43373 | 43738
L Labor | 39797.7137 | 15330.0812 | 0 | 15070.4148 | 214006.1087
M Material | 23828.2642 | 23949.3328 | 114250.608 | 1353381.7812 | 0
Non-Fermi Labor | 0 | 0 | 0 | 9018.3165 | 17467.3581
Cumulative Total | 504423.3807 | 543702.7947 | 657953.4027 | 2035423.9152 | 2266897.382
Base Cost (AY K$)

## Slide 27: Labor Resources by FY
Chart: Annual FTE's
| 42277 | 42643 | 43008 | 43373 | 43738
AD Administrative | 0.0011 | 0.0181 | 0.081 | 0.0366 | 0
EN Engineering | 0.0142 | 0 | 0 | 0 | 0
ES Environmental, Safety & Health
FM Facilities Management
IT Information Technology
SC Scientific | 0.1499 | 0.0198 | 0 | 0 | 0
TE Technical | 0.1472 | 0.0906 | 0 | 0.1721 | 1.3824
Cumulative | 0.1652 | 0.2031 | 0.2841 | 0.3207 | 0.3207
FTEs by Discipline

## Slide 28: Conclusion
Design of front end electronics meets the requirements
Advanced prototypes on all sub-systems
Initial integration pass under way
Solid cost estimate based mostly on quotes

## Slide 29: Backup

## Slide 30: TDC Using FPGA Logic Chain Delay
This scheme uses current FPGA technology
Low cost chip family can be used. (e.g. EP2C8T144C6 $31.68)
Fine TDC precision can be implemented in slow devices (e.g., 25 ps (RMS) in a 400 MHz chip).
IN
CLK

## Slide 31: Autocalibration using histogram method
It provides a bin-by-bin calibration at certain temperature.
It is a turn-key solution (bin in, ps out)
It is semi-continuous (auto update LUT every 16K events)
In (bin)
LUT
S
Out (ps)
16K
Events
DNL
Histogram