## Slide 1: Fabrication and Quality Control of the Frequency Tuner for the XFEL
Lutz Lilje
DESY
Tuner meeting - ILC / Fermilab / LCLS-II Monday 13 October

## Slide 2: Outline of the talk
Steps towards industrialisation
  Mechanics
  Motor drive
  Piezo system
Current status
Disclaimer:
  No details on Piezo amplifier or motor driver electronic given here
  Developments well on-track by LLRF WP and DESY groups MSK and MCS

## Slide 3: Tuner Scheme
Current design in use at FLASH
  Original design by CEA
  Fast piezo detuning introduced by DESY
Design by M. Maurier and P. Leconte based of the MACSE tuner design (CEA Saclay)
DLscrew
DLarms
DLcavity

## Slide 4: Tuner Parts: Overview
Mechanics
Drive Unit
Piezo System

## Slide 5: Challenges for industrialisation: Mechanics
Mechanics supplied by CEA
  Adapted to local supplier in France
Cost reduction
Material quality
  Steel with low permeability needed
Therefore
  Prototypes with companies experienced in mass production of precision machined pieces (for Airbus etc.)
Conclusions
  Several simplifications on the detailed drawings
  Relaxed tolerances to reduce cost for precision machine time
  Good basis for a successful call for tender

## Slide 6: Industrial fabrication of mechanics
Contract awarded to Astro- und Feinwerktechnik, Berlin
  Minor adaption of drawings
  After initial problems with material smooth production
Quality control
  Agreement on ‚essential‘ measures
  Pre-series completely cross-checked at DESY
  Piezo fixture incoming check at Piezo company
  QC protocols delivered into DESY EDMS system by company
Delivery
  Pre-assembled state
    Allows for additional cross-check of completeness

## Slide 7: Challenges for industrialisation: Motor and gear box
Basic idea from CEA: Step motor and harmonic drive
  Initial tests failed due to insufficient coating
    Lubrication under cold vacuum conditions tricky
  DESY in-house development on coatings
    Parts purchased via different sources
    Integration/Assembly at DESY
  Second motor supplier came into play later than expected
    Cold testing possible at vendor
Therefore:
  Training for at least two companies to deliver complete and tested drive units:
    Motor, gear box, thread with nut
    Test temperature liquid nitrogen, units under load
  Use prototyping phase
Conclusion
  Both vendors were capable to fulfill XFEL requirements
    E.g. Life-Time

## Slide 8: Industrial fabrication of drive unit
Contract awarded to Harmonic Drive, Limburg
  Minor adaption of drawings
Quality control
  Agreement on few ‚essential‘ mechanical measures
  Room temperature and at liquid N2 temperature tests
    Record current when
      Beginning of movement
      Loss of steps
      Total number of steps
  QC protocols delivered into DESY EDMS system by company
Delivery
  Delivered in a sealed bag including disseccant and humidity indicator

## Slide 9: Challenges for indutrialisation: Piezo system
DESY development with several iterations
  Guaranteeing sufficient pre-load for piezos
  Avoid loose piezos under all operation conditions
    Change of pre-tuning of cavities
Assembly ‘hand-crafted’ at DESY
No burn-in tests
  One special case of failure at initial operation suspected
    Not fully conclusive data
Therefore:
  Require companies to
    Further improve radiation resistance (ETFE cabling)
    Respect vacuum compatibility
    assemble piezo systems
      More than buying piezos only
      Use experience of piezo companies for assembly
    perform burn–in test
      Room-temperature considered sufficient
  Implementation in series production

## Slide 10: Industrial fabrication of Piezo System
Contract awarded to PI, Karlsruhe
  PI Ceramics for Piezo elements
Design improved of drawings
  Avoid local stresses on piezos by optimising the plates used for pressing the piezo elements
    Increases thickness
    Definition of surface quality
  Better fixation of the wiring

## Slide 11: Industrial fabrication of Piezo System
Quality control
  Burn-in test after assembly
    DC test
      100 % of nominal voltage for 2 hours
    AC test
      Voltage:100% of nominal piezo voltage
      Pulse length:Sinusoidal Half Wave of 1000 Hz
      Rep rate: 100 Hz
      Number of Cycles: 1 Million
    After the tests the following parameters should be measured
      Capacitance
      Stroke
      Leakage current at nominal voltage
  QC protocols delivered into DESY EDMS system by company

## Slide 12: Status of the System Components
Mechanics:
  Series fabrication finished. Delivery completed
    721 normal + 103 mirrored units
    Minor problems with tolerances
Drive unit:
  Documentation reports decided.
  More than than half of all units have FAT and been delivered to CEA and DESY.
    588 normal and 84 mirrored
Piezo system:
  Continuing tests of permanent FLASH setup.
  Series production of fixtures completed.
    824 units
    3 Piezos (of 1600) failed the FAT and were replaced by the company
QC testing during module installation at Saclay (INFN contribution).
Documentation in EDMS continues.

## Slide 13: If I had had time, …
… what would be different?
Piezo
  Design improved for mechanical robustness
  Kept overhead in voltage
  Position of the piezo?
  T-sensor?
Mechanics
  Nothing in the design
  Assembly procedures and training of personnel
Drive unit
  More lifetime testing
  T-sensor?

## Slide 14: Thanks!
Several people contributed with support and measurments to the work presented here:
R. Paparella, A. Bosotti, C. Albrecht, K. Jensch, O. Keller, K Przygoda, M. Grecki, C. Müller and many more also within the S1 Global Test at KEK