## Slide 1: Lessons Learned from SNS tuner SNS Tuner Harmonic Drive Failures
October 13, 2014
Matt Howell
SNS/ORNL

## Slide 2: SNS Tuner Design
Adapted from Saclay-TTF design for TESLA cavities mounted to helium vessel operating through a bellows
Actuated by a cold stepping motor through a harmonic drive
Piezo tuners included to compensate for Lorentz force detuning of cavities
  Never actuated in operation
  No unexpected large mechanical resonance witnessed
Tuner
Helium Vessel

## Slide 3: Where are the “weak” points?
Failure points exist at the harmonic drives, stepper motors, and Piezo stacks

## Slide 4: Types of Tuner Failures at SNS
Stepper motor and harmonic drive failures
Piezo stack failures
Irregular or excessive vibration

## Slide 5: Harmonic Drive operating principle

## Slide 6: Harmonic drive failures
Wear on the harmonic drive is caused by
  Normal wear and tear from operation
  Component installation issues where the teeth of the harmonic drive are only partially engaged
  Stepper motor failure
  Indicated by
    Inability to move tuner
    Excessive or irregular vibration in RF measurement of cavity

## Slide 7: Tuner motion before and after cavity vibration
Cavity operating at 13 MV/m with stable tuner
After winter shutdown, vibration occurs and results in reduced gradient
Eacc
Tuner motion

## Slide 8: Excessive or irregular vibration
Irregular vibration in this case
  Sometimes excessive vibration is present and sometimes not
  When excessive vibration, forward power required is higher without beam than with beam (3-5 kHz detuning)
In other cases, excessive vibration witnessed
  Vibration is constantly present
Observed from three cavities so far
Normal LFD
Excessive LFD

## Slide 9: Piezo tuner failures
Original installation of Piezo stack did not include a weld
Pressure fluctuations in Linac caused mechanical failures
  2 to 4K transition
  Upset conditions
Replaced with typical mechanical stand off
Stitch Weld

## Slide 10: Operational strategy based on previous failures
Tuners are tested before and after every 2K to 4K or 4K to 2K transition
Approximately 20 tuner repairs have been performed at SNS
Access ports allow in-situ repair of tuners in tunnel
Vibration monitoring with RF
Alignment
Bigger vibration and/or more frequent tuner motion lower gradient detune/turn–off.