## Slide 1: Ideas for a Muon Beam Monitor
W.Baldini, M. Fiorini
Ferrara University and INFN

## Slide 2: Overview
Past Experiences with fiber detectors:
  E835 @ FNAL
  Channeling
  SuperB
    The IFR Prototype and its test @ the FTBF
    SiPMs Irradiation Tests
Possible ideas for the Beam Monitor
  The Layout
  Challenges..
Discussion

## Slide 3: E835 at FNAL: Charmonium Spectroscopy

## Slide 4: E835 at FNAL
E835 was a fixet target experiment which studied the Charmonium spectroscopy at the antiproton accumulator
Antiproton on a gas jet-target and a non magnetic spectrometer to mainly detect the electromagnetic decays.
A SCI-FI detector was built by the Ferrara Univ. and FNAL to measure the polar angle q with a resolution of ~ 1mrad
The readout was through VLPCs

## Slide 5: Beam profile monitor for Channeling experiments

## Slide 6: H8-RD22 (then UA9) Experiment at CERN
Experiment to study channeling and volume reflection phenomena on bent silicon crystals
Initially in extracted line at the CERN SPS
Then application to collimation in the SPS and LHC
Used different beam types:
  protons
  pions
  electrons
  ions (planned)

## Slide 7
Beam profile monitor (1)

## Slide 8
Beam profile monitor (2)

## Slide 9
Beam profile monitor (3)

## Slide 10: The SuperB Muon Detector

## Slide 11: The SuperB Muon Detector
Part of the SuperB apparatus is the Instrumented Flux Return (IFR): the outer most detector for the identification of muons and neutral hadrons
Superconducting solenoid iron yoke instrumented with fast scintillators to cope with high flux of particles (~ few 100 Hz/cm2)
It is composed by a Central Barrel and two movable Endcaps
Each part consists of 92cm of Iron interleaved by 9 active layers of segmented scintillator
5/10cm scintillator bars readout through 3 Wave Length Shifter fibers (WLS) and Silicon Photo-Multipliers (SiPM)
The Instrumented Flux Return
Barrel
Backward Endcap
Scintillator – Iron segmentation
Forward Endcap
Particle

## Slide 12: The IFR Readout Technique
The active modules are the assembly of two layers of orthogonal scintillator bars:
  5 cm bars in each direction for the Endcaps
  10cm bars in the transverse direction for the Barrel
Each scintillator bar is readout through 3 Wave Length Shifting Fibers housed into surface grooves
The three fibers bring the light signal to a custom shaped Silicon Photo Multiplier
Each bar is Digitally readout through custom made Front End electronics
Scintillator
WLS fibers
SiPM

## Slide 13: The beam test at Fermilab
The FBTF
The “SuperB
group”
Photos by R.Malaguti
The DAQ & Trigger “scheme”
The prototype

## Slide 14: The IFR Prototype: Design and Construction
9 Active Layers
Full depth prototype: 60x60x92cm3 of Iron interleaved by 12 slots to house the active layers
12 slots: Possibility to house the 9 active layers in different positions to test different iron-scintillator configurations
Possibility to test another readout solution (TDC) and to compare different SiPMs and WLS fibers:
  4 Time Readout (TDC-RO) “standard “
  4 Binary Readout (BiRo) “standard”
  4 special modules to study different fibers and SiPM geometry
Iron

## Slide 15
Labeling and collecting
the fibers around the supports
Fill with optical glue
the embedded holes
Fill the machined grooves
with optical grease and cover it with stripes of reflecting aluminum (BiRo only)
Put double-side adhesive
to fix the second layer
(BiRo only)
Various assembling steps
of the active layers

## Slide 16: The Beam test of the Prototype
Active modules housed in light tightened boxes ( Pizza Box)
  4 Time Readout modules
  4 Binary Readout modules
  4 special modules to study
different fibers or SiPM
geometry
First Test in Dec. 2010 at the Fermilab Test Beam Facility with muon/pion (4-8GeV)
Active Layer
(“pizza box”)
A detector prototype has been built to test the technology on large scale and to validate simulation results
Iron: 60x60x92 cm3, 3cm gaps for the active layers
Up to 9 active layers readout together (about 230 independent electronic channels)
The prototype at the Fermilab
Beam Test Facility

## Slide 17: Beam Test Main Results: Detector Performances
Layers 0,2,4,6,8 Binary Readout, various fibers length (from 110cm to 370 cm )
Layers 1,3,5,7 Time Readout, SiPM on both ends of the scintillator, fibers length: 400cm. This option was eventually discharged
Thresholds: 3.5 p.e.
Very good efficiencies: ≈ 95%
Layer 0
Layer 8
Side view of the Prototype

## Slide 19: SILICON PHOTO MULTIPLIERS
SiPMs are semiconductor photo detectors composed by a matrix of Geiger Mode Avalanches Photo Diodes (GMAPD)
The output signal is the sum of the charge produced by each fired pixel.
These devices can be custom shaped

## Slide 20: The Sci-Fi with SiPM Readout Technique
The Scintillanting Fibers technique, readout through Silicon Photo Multipliers has many interesting aspects:
  Very fast: time response of few ns
  Cheap:
    fibers: few $/m,
    SiPM: < 50 $/each
  Compact: tipically 1x1 mm2
  No need for HV or Gas:
    Typical Vbias: < 100V
  Many producers:
    Hamamatsu
    SenSL
    AdvasiD
  Quality rapidly improving

## Slide 21: The Sci-Fi with SiPM readout Technique (II)
They do have a few drawbacks though:
  Relatively high dark noise (~ few 100kHz)
  RADIATION DAMAGE
We performed an extensive irradiation campaign to study the radiation damage:
  Frascati Neutron Generator (ENEA-Rome) in 2009
  GELINA (Geel, Belgium)
  Louvain La Neuve (Belgium)
Louvain
GELINA

## Slide 22: Radiation Effect at a Glance
The radiation damage is very clear looking at the dark noise:
Before irradiation
5 x 108 neq/cm2
5 x 109 neq/cm2
5 x 1010 neq/cm2

## Slide 23: Dark Spectra vs Dose
Before irradiation
5 x 108 neq/cm2
5 x 109 neq/cm2
5 x 1010 neq/cm2

## Slide 24: Different Manufacturers
PRELIMINARY

## Slide 25: First Ideas for the Beam Monitor
The general Layout could be the usual Scintillating Fiber + SiPMs readout scheme:
SiPM
Front End
Electronics
Various options:
  Fiber:
    250 mm diameter
    500 mm
    1 mm
  SiPMs:
    Pixel size (10, 15, 20, 25, 50 … mm)
    Active area (depending on Fiber diameter)
Tipically fibers are glued on a precisely machined plastic support (e.g. plexiglas)
Beam
Scintillating
Fibers

## Slide 26: Very rough estimates…
Usually fiber detectors are hit by ONE particle per fiber and per event.
Here is more “interesting”, as we expect:
  105 Muons in 120ns  ≈ 103 /nsec in a few cm of diameter
  (very) roughly speaking we expect something of the order of:
  75 muons/fiber/ns in a 250mm fiber
In a 250mm fiber we expect ≈ 5-10 p.e./particle, in linear approx. ≈750 p.e.
For 1mm fibers few 1000 p.e. …
rather challenging also for the Readout electronics
very interesting, not many studies on this topic in
literature

## Slide 27: Interesting points
Does the scintillating material show saturation effects?
  light yield of fibers
  transmission of the light
  … ?
can SiPMs deal with such a high photon flux per unit surface (we need small pixels: 10-15mm)
a challenge for the Readout Electronics (very high dinamic range)

## Slide 28: Discussion
minimum-maximum number of particle to be detected
R&D done with beam of increasing intensity to observe saturation effects: when the beam will be available? (in reasonably controlled conditions)
timescale of the project
space constraints
is there a material budget to be respected
Any constraint in the type of material

## Slide 29: Backup slides

## Slide 30: Temperature Effects
It’s well known how well the SiPM gain, current and rates depend on the temperature.
Especially the MPPC can be largely affected by temperature variation.
Current vs dose
for a 3x3mm2 MPPC
temperature variation cancels the neutron effect
Temperature was monitored but no bias correction has been applied during the test.
Temperature vs time