## Slide 1: CRAB cavities Tuner design and status
Kurt Artoos
  ( (CERN) Rama Calaga, Ofelia Capatina, Teddy Capelli, Federico Carra, L. Dassa, Norbert Kuder, Raphael Leuxe,
  P. Minginette
  Colleagues USLARP , STFC
  Remark: pretuning sensitivity DQW rectified in slides after meeting

## Slide 2: Contents
Tuning principle
DQW and RFD Tuning forces, stress and range
DQW pre tuning
Status SM18 tuner
Studies SPS tuner

## Slide 3
Symmetric actuation on cavity through tuner frame and concentric tubes. Motorization outside cryostat
Centre of the actuation is floating
DQW : 186 kHz/mm *
S. Vérdu Andrés
RFD : 345 kHz/mm *
H. Park
* Measured as tuner stroke or Δdistance between 2 plates

## Slide 4: DQW
Cavity (RT , no PCB) with He vessel + pretuning device
Input force 2.5 kN
Displacement z 0.53/0.6 mm
Maximum eq. Stress 225 MPa
Corresponds to about 0.21 MHz (0.42 MHz pp) *
For 400 MPa/1.2= 333 MPa -> 0.31 MHz (0.62 MHz) range (linear), 3.7 kN
At RT for 50 MPa , 0.25 mm maximum tuner stroke for 0.5 kN
Force/tuner stroke 2.2 kN/mm
199 MPa/mm

## Slide 5: RFD
Cavity (RT , no PCB) with He vessel
Input force 2 kN
Displacement z 0.4/0.41 mm
Maximum eq. Stress 95 MPa
Corresponds to about 0.280 MHz (0.560 MHz pp)
For 400 MPa/1.2= 333 MPa -> 0.980 MHz (1.96 MHz) range (linear), 7 kN
At RT for 50 MPa , 0.42 mm max tuner stroke for 1 kN
Force/tuner stroke 2.5 kN/mm
115 MPa/mm

## Slide 6: Pre tuning DQW
At warm
Bellows are now outside of the helium vessel
3 M6 screws (pull) and studs (push)
Pitch 1 mm
Bellows (Ti) will be probably edge welded
Sensitivity 0.8023 MHz/mm (Binping Xiao)

## Slide 7: Deformation
Top : 0.21 mm screw motion
-> 0.11 mm plate deformation
Bottom: 0.23 mm screw
-> 0.16 mm centre plate def.
Force: about 3 kN /screw M6x1
σi screw = 178 MPa (0.3 friction)
Flexibility gives the resolution
0.8023 MHz/ mm

## Slide 8: Pretuning stress
> 50 MPa
> 75 MPa
Pre-tuning 0.2 mm (distance plates) + pressure
https://indico.cern.ch/event/391211/session/4/contribution/11/material/slides/4.pptx
Ref. L. Dassa For the helium vessel as pressure vessel
this would be a limit (needs some thinking)
0.15 MHz (0.3 MHz) for 0.8 MHz/mm

## Slide 9: Tolerances tuner axis
= 1.49°
212 mm→ 5.5 mm
Requirements off set bellows
Introduce hinges (flexural)
545 mm→14 mm

## Slide 10: Status SM18 p.o.p. tuner
Motor 1.3 Nm Bipolar Nema 23
(1.8 deg/step)
HD HFUS-20-100-2SO
Ratio i : 0.01 ,
repeat. peak Torque 82 Nm, average torque 49 Nm
Accuracy < 1 arcmin, precision <0.1 arcmin
Fa Dyn 7.7 kN, η=~0.80 (grease, 20 °C)
Roller screw Rollvis RV 12 x 1
η=0.79 , static load capacity 17 kN
M= p i F/2000 π η = 0.01 Nm F= 4 kN, p= 1
Detend torque 0.017 Nm, self locking
Design: P. Minginette

## Slide 11: Instrumentation
Instrumentation:
Potentiometer Megatron RC13-25 M
25 mm range , 1 kΩ, resolution ~10 μm
Load cell Kistler
4576A55C1 class 0.1
limit switches
Mechanical stops
Precision motorisation:
1 step= 1.8° x 0.01 → 0.1 μm (p=1 mm)
Precision HD 0.1 arcmin or 0.0017° → 10 nm
Altered by friction in guides
DQW ~ 20-2 Hz
RFD ~ 35-3.5 Hz
DQW (2.2 kN/mm) →1.5 μm precision
RFD (2.5 kN/mm) → 1.3 μm precision
Design: P. Minginette

## Slide 12: Pressure compensation
Surface 0.0083 m2
R = 51.5 mm
1 atm = 101.325 kPa , Force = 844 N (on 2 tuning tubes)
Day variations 3 mbar 2.5 N
Week variations 10 mbar 8.3 N
10 mbar variation
1 atm = 0.19 mm on each plate
Load compensating springs : 3 x 5 N/mm

## Slide 13: Status p.o.p. tuner test
Motorisation:
All parts available and test mounted
Some improvements identified, some small parts to be machined
Qualification tests to be made.
Tuning frame and actuator tubes cryostat:
Production drawings ready and approved
Production being launched at the moment
Linked to production new cryo inserts for SM18
Earliest (own) guess parts available end of August

## Slide 14
Drawbacks first design:
Size …
Mass ~15 kg + 15 kg frame
Static : compensated
Dynamic First mode on cavity ~ 41 Hz
Motorisation can not be replaced
without opening cryostat (maintainability)

## Slide 15: Status design for SPS test (v1)
Size ok
Smaller mass
Can be dismounted from cryostat
Design: P. Minginette

## Slide 16: Status design for SPS test (v2)
Compact
10 to 20 times better resolution
Centre of actuation is materialised
Dismountable
Design: P. Minginette

## Slide 17: Piezo
At the moment not included.
Maximum input speed
Assuming very stiff actuation:
HD 6500 rpm : ~1 mm/s
Resolution to be tested but at best some Hz, can be improved
What resolution do we need ? How fast ?

## Slide 18: Conclusions
Calculations for DQW and RFD show the tuning ranges available that are smaller than the error on p.o.p.
A first prototype of the tuner motorisation has been built, tests with p.o.p. DQW autumn 2015 *
Options for the SPS tuner are under study, taking care of integration, resolution, pressure and load compensation and instrumentation
To be included in study: radiation, thermal optimisation
Test program to be prepared

## Slide 19
Thank you