## Slide 1: Dressed Cavity Engineering Design DQW & RFD
12/05/2015
Niklas Templeton - STFC Daresbury Laboratory
UK Collaborator
Notes: Tues 12th May 10.45 – 11.25 Hornet’s Nest WH8XO

## Slide 2: Content
Overview Dressed Cavities
Crab Cavity Design & Status
Cryogenic Magnetic Shielding
Helium Vessel Design
Analysis & Testing
Assembly Procedures
Cavity Support System

## Slide 3: Dressed Cavity Overview
Fundamental Power Coupler
Active (warm) Tuner Mechanism
HOM Coupler
Helium Vessel
Cavity
Cold Magnetic Shield
OVC Interface
Passive (cold) Tuning Component

## Slide 4: Cavity Designs
Niobium-Titanium Transition pieces
Tuner interface
Fundamental Power Coupler Port
Cavity Stiffening Ribs
Survey & Alignment Mounting Points
Niobium RRR300 Cavity – 4mm wall thickness
Double Quarter Wave
RF Dipole
Coupler & Probe Ports

## Slide 5: Double Quarter Wave
Cavity Design by BNL
Detailed drawings by CERN
Drawings finalised
Currently being manufactured by Niowave
659.6
495.7
410.5
Mass: 55kg

## Slide 6: RF Dipole
Cavity design by ODU
Detailed drawings by CERN
Drawings finalised
Currently being manufactured by Niowave
351
904.7
414
Mass: 50kg

## Slide 7: Cold Magnetic Shielding
Specification
<1µT on cavity surface
To be achieved in conjunction with 3mm warm MuMetal shield
Constraints
  Internal to Helium Tank
  Suspended in 2K Helium
  Mounted off Helium Tank – no cavity connection
Operating Conditions
>200µT – Earth’s magnetic field + shielded local sources

## Slide 8: Initial Opera Shield Analysis by Kiril Marinov ASTeC Daresbury Lab.
Cryomodule orientation comparison
Shielding effect is anisotropic - A cylinder is twice as effective against radial field as against axial field
Axial field provides worst case scenario
Radial Field
Axial Field
B
B

## Slide 9: Single Layer Solution
3mm MuMetal shield model with accurate size and penetrations analysed in worst case orientation
60µT field applied in axial direction (BEarth N-S = 48µT + safety margin)
Single layer shield is within spec. Analyses shows ~0.5µT at cavity locations
B>1µT
B = 60µT

## Slide 10: Double Layer Solution
Warm & Cold Shield models with accurate size and penetrations analysed in worst case orientation
60µT field applied in axial direction (BEarth N-S = 48µT + safety margin)
Field at cavity surface is extremely low (<<0.1µT) even before design optimisation
Double layer solution should be suitable even with increased ambient fields – further analyses required for design & optimisation
B>1µT
B = 60µT

## Slide 11: Cold Shield Design Approach
Minimise number & size of penetrations
Ease of manufacture & assembly
  Minimise number of panels
  Fabricated from Bent / Folded sheet
  Pressed panels possible future batch shield orders
Maximise penetration attenuation
Maximise curvature
Shield | No. Penetrations | No. Panels
DQW | 11 | 7
RFD | 7 | 10

## Slide 12: Common Design Features
Helium Holes
Shield perforated with at least 142 x Ø3mm holes on 50-100mm pitch for helium transfer
142 holes give 10cm2 transfer area, so that at worst case heat load (10W) heat flow is at least 1W/cm2
1mm Cryophy Panels
Panels to be manufactured from Cryophy sheet metal which is cut, bent/folded, and fastened using self clinching nuts & spring washers
Close fitting Shield
The shielding factor is inversely proportional to the shield diameter
Allows more space for connections, mounts & attenuation parts

## Slide 13: Common Design Features
Tubular Shielding
Prevents field penetration through openings.
Ideally H > ØD
Panel Curvature
More effective at containing channelled magnetic flux. Also increases structural rigidity of assembly
Additional Cover Strips
Overlapping joints prevent gaps & allows magnetic flux to follow a continuous low-reluctance path
Flexi-Mounts
Flexible Gr2 Titanium mounts connect the shield to the Helium Vessel. 8 mounting pairs are utilized in 3 orientations for maximum shield stability

## Slide 14: Crab Cavity Helium Tanks
Design by T. Capelli & R. Leuxe
Specification
Cooling capacity
Pressure vessel standards
Leak tightness
Stiffness for tuning
Minimal weld distortion on cavity
Constraints
Fabricated cavity geometry & tolerances
Cryomodule & SPS spatial constrains
Cavity interfaces and ports
Stiffening features
Clearance for cold magnetic shield
Helium volume

## Slide 15: Helium Tank Overview
Cavity & Cold Magnetic Shield
Dummy Beampipe
Helium Vessel Walls
Passive Tuning Component
Split Ring Reinforcements
Thin cap seals
2 phase line interface
DQW Helium Vessel – Exploded View

## Slide 16: Reasons for Bolted Helium Vessel
Nature of compact crab cavity design requires a stiff helium tank for pressure testing and tuning.
Thin walled vessel requires large number stiffening ribs.
Manufacturers advised that thin walled design would result in large weld distortions.
Weld distortions would be detrimental to cavity, thin walled design deemed too high risk.
Notes: I would say that the helium vessel concept has evolved until we found a suitable solution (insuring limited stress in the cavity during operation and limiting the detuning of the cavity during assembly), not that we had several suitable solutions and we had to choose one.
We have several 3D designs versions stored in our CAD management system, several ANSYS calculations stored in our calculation folders and several manufacturing tests results. We are preparing a technical note summarizing all the designs that have been calculated indicating all the steps we have passed through but it’s still far from being finished. I think the table you suggest should be included in this note.
For the presentation next week, we will be there and will answer this type of questions, if any.

## Slide 17
Weld testing of thin walled design
Two samples have been welded with the following configuration and different diameters of filler metal:
The dimensional control show some
deformations: Angular and longitudinal
Unsuccessful Metallographic test
3mm Test Piece
Reasons for Bolted Helium Vessel

## Slide 18: Double Quarter Wave Helium Vessel
Thin Caps
Split Ring Connection
30mm
30mm
20mm
20mm
20mm
20mm

## Slide 19: RF Dipole Helium Vessel
Thin Caps
Split Ring Connection
30mm
30mm
30mm
20mm
20mm
20mm
20mm

## Slide 20: Cavity & Helium Vessel Analysis
Analysis by F. Carra, L. Dassa, N. Kuder
Design in accordance with:
CERN Spec. for Category 1 Helium Vessel
BS EN 13458 – Cryogenic Vessels
VDI 2230 Part 2 – Systematic Calculation of Highly Stressed Bolted Joints
Analysis
Preload, Pressure & Pretuning
Cool Down
Cavity Buckling
Thin Cap Welds
Fastener Strength

## Slide 21: Loads & Boundary Conditions
Bolt pretension 3800 N
Gravity 9806.6 mm/s2
0.2 mm
Pressure 0.18 MPa
Thermal expansion 0.2 mm
Fixed support
Scale x100
Cavity submodel
Combining effect of bolt pretension, pressurization and pretuning

## Slide 22: Helium Vessel Stress Intensity
Maximum stress: 110 MPa
Max allowable stress: 187 MPa (Ti Grade 2)

## Slide 23: Cavity – Stress 1
Stress Intensity: “preload + pressure + pretuning”

## Slide 24: Cavity – Stress from sub-model (1)
Stress Intensity: “preload + pressure + pretuning” -> sub-model
Model re-evaluated in terms of primary & secondary stress in accordance to BS EN 13458

## Slide 25: Linearized Cavity Stress 2
Stress due to pressure (primary stress) - Pre tuning (secondary) stress not present
Stress Intensity Limits | 
Primary Membrane | 50MPa
Primary Local + Primary Bending | 75MPa
Primary + Secondary | 150MPa

## Slide 26: Cavity – Stress from sub-model 2
Stress due to pressure (primary stress) - Pre tuning (secondary) stress not present.
Stress over 75MPa (in Red) are out of spec. No such stress visible. Max Stress in due to mesh error.

## Slide 27: Further Analysis
Weight Saving Optimisation - up to 30kg
Analysis to be repeated for RFD Cavity & Helium Vessel

## Slide 28: Planned Testing Procedure
To understand and define the limits of critical dressed cavity components, including:
Fastener Strength
Welding
  Thin Caps
  Tuner and Beampipe
Prototype Helium Vessel
  Pressure & leak tightness
Magnetic Shield stress effects
TIG Welding Chamber

## Slide 29: Fastener Strength
TiGr2 screws to be tested at RT & 4K in order to determine their strength and behaviour in conditions similar to those experienced in the Helium Vessel.
Tests include:
Tractions tests for tensile strength
Torque tests for friction and preload
Shear tests for…
Bending tests for lateral loads
Screw coating to prevent galling
Fastener & Helium Vessel
Testing rig to be used in various configurations

## Slide 30: Weld Testing – Thin caps
Welding test to determine thickness of the plates, welding configuration & geometry, size and quality of the weld, parameters of the WPS.
Welds performed with and without filler metal (ERTi-2) in both cases:
Section required for design achieved (a=1mm)
Weld distortion is negligible
Metallographic & Hardness TEST

## Slide 31
Weld Testing
Tuning Interface
Dummy Beampipe
Nb
NbTi
Ti
Ti
NbTi
Nb
Transition zones

## Slide 32: DQW Assembly Procedure
Y
Z
X
Split ring reinforcements are fastened to the cavity transition pieces along with passive tuner component

## Slide 33: DQW Assembly Procedure
Y
Z
X
2 Bottom Panels assembled 1st
Cavity orientation shown upside down for clarity

## Slide 34: DQW Assembly Procedure
Y
Z
X
Shield & cavity mounted to base plate of the Helium Vessel
Top End caps are attached as well as bottom side panel and Dummy beam pipe attenuation sleeve.

## Slide 35: DQW Assembly Procedure
Final 2 top panels are brought into place and remaining cover strips and brackets are fastened

## Slide 36: DQW Assembly Procedure
Side and top Vessel walls are assembled with remaining Flexi-Mounts before Helium Vessel is closed

## Slide 37: DQW Assembly Procedure
Thin caps are TIG welded over the fastener slots
Vessel is sealed

## Slide 38: RFD Assembly Procedure
Split ring reinforcements are fastened to the cavity transition pieces

## Slide 39: RFD Assembly Procedure
Pre-assembled shield body is assembled Top and Bottom

## Slide 40: RFD Assembly Procedure
Shield body is mounted to Helium Vessel base

## Slide 41: RFD Assembly Procedure
Split folded-end panels are assembled around 3 ports
End Cover is assembled to main body and fastened with cover panels and brackets

## Slide 42: RFD Assembly Procedure
2 Curved-End panels are assembled around Beam Pipe

## Slide 43: RFD Assembly Procedure
Split panels complete the Shield at the FPC & HOM Ports
Remaining cover strips are assembled

## Slide 44: RFD Assembly Procedure
Flexi-mounts are connected and Helium Vessel is assembled

## Slide 45: RFD Assembly Procedure
Thin caps are TIG welded over the fastener slots
Vessel is sealed

## Slide 46: Dressed Cavity Support System
Approach
Minimise stress of FPC
Minimise heat leak to cavity
Active alignment & adjustment
Thermally neutral on cool down
Maximise modal stiffness
Minimise vibration response magnitude
Rigid FPC – Fixed point for Adjustment
Suspension rods compensate offset load
Additional inter-cavity support can increase system stiffness
Fundamental Mode Shape

## Slide 47
Thank You!
Questions?
For more details and summary of actions see https://indico.cern.ch/event/391211/