## Slide 1
Emmanuele Ravaioli
Toohig fellowship candidate
LARP Collaboration Meeting
11 May 2015
“The reward is that Joy.”
Timothy Toohig

## Slide 2
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
2008, M.Sc. in Energy engineering at the University of Bologna, Italy
Best Italian thesis concerning urban heating
2009-12, Fellow at CERN
Circuit modelling of LHC superconducting circuits
Optimization of the quench detection system (LHC restart 2010-11)
Wave propagation in superconducting circuits
2012-15, PhD at CERN and University of Twente
Title of my dissertation: “CLIQ”
Quench simulation
Magnet testing
Design and optimization of quench protection systems
My background

## Slide 3
All most critical circuits modeled
Electro-thermal models
Wave propagation
Development of a Quench Simulation Framework
Analysis of fault cases
Fellow at CERN – Modelling of LHC superconducting circuits
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
QSF

## Slide 4
Notable example: LHC main dipole circuit -1
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Power converter
switching-off
1st energy-extraction
switch opening
2nd energy-extraction
switch opening
Voltage transients propagating along the chain
Spurious triggering of the quench detection system

## Slide 5
Notable example: LHC main dipole circuit -2
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Wave propagation
Reflection and superposition

## Slide 6
LHC main dipole circuit – Analysis of failure cases
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Worst-case estimation of the peak voltage to ground reviewed
(900 V  1300 V)
Position of the short circuit pinpointed very quickly
4 years later

## Slide 7
LHC main dipole circuit – Intermittent short to ground -1
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Intermittent short to ground
2nd switch opening
1st switch opening

## Slide 8
LHC main dipole circuit – Intermittent short to ground -2
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
t<320 ms
Short present
t=320 ms
1st switch
t=360 ms
Short disappears
t=420 ms
Short reappears
t=450 ms
Short disappears
t=455 ms
Short reappears
t=480 ms
Short disappears
t=580 ms
2nd switch

## Slide 9
My PhD thesis: “CLIQ” – A new quench protection method
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Develop ment
Theory
CLIQ
Modeling
Testing
Optimi zation

## Slide 10
CLIQ – Coupling-Loss Induced Quench protection system
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Current Change
Magnetic Field Change
Coupling Losses (Heat)
QUENCH
Temperature Rise
Patent EP13174323.9

## Slide 11
CLIQ – Typical discharge
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Excellent agreement between simulations and measurements

## Slide 12
CLIQ – Main advantages
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
More effective energy deposition
Faster and more homogeneous quench initiation
More robust electrical design
Easier to implement and repair
Lower expected failure rate
External system not interfering with the coil winding technology
Cost- and time-effective back-up solution for protecting magnets with failing quench heaters
15 m long LHC main dipole magnet

## Slide 13
Modeling CLIQ – Challenges
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Coupling losses:
Where is the energy coming from?
How does the magnet differential inductance change with the current ramp rate?
(Critical for CLIQ)
New model required!
Conventional models

## Slide 14
Modelling CLIQ – A novel, elegant modelling technique
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
LEDET method (Lumped Element Dynamic Electro-Thermal)
Fast, efficient 2D model
Complex dynamic effects represented with equivalent networks of lumped-elements
All energy exchanges coherently accounted for

## Slide 15
Testing CLIQ
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
7 CLIQ test campaigns
(CERN, LARP collaboration, industry)
Functional requirements for CLIQ units and test facilities
Test plan
Test coordination
(good planning, and a lot of problem solving..)
Data analysis
(on-air comparison with simulations often possible)
Definition of main objectives

## Slide 16
Testing CLIQ – Nb-Ti model magnet for HL-LHC (MQXC2)
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
First CLIQ tests on an accelerator magnet

## Slide 17
Testing CLIQ – Nb3Sn model magnet for HL-LHC (HQ02b)
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
First CLIQ tests on a Nb3Sn magnet

## Slide 18
EE
EE
EE
Testing CLIQ – Full-size LHC matching quadrupole (MQY)
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
First CLIQ tests on a full-size magnet

## Slide 19
Optimizing CLIQ – Examples of possible configurations
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Different configurations can be obtained by varying the electrical order of the poles and the positioning of the CLIQ terminals

## Slide 20
Optimizing CLIQ – CLIQ effectiveness, Ѱ
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
CLIQ effectiveness, Ѱ
Introduced magnetic-field change, per unit of charging voltage and magnet length

## Slide 21
Quadrupole
Dipole
Block coil
Solenoid
Optimizing CLIQ – Different magnet geometries
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Subdividing the coil in multiple sections
Introducing opposite current changes in coil sections
that are physically adjacent
Golden rules

## Slide 22
Designing CLIQ – Protection of full-size MQXF magnet
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Performance evaluation
Optimum parameters
Integration in the circuit
Double redundancy
CLIQ + Outer quench heaters
Redundancy
Avoiding the installation of the
energy-extraction systems results in savings in the order of a few million $

## Slide 23
Designing CLIQ – Simulated CLIQ on a 7 m long MQXF
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Temperature
Voltage to ground
t= 10 ms

## Slide 24
Designing CLIQ – Simulated CLIQ on a 7 m long MQXF
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Temperature
Voltage to ground
t= 20 ms

## Slide 25
Designing CLIQ – Simulated CLIQ on a 7 m long MQXF
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Temperature
Voltage to ground
t=100 ms

## Slide 26
Designing CLIQ – Simulated CLIQ on a 7 m long MQXF
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Temperature
Voltage to ground
t=500 ms

## Slide 27
Designing CLIQ – Simulated CLIQ on a 7 m long MQXF
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Temperature
Voltage to ground

## Slide 28
My profile
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Multi-disciplinary
Experience in circuit design, quench protection, modeling, magnet testing..
My accomplishments
Self-starter
CLIQ from scratch, LEDET from scratch
Very active scientific writer
Main author of 15 papers (6 this year) 1 patent (CLIQ)
Award winning
Used to cope with stress
Urgent analyses and simulations of failure events in LHC circuits
IEEE CSC Graduate Study Fellowship
Best Student Paper at ASC 2014
ESAS prize at EUCAS 2013
Super motivated
Excited at the prospect of working for a period in a US laboratory
Good organizer
Supervised 5 students at CERN

## Slide 29
My interests in the LARP – How I’d ideally spend my time…
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
I’m ready to take the challenge of working on new topics if an interesting project is proposed.
Magnet quench protection
Circuit design and modelling
Quench simulation
Functional requirements of CLIQ units
Magnet testing
Though with limited experience, I’d be interested in magnet design and manufacturing as well
Smaller research project of my own initiative
(CLIQ on HTS? New CLIQ variant?)
50%
50%
20%

## Slide 30
Emmanuele Ravaioli
Toohig fellowship candidate
LARP Collaboration Meeting
11 May 2015
“The reward is that Joy.”
Timothy Toohig
Thanks to
H. ten Kate and A. Verweij,
V. Datskov and G. Kirby,
J. Blomberg Ghini, M. Maciejewski, and K. Sperin,
H. Bajas, K. Dahlerup-Petersen, V. Desbiolles, A. Dudarev,
J. Feuvrier, C. Giloux, T. Mulder, F-O. Pincot, F. Rodriguez-Mateos,
G. Sabbi, A. Siemko, and G. Willering

## Slide 31
Annex
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015

## Slide 32
A few months before the end of my fellowship…
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Glyn Kirby: “Is it possible to protect a magnet with AC losses?...”
“Temperature and Pressure Rise in Supercritical Helium during the Quench of Indirectly Cooled SC Coils”,
R. M. Schotter and H. W. Lorenzen, Technische Universität München
“Quench Protection for a 2-MJ Magnet”, Taylor et al., Lawrence Berkley National Laboratory
1978
1996
After 3 year of intense work, it is possible to protect full-size magnets using this new method, CLIQ (Coupling-Loss Induced Quench)
Vladimir Datskov: “I remember a few old papers…”
My idea: Not a pulse but a series of oscillations
Patent EP13174323.9

## Slide 33: Summary of CLIQ and QH performance on the model magnet
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
At nominal current quench load reduced by ~30% using CLIQ
However, CLIQ performance strongly depends on the magnet length

## Slide 34
Protecting full-scale magnets with CLIQ – The strategy
Power per unit volume deposited by CLIQ depends on inter-filament loss (IFCL)
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Charging voltage
(limited for safety reasons)
Equivalent inductance
of the discharge circuit
  → Coil geometry
  → Position of CLIQ connections
  → Electrical order of the poles
  (always an advantage, typically possible with minor changes)
Magnet length
(defined by design)
Number of CLIQ units
(for quadrupoles up to 2 units)
Capacitance of CLIQ unit
(no effect on power, but
to discharged energy)
For a given quadrupole magnet
Choose optimum CLIQ configuration
Increase voltage U0
2-CLIQ
Increase capacitance of CLIQ unit(s)

## Slide 35
Optimum CLIQ discharge configuration -1
Golden rule for optimizing any CLIQ discharge circuit
Introduce opposite current change in coils which are physically adjacent
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Optimized
Not Optimized
Significant reduction of Leq (2.5-3 times!)
→ Increase of deposited loss (6-9 times!)
+
+
–
–
+
–
–
+

## Slide 36
1
2
3
4
1
2
3
4
Optimum CLIQ discharge configuration -2
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
[a.u.]
[a.u.]
Golden rule for optimizing any CLIQ discharge circuit
Introduce opposite current change in coils which are physically adjacent
Efficient distribution of magnetic-field change
Optimized
Not Optimized

## Slide 37
Multi-CLIQ
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Further decreasing the impedance of the circuit can be reduced by subdividing the electrical circuit into 2xNC elements, effectively in parallel when CLIQ is triggered.
1-CLIQ
2-CLIQ

## Slide 38
Simulation results – I0 = 17.3 kA (Inom)
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Assumptions: no QH; no EE; RRR=140;
10 ms detection time
For each studied configuration a minimum capacitance is needed to protect the magnet
As expected performance of
2-CLIQ-500 V
similar to 1-CLIQ-1 kV
MQXF
Magnetic Length 6.8 m
Self-inductance 70 mH
Nominal current 17.3 kA
Quadrupole magnet for the LHC high luminosity upgrade
(US-LARP collaboration)

## Slide 39
Simulation results – I0 = 9 kA (~50% Inom)
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
1-CLIQ-500 V
is not sufficient to protect the full-length magnet
Both 2-CLIQ-500 V
and 1-CLIQ-1 kV are valid protection solutions for C>50 mF
Assumptions: no QH; no EE; RRR=140;
10 ms detection time

## Slide 40
CLIQ – Coupling-Loss Induced Quench
Current
Change
Magnetic Field
Change
Coupling-Losses
(Heat)
QUENCH
Temperature
Rise
Principle: When subjected to a magnetic field change, coupling losses occur in superconducting wires and cables. These losses are heat generated directly in the superconductor to quench!
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015

## Slide 41
With CLIQ connections at the joint between inner/outer layers
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
2o
3o
2i
3i
1o
4o
1i
4i
Golden rule for optimizing any CLIQ discharge circuit
Introduce opposite current change in coils which are physically adjacent
2o
3o
2i
3i
1o
4o
1i
4i
2o
3o
2i
3i
1o
4o
1i
4i
2o
3o
2i
3i
1o
4o
1i
4i
Existing magnets
Configurations easy to implement on most existing magnets
Future magnets
With connections between
in/out layers

## Slide 42
CLIQ – How is the energy deposited? with Inter-Filament Coupling Loss
Inter-Filament Coupling Loss
For typical filament twist-pitch and Cu transverse resistivity, time constant in the order of tens of ms
High energy deposition
with CLIQ discharge
Inter-Strand Coupling Loss
For typical strand twist-pitch and cross-contact resistance, time constant in the order of hundreds of ms / seconds
Limited energy deposition with CLIQ discharge
Magnetization Loss
Very limited change in the local magnetic field, hysteresis loops are small
Limited energy deposition with CLIQ discharge
For typical ranges of magnet inductance (5-100 mH) and CLIQ capacitance (5-50 mF), the range of the CLIQ oscillation period is 10-100 ms (frequency range 10-100 Hz)
The current introduced in the magnet coil generates a change in the local magnetic field.
When a superconductor is subjected to an applied magnetic-field change, an induced magnetic field is generated which opposes to the applied field.
For fast transients, the actual magnetic field does not change much, because the applied and induced magnetic field almost cancel out.
The presence of the induced field generates currents between superconducting filaments and between superconducting strands. These currents flow through the copper matrix of the conductor, thus they generate loss (=heat) inside the cable.
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015

## Slide 43
Multi-CLIQ – 2 CLIQ units, 4 CLIQ units, NC CLIQ units…
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Parameter | 1 CLIQ | 1 CLIQ 2xU0 | 2 CLIQ | 4 CLIQ | NC CLIQ
Number of elements, NE | 2 | 2 | 4 | 8 | 2 Nc
Equivalent inductance, Leq | Leq | = | ÷4 | ÷16 | ÷NC2
Total capacitance, Ceq | C | = | x2 | x4 | xNC
Charging voltage, U0 | U0 | x2 | = | = | =
Peak current change, dI/dt | U0/Leq/NE | x2 | x2 | x4 | xNC
Peak deposited loss | ∞(U0/Leq/NE)^2 | x4 | x4 | x16 | xNC2
Peak AC current, I | ∞U0*sqrt(Ceq/Leq)/NE | x2 | x20.5 | x2 | xNC0.5
Frequency, f | 1/2/π/sqrt(Leq*Ceq) | = | x20.5 | x2 | xNC0.5
Leq can be reduced by further subdividing the electrical circuit into NE elements, effectively in parallel when CLIQ is triggered.
They can be magnets in a chain, poles of a magnet, or inner/outer layers of each pole.
1-CLIQ
4-CLIQ
2-CLIQ
Peak power deposition
proportional to NC2

## Slide 44
Why do we need to delay the triggering of the extraction-system?
Avoid interference between CLIQ and EE system
  Avoid superposition of voltage across CLIQ and across EE resulting in voltage too high
  Avoid reducing CLIQ performance
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015

## Slide 45
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
Event in RB56 – Cpr to simulation without faults

## Slide 46
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
nQPS measurements cpr to Simulation – Intermittent short
EE openings
Short to ground

## Slide 47
Emmanuele Ravaioli - Toohig fellowship candidate LARP Collaboration Meeting - 11 May 2015
iQPS measurements cpr to Simulation – Intermittent short
EE openings
Short to ground