## Slide 1: QXF Long Coil Fabrication Status and Plans
J. Schmalzle
May 12, 2015

## Slide 2: QXF Long Coils
Preparation for reaction & impregnation of 4 m coils.
Plans for winding and curing.
Plans for 4.2 m coils.

## Slide 3: QXF Long Coils
Preparation for reaction / impregnation of 4 m coils:
  Coil lifting fixture fabrication, assembly and load test complete – 3 sets.
  Coil shipping fixtures – fabrication and assembly complete.
    Fabrication of wooden crates also complete.
  One shipping fixture and one lifting beam shipped to FNAL.
  Reaction / Impregnation tooling to be supplied by FNAL.

## Slide 4: QXF Long Coils
Fixture lifting / rotating beams.
  Fabrication complete.
  Load testing planned for next week.
Reaction oven length is sufficient to accommodate 4 m coils.
Impregnation tank and top hat are suitable for long coils.
  New impregnation fixture heaters purchased.

## Slide 5: QXF Long Coils
Plans for winding and curing.
  Winding machine and curing press existing.
  QXF winding and curing tooling preliminary design complete.
  Detailed W/C tooling design to start in June.
  Funding for tooling fabrication expected in FY16.
Plans for 4.2 m coils.
  Need to extend the reaction oven to accommodate the longer coils.
    Looking at adding an extension of approximately 1 meter.
    Working with oven vendor to come up with a detailed plan for fabrication and installation of oven extension.
  Coil lifting and coil shipping fixtures will need to be modified / extended.