## Slide 1
X. Gu
E-lens operation and electron beam characterization
Notes: 30 slides

## Slide 2: RHIC electron lenses - 2015
2015 – First proton run with electron lenses => compensation
Larger cathodes (7.5 vs. 4.1 mm radius) => allows for matched beam size with high solenoid field => raises instability threshold => easier alignment
Transverse damper => raises instability threshold
New lattice, based on ATS optics (S. Fartoukh, CERN) => phase advance kp between p-p and p-e interactions => small nonlinear chromaticity => no depolarization

## Slide 3: RHIC electron lens -- Layout
1 Anode-Beam Current 3 Collector-Beam Power
2 Bias-Beam Energy 4 GS1-Beam Size

## Slide 4: RHIC electron lens – Operating Parameters
Easy to control - operators know how to use it.

## Slide 5: RHIC Operation with E-lens
Turned on for every store (45~60 min.)
High reliability: available for all stores after running
E-beam current
Intensity
Emittance (IPM)
E-beam current
Emittance (IPM)
Tune

## Slide 6: Electron Gun Perveance - Pulse Beam
Design Value = 3.0 uA V-1.5
The perveances of the electron guns are within 10% and 15% of the design value for blue and yellow.
The variation in distance between anode and cathode could account for this.

## Slide 7: Electron beam current
Yellow e-beam current – DC 1100 (700) mA
Blue e-beam current - DC 600 (400) mA
With the pulsed mode, both blue and yellow electron currents can reach 1 A.
For a DC beam, the yellow e-lens can reach 1.1 A.

## Slide 8: Blue e-beam current instability with ~800 mA
Blue gun vacuum
Blue e-beam current
Can cause beam loss even with 5 mm separation
Can be impressed via higher collector voltage

## Slide 9: Blue electron beam current oscillation ( < 200 mA)
Blue e-beam current
Oscillations in the blue e-lens DC electron beam were observed when the current was below 200 mA.
The oscillations could be suppressed by using the split drift tube

## Slide 10: Reasons for Blue Electron Beam Issue
Yellow electron beam is Off-axis inside of Collector.
Reflected electron beam from collector (30 mm vs 22 mm ID)
Ion accumulation (ion collector transmitter failures)
Cathode/gun and collector contamination (high-pot vacuum spikes).
Blue Collector Temperature
Yellow Collector Temperature
Same DC Beam Current 1100 mA

## Slide 11: Electron beam profile
Beam profile can be fitted well to Gaussian.
Reason for small discrepancies in the center area: unknown .
Beam Image from YAG Screen
Gaussian Fitting

## Slide 12: Superconducting Magnet Current and Field
Both blue and yellow solenoid can run 6T;
Reliability is good;
SRF cavity could cause yellow quenches;

## Slide 13: RHIC beam Fill Pattern Imprinted on DT05
Electron beam can ‘see’ the proton beam even without colliding with it.

## Slide 14
Thank you !

## Slide 15: Head-on beam-beam compensation in RHIC W. Fischer, X. Gu, S.M. White, Z. Altinbas, D. Bruno, M. Costanzo, J. Hock, A. Jain, Y. Luo, C. Mi, R. Michnoff, T.A. Miller, A.I. Pikin, T. Samms, Y. Tan, R. Than, P. Thieberger, ... , Brookhaven National Laboratory
LARP CM24, 12 May 2015
LARP supported beam-beam simulations 2005 – 2009.
Notes: 60 min, 45 slides

## Slide 16: Acknowledgements
Brookhaven National Laboratory
M. Anerella, M. Bai, C.D. Dawson, A.K. Drees, B. Frak, G. Ganetis, D.M. Gassner, R.C. Gupta, P. Joshi, K. Hock, L. Hoff, P. Kovach, R. Lambiase, K. Mirabella, M. Mapes, A. Marone, A. Marusic, K. Mernick, M. Minty, C. Montag, J. Muratore, S. Nemesure, S. Plate, G. Robert-Demolaize, L. Snydstrup, S. Tepikian, C.W. Theisen, J. Tuozzolo, P. Wanderer, W. Zhang STAR and PHENIX experiments – supported parasitic commissioning
Institutions
FNAL: TEL experience, beam-beam experiments and simulations US LARP: beam-beam simulation CERN: beam-beam experiments and simulations
Individuals H.-J. Kim, V. Shiltsev, T. Sen, G. Stancari, A. Valishev, G. Kuznezov, FNAL; G. Kuznezov, BINP; X. Buffat, R. DeMaria, J.-P. Koutchouk, T. Pieloni, F. Schmidt, F. Zimmermann, CERN; V. Kamerdzhiev, FZJ; A. Kabel, SLAC; P. Goergen, TU Darmstadt

## Slide 17: Contents
Head-on beam-beam compensation principle
Electron lenses in RHIC
  Tune spread from lens
  Additional emittance growth and loss rate from lens
Head-on beam-beam compensation in operation (100 GeV polarized protons)
  Beam-beam parameters and luminosity in 2012 and 2015
  Operational use
  Emittance growth going into collisions

## Slide 18: Head-on beam-beam compensation Phase space
Tune spread compensation => e-p has same amplitude dependent force as p-p => provided by electron lens
Resonance driving terms compensation => phase advance between p-p and e-p is Dy = k p => provided by lattice (new lattice in 2015, based on ATS – S. White)
e-beam lens focuses
p-beam lens defocuses
Notes: Have phase space picture – also pics of footprint compression and resonance driving terms

## Slide 19: RHIC BTF with coherent modes
Coherent s- and p-modes in all BTF (amplitude response)
Prevent extraction of incoherent tune spread (imaginary part of complex BTF)
Notes: Run-15 fillno 18917, beginning of store (typical good store)

## Slide 20: Tune spread from BTF in presence of coherent modes
P. Görgen, TU Darmstadt, NIM A 777, pp. 43-53 (2015)
p-mode
s-mode
Determine Im(BTF)
Suppress coherent modes in analysis (location known)
Coherent mode suppression did not work in practice
incoherent tune spread

## Slide 21: Tune spread with 0, 1, 2 pp collisions, + e-lens
 0, 1, 2 pp without e-lens
 2 pp without and with e-lens
DQ = 0.024 given by s- and p-modes
change due to e-lens but incoherent distribution cannot be determined

## Slide 22: Tune spread from e-lens Current dependence
DQ = 0.013
 e-lens creates
as much DQ as one beam-beam collision

## Slide 23: Tune spread from e-lens e-beam size dependence
 e-lens creates
as much DQ as one beam-beam collision
DQ = 0.013

## Slide 24: Additional emittance growth and loss rates from e-lens
E-lens in operation typically on for ~1h.
Tested additional emittance growth and loss in Yellow with 2 stores (6.75 h, 5.25 h long).
8 good stores, e-lenses on for ~1 h
Yellow emittance growth ~0.1 mm/h
Yellow intensity decay time ~90 h [loss rate ≤1%/h]
e-lenses on for 6.75, 5.25 h
Yellow emittance growth ~0.1 mm/h
Yellow intensity decay time ~50 h [loss rate 2.5%/h]
When not limited by beam-beam there is no additional emittance growth from the Yellow lens (400 mA), additional losses of 1−2%/h.
Notes: Fillno 18849, 18855 with Yellow e-lens on for 6.75h and 5.25 h (400 mA)

## Slide 25: 100 GeV pp stores in 2012 and 2015 (typical good)
2012
2015
intensity
bb parameter +50%
rms emittance
peak luminosity +120%
300
5
140
12
4
[2012: 9 pb-1/week 2015: 25 pb-1/week]
Notes: 2012: fillno 16470; 2015: fillno 18917

## Slide 26: e-lens use in operation – collisions at 2 experiments
collisions start
IPM emittances
beam loss rates
e-lens e-beam currents
backscattered electron rates
e-lenses turn on before collision
Beams go into collision at PHENIX
collimators go to store positions (requires PHENIX collisions)
Beams go into collision at STAR e-lenses prevent emittance growth for large bb param. x
Lenses are gradually turned off, linear tune shift compensated (off when x < xmax,2pp)
eBSD rate [Hz]

## Slide 27: Max beam-beam parameter with and w/o e-lens in operation
xmax,2pp (2012)
xmax,2pp+pe (2015)
xmax,2pp (2015)?
intensities
beam-beam parameters x/IP
lenses should turn off at xmax,2pp to avoid additional beam losses
xmax,2pp also determines luminosity gain from lattice alone, and additional luminosity gain from e-lenses
determination of xmax,2pp would require about 1 week of operation without lenses (not done for fear of luminosity loss, only 11-week run)
Need to estimate xmax,2pp from available data (still in progress)

## Slide 28
Notes:
(1) Tests with 48x48 bunches (gives larger x due to smaller en) – all but case 1 (ops store)
(2) Use IPM for en (reports ~20% less than ZDC calculated en) – monitors emittance blow
Limit without e-lens: case 6 – emittance blow-up
Limit with e-lens: not found – not enough Nb/en from AGS
Max beam-beam parameter with and w/o e-lens in APEX (preliminary analysis X. Gu)

## Slide 29: Summary RHIC head-on beam-beam compensation
Head-on beam-beam compensation scheme in operation in 2015, consisting of new lattice (RDT compensation) + e-lenses (DQ compensation) Lpeak +150% Lavg +90% Lweek +170%
e-lens creates beam-beam tune spread without additional emittance growth, and small additional loss rate (1−2%/h)
e-lenses turned on before going into collision to prevent emittance growth, turned off gradually after ~1 h
Higher x/IP possible, presently constrained by injectors (potential for ~2× L in future runs)

## Slide 31: APEX 03/11/2015 Tune shift from e-lenses (X. Gu)
0.89E-3 for yellow, and 0.86E-3 for blue

## Slide 32: Tune shift as function of e-beam current (X. Gu)
0.00203
0.00171
0.00145
0.00125
Per / 100 mA

## Slide 33: Max beam-beam parameter with and w/o e-lens in APEX
*Mark: no e-lens, same injection intensity, y emittance blow up
Calculated with average intensity per bunch and average IPM emittance
No emittance blow-up when going into for any of the stores with the e-lenses
Tune scan with e-lens, with IP6 and IP8, blue /IP = 14.8, yellow /IP = 12.6:
Moving up tunes even 0.0005 will cause Blue beam decay increase. Moving tunes down 0.003, we observed emittance blow-up only in Blue ring. At that point, Qy from schottky was 0.681, which is similar to that from without BB compensation.