## Slide 1: Status of SSR1 and SSR2
Leonardo Ristori
P2MAC Meeting
9-10 March 2015

## Slide 2: Overview
325 MHz section of PIP-II Linac
SSR1 & SSR2 Cryomodules
SSR1 development
  Focusing elements
  SRF cavities
  Tuners
  Couplers
SSR1 schedule
SSR1 collaboration with IUAC
SSR2 design status

## Slide 3: PIP-II Superconducting Linac (RDR 2.1.3)

## Slide 4: SSR1 Cryomodule
5.2 m long
8 Cav + 4 Magnets
Bottom-supported elements with warm strongback
Tuner access ports
Current leads
Alignment
viewports
Couplers
COLD-MASS
T. Nicol, Y. Orlov

## Slide 5: SSR2 cryomodule
6.5 m long
5 Cav + 3 Magnets

## Slide 6: SSR1 CAVITY-MAGNET STRING
2 versions of cavities (A & B)
4 Solenoids+BPM
Vacuum manifold
13 interconnecting bellows (4 types)
T. Nicol, Y. Orlov
CAVITY-MAGNET STRING

## Slide 7: Focusing Elements
Lens strength (T2·m) 4
Steering dipole strength (T·m) 2.5·10-3
Insertion length, max. (mm) 160
Ferromagnetic shielding NO
Magnetic field on Cavity, max. (μT) 0.5·Q0 criterion Transverse misalignment (mm) 0.5 RMS
Angular misalignment (mrad) 1 RMS
Effects of magnetic field trapping during quenching
Axial Field: Measured vs Predicted
Quench Performance at 4 K and 2 K
Cavity Q degradation predicted vs measured
Solenoid installed on SSR1 during VTS tests
Excellent agreement between predicted and measured performances
I. Terechkine

## Slide 8: Focusing Elements
Prototype lens’ cold mass procured and tested at 2 K
The lens assembled and re-tested
Position of magnetic axis was measured by the vendor and at Fermilab: ΔR < 0.2 mm; Δα < 0.7 mrad
Maximum field on the surface of the cavity is below 5 G.
Four production lenses’ cold masses procured and tested at 4 K by the vendor.
The lenses have been prepared for the final performance test in the VTS at 2 K.
Prototype FL
Production FL
Quench protection studies
Voltage to the ground in the main coil
Temperature in quenching bucking coil
Production completed, cold tests next month
I. Terechkine

## Slide 9: SSR1, SSR2 – Main Requirements
 | SSR1 | SSR2
Frequency | 325 MHz | 
Operation | Pulsed / CW | 
βOPT | 0.222 | 0.475
Gain/cav | 2 MeV | 5 MeV
Q0 at 2K | > 0.6 1010 | > 0.8 1010
Bpeak | 58.1 mT | 64.5 mT
Epeak | 38.4 MV/m | 40 MV/m
Surface Res | 14 nΩ | 14 nΩ
LEFF (βλ) | 205 mm | 438 mm
G | 84 Ω | 115 Ω
R/Q | 242 Ω | 296 Ω
LFD sensitivity | < 5 Hz/(MV/m)2 | 
Tuning constant | 40 N/kHz | 90 N/kHz
LHe Sensitivity | < 25 Hz/torr | 
SSR1

## Slide 10: RF design of SSR1
Ivan Gonin

## Slide 11: Multipacting studies
Gennady Romanov

## Slide 12: Lorenz-Force Detuning studies
Spring Const [kN/mm] | LFD [Hz/(MV/m)^2]
∞ | -1.69
4000 | -1.69
400 | -3.38
40 | -5.07
0 | -7.6
Production
Prototype
Spring Const [kN/mm] | LFD [Hz/(MV/m)^2]
∞ | -2.74
4000 | -2.95
200 | -4.63
100 | -4.85
40 | -5.27
0 | -5.48
The LFD factor of SSR1 was studied with various boundary conditions.
In working conditions the predicted LFD factor is less than - 3 Hz/(MV/m)2
The requirement is < 5 Hz/(MV/m)2
M. Awida Hassan

## Slide 13: SSR1- Sensitivity to He pressure variations
SSR1 must operate within a small bandwidth ± 20 Hz
Pressure of LHe can vary by ± 0.5 Torr in the cryomodule
A self-compensating design was developed allowing low sensitivity
Despite non-negligible deformations (see picture), net shift is very low thanks to Slater’s Theorem
Bare cavity ~ 600 Hz/Torr, with He vessel ~ 10 Hz/torr
Ease of tuning 39 N/kHz (bare), 40 N/kHz* (with He vessel)
Deformations in high E and B regions balance out resulting in a small frequency shift (Slater’s Theorem)
D. Passarelli
Tuning
* It is possible to reduce sensitivity without increasing rigidity

## Slide 14: Harmonic Analysis – SSR1
Oscillating force f (x,y,z)
rigid modes
(not critical)
lowest RF-coupled mode
(well above 100 Hz)
hazard zone
L. Ristori

## Slide 15: Processing/Testing steps (ANL, FNAL)
1. Inspection – RF & Optical
2. BCP 120-150 μm (flip half-way)
3. HPR
4. 600 °C, 10 h (< 5°C/min ramp rate)
5. RF Tuning
6. BCP 20-30 μm
7. HPR (horiz + vert)
8. Assemble
9. Evacuate + 120 °C, 48 h
10. Vertical Test
11. Helium Vessel Dressing
RF Tuning
13. BCP 20-30 μm
14. HPR
Assemble
Evacuate + 120 °C, 48 h
15. Horizontal Test
16. Ready for String
Low-Temp Ovens (<300’C)
High-Temp Oven (<1000’C)
FNAL
FNAL
Bare cavity BCP setup
ANL
ANL
ANL

## Slide 16: Status of SSR1 cavities
Most of the 10 production cavities are in the jacketing stage
S107 is leading the group, 2nd test in STC to qualify prototype coupler and tuner
S106 and S105 are trailing due to repairs
9 of 10
Delivery
(Bare Cavity)
9 of 10
Cold Test
(Bare Cavity)
3 of 10
Jacketing
1 of 10
Cold Test
(Jacketed Cavity)

## Slide 17: Vertical Test Stand (VTS)
Successful qualification of production cavities for PXIE cryomodule
A. Sukhanov

## Slide 18: Spoke Test-Cryostat (STC) – S107 Run 1
Sep-Oct 2014
Successful cold tests of first production SSR1 (S107) and piezo encapsulations
A. Hocker, A. Sukhanov

## Slide 19: Prototype Tuner
Cartridge with motor and piezos
Installation of cartridge
Alignment system for main arms
Piezo encapsulations include bellows for retainment
D. Passarelli
Parameter | Req.
Coarse range | > 135 kHz
Fine range | > 1 kHz
Coarse resol. | < 20 Hz

## Slide 20: Couplers
We have 3 prototypes
  2 installed on RF test stand, 1 installed on first production cavity in STC
Design was changed to address several issues
  upgrade to aluminum seals, increase thickness of electro-deposited bellows,...
All components for 10 production couplers have been ordered
  cold-ends are needed for qualification of cavities
S. Kazakov, O. Pronitchev

## Slide 21: Prototype couplers
Warm Outer conductor
Electro-deposited bellows
(Cu-Ni layers)
Warm Inner conductor
Cold-end assembly
RF test stand

## Slide 22: Preparations for Run 2 – Installation of prototype coupler
All work done at MP9
Unity coupler was replaced with prototype high-power coupler

## Slide 23
mascot
“Pip”
Prototype coupler
S107 – Run 2
Prototype tuner

## Slide 24: Other cryomodule components received as of today..
Vacuum vessel
Focusing Elements
Support Posts
Strong-back

## Slide 25: SSR1 Cryomodule Schedule
String assembly rehearsal
  July - Aug 2015
Cav. qualifications
  Nov 2015 - Apr 2016
String assembly
  May - July 2016
Cold mass assembly
  Aug - Nov 2016
Cryomodule assembly
  Oct 2016 - May 2017
1/2016
1/2017
TODAY

## Slide 26: SSR1 - Collaboration with IUAC (New Delhi) – P.N. Prakash
IUAC is developing 2 SSR1 cavities
Slightly different process with EP components (intead of BCP)
Interesting to compare results
Delivery this year

## Slide 27: RF Design of SSR2 - Multipacting
Most severe multipacting take place near transition of cylindrical part to end walls. Several design options of this transition was considered. Most significant improvement was achieved after introducing additional step in the transition are.
Modification of this transition reduce multipacting in operating range of cavity fields.
SSR2 v1
SSR2 v2.6
SSR2 v2.6
P. Berrutti

## Slide 28: SSR2 - Multipacting SEY comparison
Secondary Emission Yield (SEY)significantly reduced in the operating gradient range of 5-12 MV/m. Comparison with SSR1 cavity demonstrates that multipacting in the modified SSR2 cavity version 2.6 can be processed away easier than in SSR1 cavity.
P. Berrutti
Parameters | SSR2 v1 | SSR2 v2.6
Optimal beta | 0.471 | 0.475
Epeak/Eacc | 3.45 | 3.69
Bpeak/Eacc [mT/(MV/m)] | 6.107 | 5.95
G [Ohm] | 112.98 | 114.9
R/Q [Ohm] | 289.94 | 295.6

## Slide 29: Summary
Production of SSR1 cryomodule has begun
  All bare cavities tested successfully
  1st Jacketed cavity tested successfully
  Prototype coupler and prototype tuner under testing
  All bare solenoids tested successfully
  Large components received
SSR1 cryomodule estimated to be completed in May 2017
IUAC will deliver (2) SSR1 cavities to FNAL
Design of SSR2 recently changed to address MP

## Slide 30
Thank you ...

## Slide 31
Backup Slides

## Slide 32: SSR1 Prototypes – VTS tests
During cool down, a 7 hr hold at 100 K produced a large Q0 drop, confirming Q disease.
Subsequently baked SSR1-01 at 600 C for 10 hours at Jlab.
Effects of Q disease should not appear on first cooldown.
X-rays increase at MP barriers, then disappear after punch through.
S102 – 1st test
S101 – 4th test

## Slide 33: SSR1 Prototype – STC Tests

## Slide 34: SSR1 Tuner: Requirements and data
Introduction
Assembly procedure
Meeting the technical specification
Feature of interest

## Slide 35: ASME Pressure Rating
The table summarizes the results obtained by simulations performed following the Div 2, Part 5 directions. It shows that the desired MAWP is achieved both at RT and CT.
    MAWP
    > 2 bar at 293K
> 4 bar at 2K
Protection against collapse from buckling
(P+D) pcollapse = 13.44 bar
(P+D+T1) pcollapse = 13.24 bar
(P+D+T2) pcollapse = 11.2 bar
(P+D+T1+T2) pcollapse = 11.2 bar
Protection against cyclic loading
Ratcheting
There is no plastic deformation in the overall dimension of the SSR1 resonator
Protection against plastic collapse
GC1 : pcollapse = 2.23 bar @ RT (P+D)
GC2 : pcollapse = 2.78 bar @ RT (P+D+T1)
GC2 : pcollapse = 8.97 bar @ CT (P+D+T1+T2)
Protection against local failure
Fatigue Assessment
No fatigue analysis is necessary
D. Passarelli

## Slide 36: Jacketing operations
Thermal cameras insertion tubes (above)
Screenshot of remote connection from FNAL
Welding inch-by-inch on 6 mm thick steel
Large fixtures needed to control warping
D. Passarelli, M. Hassan, P. Berrutti