## Slide 1: Physics design of 1 GeV Accelerator
S.V.L.S Rao
On behalf of our IADD

## Slide 2: Outline of talk
Purpose of doing these studies
LEHIPA parameters
1 GeV Linac simulations
Future studies

## Slide 3: ADS
High energy proton accelerator
Spallation target
Sub-Critical reactor

## Slide 4
Pth (MW) | I (mA) k=0.95
1000 | 29.2
1500 | 43.9
2000 | 58.5
2500 | 73.1
3000 | 87.7
Proton Energy : 1 GeV
νs = 25 neutrons/proton
ν = 2.5 neutrons/fission
I (mA) k=0.98
10.2
15.3
20.4
25.5
30.6
Beam current requirement

## Slide 5
Proton IS
50 keV
RFQ
3 MeV
DTL
20 MeV
DTL/
CCDTL
Super-
conducting
SC Linac
1 GeV
200 MeV
Normal Conducting
High current injector 20 MeV, 30 mA
Schematic of Accelerator Development
Design completed & fabrication is in progress
ECR Ion Source
LEBT
RFQ
Drift Tube Linac
60 kW RF System
1.3 MW Klystron
Phase 1
Phase II
Phase III
LEHIPA
50 kW RF Coupler

## Slide 6
Schematic of New 1 GeV accelerator
Elliptical
Cavities
200 MeV
1 GeV
IS
RFQ
HWR,
SSR
50 keV
3 MeV
150 MeV
Elliptical Cavities
LEBT
MEBT

## Slide 7
Element | Length (cm) | Strength (G)
Drift | 110 | 
Solenoid | 30 | 1481
Drift | 140 | 
Solenoid | 30 | 2004
Drift | 20 | 
Frequency | 352.21 MHz
Energy | 50 keV/ 3 MeV
Input current | 30 mA
Vane voltage | 68 kV
Avg. Aperture R0 | 3.063 mm
Modulations | 1-1.81
Length | 4 m
Total RF power (1.37SF) | 470 kW
Transmission* | 96%
Parameters of the RFQ
115.5 cm
D
D
EMQ1
25.5
21
5
8
7
8
10
10
5
8
8
EMQ2
EMQ3
EMQ4
BC
Layout of MEBT
EMQ No | B Field Gradient (T/m) | Eff. Length (cm)
1 | -24.18 | 8
2 | 18.69 | 8
3 | 19.20 | 8
4 | -23.49 | 8
LEHIPA parameters:

## Slide 8
Parameters |  | Tank 1 | Tank 2 | Tank 3 | Tank 4
Input Energy (MeV) |  | 3.03 | 6.86 | 11.26 | 15.75
Output Energy (MeV) |  | 6.86 | 11.26 | 15.75 | 20.23
No. of cells |  | 36 | 28 | 23 | 20
Lattice period |  | 4 βλ | 4 βλ | 4 βλ | 4 βλ
Current (mA) |  | 29.38 | 29.38 | 29.38 | 29.38
Eff. Length of quad (cm) |  | 4.715 | 4.715 | 4.715 | 4.715
No. of quads. |  | 37 | 29 | 24 | 21
Aperture radius (cm) |  | 1.2 | 1.2 | 1.2 | 1.2
Synchronous phase |  | -30 | -30 | -30 | -30
Acc. Field grad. (MV/m) |  | 2.14 | 2.14 | 2.14 | 2.14
Dissipated Power (kW) |  | 284.14 | 285.14 | 279.85 | 277.7
Tank Length (m) |  | 3.05 | 3.26 | 3.27 | 3.28
Drift space after tank (cm) |  | 5.553 | 8.388 | 10.684 | 
No. of Post Couplers |  | 12 | 14 | 11 | 10
No. of tuners |  | 6 | 6 | 6 | 6
No. of rf ports |  | 2 | 2 | 2 | 2
No. of Vacuum ports |  | 2 | 2 | 2 | 2
Norm. RMS Emittance | x(π cm mrad) | 0.02134- 0.02113 | 0.02107 | 0.02102 | 0.02119
 | y(π cm mrad) | 0.02037-0.02062 | 0.02091 | 0.02111 | 0.02123
Long. Emittance(deg. MeV) |  | 0.10392- 0.11131 | 0.11211 | 0.11335 | 0.11536
DTL parameters:
1.2 m long prototype DTL

## Slide 9
Old 1 GeV Linac:
Computer codes:
Lidos and Parmila
Beta: 0.49,0.62 and 0.8

## Slide 10
New 1 GeV Linac Layout
ECR Ion source
RFQ (NC)
(SRF Linac)
325 MHz, 30 mA
325, 650 MHz
Spoke and elliptical
3 MeV
RFQ designs:
computer code Toutatis is used
3 MeV 325 MHz RFQ (LANL type design)
  Shaper section has modified
3 MeV 162.5 MHz RFQ
MEBT

## Slide 11
RFQ for 200 MeV Linac:
Requirement:
Good beam quality
(Long emittance should be less)
Maximize the Transmission
Results:
Length of RFQ : 4 m
Transmission : 99.6 %
Accelerated : 99.3 %
(3+/-0.072 MeV)
RMS emittances at exit of RFQ:
O/P T emit: 0.02 cm-mrad
O/P L emit: 0.03 cm-mrad

## Slide 12
Input distribution to MEBT:
Input distribution to RFQ is 6 sigma gaussian

## Slide 13
Medium Energy Beam Transport (MEBT):

## Slide 14
Rms emittance:
Transverse : 0.245 mm mrad
Longitudinal : 0.286 mm mrad

## Slide 15: SRF Linac Layout
SSR0
SSR1
SSR2
Ell 0.6
Ell 0.8
Section | βG | Frequency (MHz) | Energy (MeV) | No. of cavities | Length (m) | Focusing
SSR0 | 0.11 | 325 | 3-10.51 | 19 | 13.71 | SC Solenoids
SSR1 | 0.21 | 325 | 10.51-50.05 | 26 | 23.24 | 
SSR2 | 0.4 | 325 | 50.05-205.17 | 53 | 51.36 | 
Ell 0.6 | 0.6 | 650 | 205.17-440.35 | 48 | 129.45 | Warm Quad doublets
Ell 0.8 | 0.8 | 650 | 440.35-1001.5 | 63 | 120.06 | 
Total Length = 337.86
Computer codes:
Toutatis, GenlinWin and TraceWin

## Slide 16: Period Length & Lattice Type
SSR : Solenoid Cavity Solenoid
Ell 0.6 : Quad Doublet Cavity Quad Doublet
Ell 0.8 : Quad Doublet Cavity Cavity Cavity Quad Doublet

## Slide 17
Accelerating field Gradient in SRF Linac cavities

## Slide 18
Beam Envelopes for 30 mA beam

## Slide 19
Evolution of Beam emittances along the SRF Linac:
Input emittance:
εx = 0.245 π mm mrad
εy = 0.245 π mm mrad
εz = 0.29 π mm mrad
= 0.106 π deg MeV
Output emittance:
εx = 0.263 π mm mrad
εy = 0.269 π mm mrad
εz = 0.376 π mm mrad
= 0.138 π deg MeV

## Slide 20
Cavity | Max Energy gain (MeV/cavity) | Max Beam power (kW/cavity)
SSR0 | 1.65 | 50
SSR1 | 1.65 | 50
SSR2 | 3.00 | 90
Elliptical (beta=0.6) | 6.00 | 180
Elliptical (beta=0.8) | 10.00 | 300
Maximum Power required for SRF cavities

## Slide 21
Parameters | Value | Units
Frequency | 325 | MHz
Geometric beta | 0.21 | 
Beta (opt) | 0.22 | 
Aperture (dia) | 30 | mm
R/Q | 255 | Ohm
Transit time factor | 0.84 | 
Ep/Eacc | 4.28 | 
Bp/Eacc | 7.24 | mT/MV/m
Height of spoke | 48.9 | cm
Thickness of spoke near beam axis | 4.08 | cm
SSR1 cavity design studies:
T
Liris
H
D
Lcav
Sectional view of SSR cavity
CST Microwave studio

## Slide 22
CST Tetrahedral mesh:
Chart: T/Liris
| 0.2939753846153848 | 0.31392307692307753 | 0.32588307692307772 | 0.35653600000000002 | 0.37462307692307734
 | 4.5617 | 4.2824 | 4.3769 | 4.6859 | 4.8753
Ratio of Ep to Eacc
Chart: beta (v/c)
| 0.1 | 0.15000000000000019 | 0.22 | 0.30000000000000032 | 0.4 | 0.5 | 0.60000000000000064
 | 0.09 | 0.67 | 0.84 | 0.77 | 0.64 | 0.54 | 0.46
Transit time factor

## Slide 23
Parameters | Value | Units
Frequency | 325 | MHz
Geometric beta | 0.4 | 
Beta (opt) | 0.4 | 
Aperture (dia) | 60 | mm
R/Q | 271 | Ohm
Transit time factor | 0.81 | 
Ep/Eacc | 5.54 | 
Bp/Eacc | 7.87 | mT/MV/m
Height of spoke | 50.25 | Cm
Thickness of spoke near beam axis | 5.83 | Cm
Parameters of SSR2 cavity:
Chart: 
| 0.25 | 0.30000000000000027 | 0.35000000000000026 | 0.4 | 0.45 | 0.5 | 0.55000000000000004 | 0.60000000000000053 | 0.70000000000000051 | 0.8
for ssr2 transmit time factor | 0.514 | 0.7 | 0.788 | 0.815 | 0.81 | 0.79 | 0.76 | 0.73 | 0.66 | 0.6
Transit time factor vs beta (v/c)

## Slide 24: 162.5 MHz RFQ design studies
No. of particles in a bunch
  5.7e8 (30 mA, 325 MHz)
  5.7e8 (15 mA, 162.5 MHz)

## Slide 25
Parameters | BARC (RFQ) | PXIE RFQ
Frequency | 162.5 MHz | 162.5 MHz
I/O energy | 0.03/2.1 MeV | 0.03/2.1 MeV
Beam current | 15 mA | 5 mA
Vane voltage | 60 kV | 60 kV
Length | 5.15 m | 4.35 m
I/O Rms emittance | 0.3/0.32 mm-mrad | 0.11/0.14 mm mrad
Long* | 0.50/0.09/1.54 | 0.22/0.04/0.68
Transmission | 99 % | 99.8 %
Acceleration efficiency | 0.58 | 0.69
* Longitudinal emittance: mm-mrad/MeV-deg/kev-nsec
Parameters of 162.5 MHz RFQ

## Slide 26
Future studies:
Beam dynamics
  End-to-end simulations
  Complete error analysis
  Fault-tolerance studies
Cavity design
  Effect of HOM in the superconducting cavities (spoke and elliptical cavities)
  Lorentz force detuning and its compensation