## Slide 1: Status of the European Spallation Source ESS
Torsten Bögershausen
SW Engineer
Motion Control and Automation Group
www.europeanspallationsource.se
2015-05-19

## Slide 2: Max IV and ESS
ESS neutron source
(2019)
MAX IV synchrotron (2016)
Science Village Scandinavia
Lund University
Copenhagen University Cph airport
Ideon and Medicon Village business incubators
Malmö University

## Slide 3: Funding is Cash and In-Kind Deliverables
Sweden and Denmark:
47,5% Construction 15-20% Operations
Cash ~100%
Partner Countries: 52,5% Construction
80-85% Operations
IKC/Cash ~ 70% / 30%
1843 M€ construction
140 M€/yr operations

## Slide 4: Time Structure of the Neutron Beam
3 ms
68 ms
14 Hz rep rate
71.4 ms cycle time
2.86 ms pulse time
4% duty cycle
200 – 2000 m/s
30.5 ms
30.5 ms
71 ms
t
d

## Slide 5: Air view March 2015

## Slide 6: Inside the tunnel

## Slide 7: More tunnel to come

## Slide 8: EPICS within the ESS organization
Machine directorate
Integrated Control Systems “ICS”
  EPICS to control the whole facility
Science directorate
Motion Control and Automation Group “MCAG”
  EPICS for the new motion control
Data Management and Software Center “DMSC”
  Located in Copenhagen
  Scientific computing
  Instrument control
More EPICS users:
  Choppers, Sample environment, Detectors
  In kind partners

## Slide 9: Some EPICS decisions
EPICS for controls in the whole site, from accelerator to neutron instruments
Plan to benefit from EPICS V4: pvAccess everywhere
CS-Studio as the generic user interface tool: control room, subsystem developers, etc.
Databases (configuration, cable, RBAC, …)
Probably python to control scientific instruments
Work together with the EPICS community

## Slide 10: Controls hardware: Fast Realtime IO
  Fast real time I/O
    beam diagnostics and Low Level RF
    Synchronized with the 14 Hz pulse
    > Megabyte/sec

## Slide 11: Controls hardware: Non real time IO
  Non real time
    E.g. Vacuum
    Reliable
    < 10 Hz, “Slow”

## Slide 12: Controls hardware: real time IO
  Mid range
    Synchronized with the 14 Hz pulse
    1 Hz .. 10 kHz, max 100 kHz
    real time

## Slide 13: Hardware standards, the whole spectrum
  Fast real time I/O
    MicroTCA 4
  Mid range Real time industrial I/O EtherCAT
  Slow non real time I/O
    PLCs

## Slide 14: ESS Motion Control and Automation Group
ESS Motion Control and Automation Group (MCAG)
select a motion control solution for the whole facility (Accelerator, Scientific Instruments)
Scope includes also
  Integration of the new motion control with EPICS
  Robotics

## Slide 15: Motion platforms
Motion controller – HW
Temporary solution: DeltaTau GeoBrick
Evaluating
  DeltaTau Power PMAC
  Beckhoff TwinCAT (different talk: EPICS – TwinCAT)
  ESRF ICEPAP

## Slide 16: Summary
ESS building has started for real
  Commissioning of the accelerator will start in 2 years
Control system effort is ramping up
  Moving to design decisions
  EPICS V4: pvAccess everywhere
  Come to Sweden ? Hiring people – (watch our web pages)
Motion control evaluation ongoing
  EPICS integration part of the evaluation
Need to bring EPICS to the Science Directorate in ESS, in kind partners

## Slide 17: Staff March 2015

## Slide 18
Thank you
Questions ?