## Slide 1: Scan System Update
Kay Kasemir,
May 2015

## Slide 2: Scan Server
Sample Environment Equipments
Sample Environment Equipments
Sample Environment Equipment
GUI: CSS
Script
EPICS IOCs
Scan Server
Channel Access
REST

## Slide 3: What it is and isn’t*
Is
Automation via Channel Access
Scan = Batch of commands
Queue multiple scans
Basic value logging
Submit, monitor, pause, resume, abort
* .. depends on your definition of “is”
Isn’t
Synchronization of actions beyond Channel Access
Data Acquisition (log every event, catalog, keep forever)

## Slide 4: Set, Loop Commands
Set “some_pv” = 3.14
Loop “some_pv” = 1..10, step 0.5
Optionally
  Await completion (put-callback)
  Check read-back to match written value (same or other pv)
    .. With numeric tolerance
  Timeout

## Slide 5: Direction of (Nested) Loops
Loop(‘x’, 0, 5, 1)  0, 1, 2, 3, 4, 5
Loop(‘y’, 5, 0, -1)  5, 4, 3, 2, 1, 0
Loop(‘x’, 0, 5, 1, Loop(‘y’, 0, 5, -1)) Alternate direction on ‘mismatch’

## Slide 6: Other Commands
Wait for “pv1” > 100
Wait for “pv2” to increment by 200
  Get-callback for initial value, then monitors
Log “pv1”, “pv2”, “pv2”
  Get-callback for current value, to RDB
Invoke ‘MyScript’
  Jython-based custom commands

## Slide 7: Like Sequencer?
Yes: Read/write Channel Access
No compilation
Monitor & control progress of scan
Basic data log
Schedule multiple scans
No arbitrary C code
No ‘if-then-else’ command

## Slide 8: Like Scan Record?
Loop y=1..10: Loop x=1..5: Set “det_trigger”=1 with completion, Log “x.RBV”, “y.RBV”, “det_counts”
Monitor, pause, resume, abort. Save, edit, resubmit scans vs. save/restore scan records.
Add 3rd loop without rebooting IOC to add 3rd scan record
Queue multiple scans
Logs to RDB w/ REST readout. No MDA/XDR/Nexus.

## Slide 9: REST Interface

## Slide 10: Scan Editor
Add commands
Set parameters
Open, save

## Slide 11: Python API

## Slide 12: Site-Specific Settings
class BeamlineScanSettings(ScanSettings): def __init__(self): self.defineDeviceClass("chopper:.*", completion=True) self.defineDeviceClass("motor.*", completion=True, readback=True)
def getReadbackName(self, device_name): if "motor" in device_name: return device_name + ".RBV“ return device_name
“Set(‘x’, 42)”  Set(‘x’, 42’) “Set(‘motor_x’, 42)”  Set(‘motor_x’, 42, completion=True, readback=‘motor_x.RBV)

## Slide 13: GUI for Routine Beam Line Task

## Slide 14: Under the hood
Scan Server

## Slide 15: Alignment Scan

## Slide 16: Table Scan
Load/save *.csv, *.xls

## Slide 17: Scripted Scan

## Slide 18: Parallel Command

## Slide 19: Sequence Command

## Slide 20: Scan Monitor

## Slide 21: Scan Plot
Plot variables logged by scan
Get data from Running or Finished scans

## Slide 22: Summary
Scan System helps automate SNS since 2013
Scan Server: REST instead of JNI
Python API: Pure Python instead of Jython
  Thanks to Qui Yongxiang, Guobao Shen, Dylan Maxwell
New Parallel & Sequence commands
Biggest Issue:
Can’t use numpy (Fortran) inside Script command (Jython)